## Slide 1: Capacity Simulation of High Density Indoor WLAN Systems
Date: 2013-09-16
Authors:

## Slide 2: Abstract
Preliminary results from simulation of high density indoor WLAN systems. The static simulation is similar to one used for cellular applications

## Slide 3: Topics
WLAN multi-cell performance aspects
Models and assumptions
Results
Summary

## Slide 4: WLAN Multi-cell Performance Aspects
802.11n and 802.11ac have similar physical layer characteristics as cellular systems, e.g. LTE
  Modulation, channel coding, MIMO capabilities
But…
The CSMA-based MAC limits densification
  Nodes that hear each other cannot be active at the same time
  This creates a re-use in the time domain
Operation in uncontrolled environments with external interference will further limit performance
  Not modeled here

## Slide 5: Models and Assumptions
IEEE 802.11n modulation and coding rates
2.4 or 5GHz
Frequency reuse varied between 1 and 12 vs isolated AP
  Choose channels that maximize distance between APs that use the same frequency
One single 20MHz carrier per AP
AP and STA power 100mW (EIRP)
CS (Carrier Sense) threshold -85dBm
2x2 MIMO in DL and UL
No external interference
File transfer traffic
75% in downlink and 25% in uplink
MAC PDU size 65KB
Notes: Interference: STAs on one AP still interfere with other APs

## Slide 6: Deployment Scenario
An office-like building with 80x50m footprint
Ten floors of height 3m
Interior walls every 10m (10x10m rooms)
Winner II propagation
  Free-space propagation with inner wall loss of 12dB, and floor loss of 17dB for first floor and 4dB for following floors
  Log-normal shadowing with standard deviation 8dB
Subscriber density 1/16m2  250/2500 per floor/building
  ~30 subscribers per AP
8 APs per floor, randomly deployed per floor, all floors same

## Slide 7: Traffic Load per AP vs Monthly Volume per User
Subscriber density 1/16m2  250/2500 per floor/building
200 busy hours per month
Traffic per subscriber and month v busy hour traffic per floor
  Assume 10 GB per month per sub x 250 subs per floor / 200 busy hours per month = 27Mbps per floor or 3.4Mbps per AP

## Slide 8: Radio Characteristics and Performance Measurement Method

## Slide 9: AP to STA Radio Characteristics
Good coverage
  Well above total gain of -100dB which corresponds to -80dBm received power
Good isolation geometry due to walls and floors
September 2013

## Slide 10: Cell Isolation
Propagation as a function of distance and floor
Total loss <105dB (received power >-85dBm) some two to three walls or floors away
2.4GHz
5.0GHz
September 2013

## Slide 11: Cell Isolation
An active AP triggers carrier sensing (>-85dBm) in 7.1 and 5.9 neighbor APs (on average) in 2.4GHz and 5.0GHz respectively
The graph shows average received power from neighbor APs in order of strength
September 2013
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 12: Performance Measurement Method
Cell-edge (5th percentile) and mean user throughput vs traffic load
‘How much can the system be loaded before user experience gets unacceptable?’
Datarates decrease when load increases due to increased interference and more active users sharing channel
Traffic load
Traffic load

## Slide 13: Performance Results 2.4GHz

## Slide 14: Isolated APs, 2.4GHz, DL
5th percentile throughput is at most 40Mbps
Utilization approaching 75% (CSMA efficiency)

## Slide 15: Reuse 3, 2.4GHz, DL
5th percentile throughput is at most 12Mbps
Utilization approaching 30%

## Slide 16: Reuse 1, 2.4GHz, DL
5th percentile throughput is at most 7Mbps
Utilization approaching 10%

## Slide 17: Reuse 1, 3, Isolated, 2.4GHz, UL
Same trends as in downlink

## Slide 18: Capacity
Maximum served traffic for cell-edge (5th percentile) user throughput of at least 5Mbps
Isolated [100%]
Isolated [100%]
Reuse 3 [100%]
Reuse 3 [100%]

## Slide 19: Spectral Efficiency
Capacity divided by total spectrum usage in used direction
  Spectral Efficiency = Capacity / (reuse * 20MHz x f)
  Downlink = 0.75 Uplink = 0.25
Increases with tighter reuse, but still rather low
Reuse 3
Reuse 3

## Slide 20: Performance Results 5GHz

## Slide 21: Reuse 1-12, Isolated, 5GHz, DL
Same trend as in 2.4GHz
Slightly better than 2.4GHz due to better isolation

## Slide 22: Reuse 1-12, Isolated, 5GHz, UL
Same trends as downlink

## Slide 23: Capacity 5GHz
Maximum served traffic for cell-edge (5th percentile) user throughput of at least 5Mbps
Isolated [100%]
Isolated [100%]
Reuse 12 [100%]
Reuse 12 [100%]

## Slide 24: Spectral Efficiency
Capacity divided by total spectrum usage in used direction
  Spectral Efficiency = Capacity / (reuse * 20MHz x f)
  Downlink = 0.75 Uplink = 0.25
Increases with tighter reuse, but still rather low

## Slide 25: Next Steps
Inter-cell carrier sensing based only on AP-to-AP channel, need to look at STA as well
Include hidden nodes
Include RTS/CTS
  Currently not explicitly modeled, but no hidden nodes assumed either
Model more realistic modulation rate algorithms
Model effects of more realistic AP channel selection and placement

## Slide 26: Summary
High capacity multi cell systems can be built with WLAN technology (!)
Inter-cell carrier sensing limits performance
Possible to mitigate with more channels
Are there more spectrally efficient solutions?
We have a good baseline to assess enhancements

## Slide 27: References
[1] I. Siomina, A. Furuskär, and G. Fodor. A mathematical framework for statistical QoS and capacity studies in OFDM networks, Proc. of IEEE PIMRC ’09, Sep. 2009.