## Slide 1: Capacity Simulation of High Density Indoor WLAN Systems
Date: 2013-09-17
Authors:

## Slide 2: Abstract
Preliminary results from simulation of high density indoor WLAN systems. The simulation methodology is similar to the one used for evaluating cellular networks
Notes: Feedback on the application of the used simulation methodology to WLAN is greatly appreciated.

## Slide 3: Topics
WLAN Multi-cell Performance Aspects
Models and Assumptions
Performance Metrics
Results
Summary

## Slide 4: WLAN Multi-cell Performance Aspects
IEEE 802.11n and IEEE 802.11ac have similar physical layer characteristics as cellular systems, e.g. LTE
  Modulation, channel coding, MIMO capabilities
But…
The CSMA/CA-based MAC limits densification
  Nodes that hear each other cannot be active at the same time
  This creates a re-use in the time domain
Operation in uncontrolled environments with external interference will further limit performance
  Not modeled here

## Slide 5: Models and Assumptions
IEEE 802.11n modulation and coding rates
2.4 or 5GHz
Frequency reuse varied between 1 and 12 vs. isolated AP
  Choose channels that maximize distance between APs that use the same frequency
One single 20MHz carrier per AP
AP and STA power 100mW (EIRP)
CS (Carrier Sense) threshold -85dBm
2x2 MIMO in DL and UL
No external interference
File transfer traffic
75% in downlink and 25% in uplink
MAC PDU size 65KB
Notes: Interference: STAs on one AP still interfere with other APs

## Slide 6: Deployment Scenario
An office-like building with 80x50m footprint (similar to [2])
Ten floors of height 3m
Interior walls every 10m (10x10m rooms)
Winner II propagation
  Free-space propagation with inner wall loss of 12dB, and floor loss of 17dB for first floor and 4dB for following floors
  Log-normal shadowing with standard deviation 8dB
Subscriber density 1/16m2  250/2500 per floor/building
  ~30 subscribers per AP
8 APs per floor, randomly deployed per floor, all floors same
Notes: AP deployment is done to maximize coverage. Channel selection is done to minimize interference. The maximum distance between a room and the nearest AP is a measure of 'cell range', and this we want to minimize.

## Slide 7: Traffic Load per AP vs. Monthly Volume per User
Subscriber density 1/16m2  250/2500 per floor/building
200 busy hours per month
Traffic per subscriber and month vs. busy hour traffic per floor
  If we assume:
  10 GB per month per sub x 250 subs per floor / 200 busy hours per month = 27Mbps per floor or 3.4Mbps per AP

## Slide 8: Performance Metrics
Cell-edge (5th percentile) and Mean User Throughput (per BSS) vs. Traffic Load (similar to the one proposed in [3])
‘How much can the system be loaded before user experience gets unacceptable?’
Traffic load
Traffic load
Notes: Data rates decrease when load increases due to increased interference and more active users sharing channel

## Slide 9: Performance Results 2.4GHz

## Slide 10: Isolated APs, 2.4GHz, DL
Served traffic is at most 40Mbps (to the 5th percentile)
Channel utilization approaching 75% (CSMA efficiency)

## Slide 11: Reuse 3, 2.4GHz, DL
Served traffic is at most 12Mbps (to the 5th percentile)
Channel utilization approaching 30%

## Slide 12: Reuse 1, 2.4GHz, DL
Served traffic is at most 7Mbps (to the 5th percentile)
Channel utilization approaching 10%

## Slide 13: Reuse 1, 3, Isolated, 2.4GHz, UL
Same trends as in downlink

## Slide 14: Capacity 2.4GHz
Maximum served traffic for cell-edge (5th percentile) considering user throughput of at least 5Mbps
Isolated [100%]
Isolated [100%]
Reuse 3 [100%]
Reuse 3 [100%]

## Slide 15: Spectral Efficiency 2.4GHz
Capacity divided by total spectrum usage in used direction
  Spectral Efficiency = Capacity / (reuse * 20MHz x F)
  FDOWNLINK = 0.75, FUPLINK = 0.25
Increases with tighter reuse, but still rather low
Reuse 3
Reuse 3

## Slide 16: Performance Results 5GHz

## Slide 17: Reuse 1-12, Isolated, 5GHz, DL and UL
Same trend as in 2.4GHz
Slightly better than 2.4GHz due to better isolation

## Slide 18: Capacity 5GHz
Maximum served traffic for cell-edge (5th percentile) considering user throughput of at least 5Mbps
Isolated [100%]
Isolated [100%]
Reuse 12 [100%]
Reuse 12 [100%]

## Slide 19: Spectral Efficiency 5GHz
Capacity divided by total spectrum usage in used direction
  Spectral Efficiency = Capacity / (reuse * 20MHz x F)
  FDOWNLINK = 0.75, FUPLINK = 0.25
Increases with tighter reuse, but still rather low

## Slide 20: Summary
High capacity multi cell systems can be built with WLAN technology (!)
  Inter-cell carrier sensing limits performance
  Possible to mitigate with more channels
Are there more spectrally efficient solutions?
Can we use this methodology (adopted from cellular network evaluations) to asses enhancements?

## Slide 21: References
[1] I. Siomina, A. Furuskär, and G. Fodor. A mathematical framework for statistical QoS and capacity studies in OFDM networks, Proc. of IEEE PIMRC ’09, Sep. 2009.
[2] 11-13-1081-00-0hew-hew-simulation-methodology
[3] 11-13-1137-02-0hew-definition-of-performance-metric

## Slide 22: AP to STA Radio Characteristics
Good coverage
  Well above total gain of -100dB which corresponds to -80dBm received power
Good isolation geometry due to walls and floors
September 2013

## Slide 23: Radio Characteristics - Cell Isolation
Propagation as a function of distance and floor
Total loss <105dB (received power >-85dBm) some two to three walls or floors away
2.4GHz
5.0GHz
September 2013

## Slide 24: Radio Characteristics - Cell Isolation
An active AP triggers carrier sensing (>-85dBm) in 7.1 and 5.9 neighbor APs (on average) in 2.4GHz and 5.0GHz respectively
September 2013
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
The graph shows average received power from neighbor APs in order of strength