## Slide 1: Some Par and 5C Requirements
Date: 2013-9-17
Authors:

## Slide 2: PAR Background – Defining the Scope of Work
What is a PAR: http://standards.ieee.org/faqs/pars.html
The PAR defines a IEEE-SA project and includes sections for:
5.2.a. Scope of the complete standard:
  The scope includes phrases to focus the groups work, like: ” ... Improve performance in dense environments ...”
5.2.b. Scope of the project:
5.4 Purpose:
5.5 Need for the Project:
So how much technical detail do we need in the PAR
Very little, just enough to scope the project
However, we all really do want to know we are about to create
  Use cases discussions and the 5C targets are very valuable

## Slide 3: HEW Study Group Current Discussions
Topics of discussion have included ...
Carrier offload, Efficiency, Dense Environments ,Improved performance, modeling, use cases, etc.
This background requirements will map into the PAR scope phrases as that might include:
  ... Improving the efficiency and performance of ...
  ... Include XYZ feature ...
  etc.
What has been missing in the current scope discussions?
Security
  Security is usually an afterthought in 802.11
  Proactively addressing security results in less hacks to put it in later
  Adding security work to the scope can do more than improve security

## Slide 4: Improving Security in HEW
Security is typically viewed as preventing potential attacks
Security work in HEW could also:
Improve efficiency
Support new use cases
Increase throughput
Enable new operational models (e.g. OBSS)
Increased robustness
Provide for ease-of-use
        Wi-Fi Attack Vectors (2011) doc.: IEEE 802.11-11-1250-00-00ai

## Slide 5: Security Related Areas for Possible HEW Technical Work
Security Improvements topics that could be considered:
  Group key and OBSS security
  Encapsulation algorithms
  Algorithm initialization (PN.IV, Sequence Num)
  Device to device authentication
  Privacy

## Slide 6: Group Keys and Broadcast Security
The AES-CCM Algorithm requires a unique key/nonce pair
  Stream cipher uses XOR, so stream must be unique
  In a non-star topology every device must have it’s own unique broadcast key
  Every device must then give every other device it’s key
  For N devices, this is N^2 protocol exchanges!!!
Other encryption modes would not have this problem!
  AES would still be used, but a new mode
  Benefits: scalable P2P security, OBSS security, efficiency, etc
  This would be a new encapsulation algorithm/mode

## Slide 7: Algorithm Initialization
802.11 use of the PN is odd and inefficient
  Issues and with multiple traffic queues
Possible solutions and work
  802.11ah has some proposed improvements that could be used and extended
  New modes of operation may have less stringent requirements
Benefits:
  Improved efficiency
  Faster initialization / authentication

## Slide 8: Privacy
Privacy is important
  New services in dense environments will expose mobile users
  Very strong public concern for consumer privacy
  Demonstrated DIY tools: creepydol-wifi-surveillance-project-debuts-at-blackhatdefcon
Possible mechanisms:
  Local MAC addresses integrated with authentication protocol
  Privacy and authentication are possible at the same time

## Slide 9: Device to device authentication
IEEE 802.11 does NOT have a have a good peer-to-peer authentication mechanism!
  This could be AP-to-AP (OBSS)
  Mobile-to-mobile
Benefits would include
  Very interesting new use cases with strong security
  Trust in OBSS communications
  Greatly improved ease of use

## Slide 10: Summary
The HEW PAR and 5C should include “security and privacy” in the scope and 5C.
Possible phrases for inclusion might look like:
  This amendment defines standardized modifications to .... supporting: ... - Enhancements to improve security and privacy ... ”