## Slide 1: Some Simulation Scenarios for HEW
Name | Affiliation | Phone | Email
Reza Hedayat | Cisco Systems |  | rehedaya@cisco.com
Brian Hart | Cisco Systems |  | brianh@cisco.com
Andrew Myles | Cisco Systems |  | amyles@cisco.com

## Slide 2: HEW simulations need to include P2P, unassociated & sticky clients to maintain connection with real world
  The HEW PAR emphasizes real world performance
  The simulation scenarios used in HEW also need to emphasize real world performance
  In particular, HEW simulation scenarios must include real world, high density AP/STA environments
  Simulation should include a high density AP/STA scenario with
    P2P traffic
    Unassociated clients
    Sticky clients

## Slide 3: The HEW PAR emphasizes real world performance
  SG formation motion
  Do you support starting a new study group called “high efficiency WLAN” to enhance 802.11 PHY and MAC in 2.4 and 5GHz with a focus on:
      Improving spectrum efficiency and area throughput
      Improving real world performance in indoor and outdoor deployments
      in the presence of interfering sources, dense heterogeneous networks
      in moderate to heavy user loaded APs

## Slide 4: The simulation scenarios used in HEW also need to emphasize real world performance
  During past two HEW F2F meetings, several contributions introduced many simulation scenarios of importance to the Wi-Fi industry
  13/1000r0 summarized and classified HEW simulations scenarios and defined a simulation scenario by:
    Topology: AP/STAs positions, obstructions , layout, propagation model
    Traffic model: STA-AP or P2P traffic, “idle” devices (management traffic)
    Parameters: List of PHY, MAC, Management parameters
    Interference scenario: Managed vs unmanaged WLAN
  Most of the simulation scenarios that have been proposed so far will provide insight into HEW
  However, there is not sufficient emphasis on scenarios that are linked to some real world WLAN scenarios
  This needs to change to ensure we make the right design choices for HEW

## Slide 5: HEW simulation scenarios must include real world, high density AP/STA environments
  People increasingly use their portable devices in public venues, often relying on Wi-Fi connectivity
  In many venues cellular connectivity will be insufficient due to the highly dense nature of the venues, further highlighting Wi-Fi’s importance
    e.g. stadiums, sport venues, airports, train stations
  The good news is that Wi-Fi is capable of addressing the needs of dense venues
  The bad news is that there are many old design choices (see 13/545r1) or new Wi-Fi use cases that significantly affect performance in dense environments:
    Soft-APs and tethering
    Excess management traffic such probe requests/responses
    P2P traffic
    Sticky clients
    …

## Slide 6: Simulation should include a high density AP/STA scenario with P2P traffic
  Many venues, particularly in the enterprise segment, achieve optimal performance by carefully managing the Wi-Fi infrastructure and the environment
  However, the increase of P2P use cases, relying on technology such as Wi-Fi Direct, IBSS and TDLS, diminishes the manageability in these venues
  We propose HEW considers a simulation scenario incorporating P2P
    Topology: uniform dense AP/STA distribution, with some percentage of random-location unmanaged P2P activity
    Traffic model: enterprise/mobile traffic models plus P2P traffic (e.g. video)
    Propagation/channel model: Indoor, with Channel D for most venues and Channel F for larger venues like malls and airports

## Slide 7: Simulation should include a high density AP/STA scenario with many unassociated clients
  Unassociated clients can contribute significantly to management traffic
    Many unassociated smartphones send probe requests to all the SSID’s stored on the phone
    Others broadcast probes and receive responses from all nearby, managed and unmanaged AP’s
  We propose HEW considers a simulation scenario incorporating unassociated clients
    Topology: uniform dense AP/STA distribution
      Managed AP’s with some unmanaged soft-APs
    Traffic model: mobile traffic models for smaller percentage of clients, plus initial/periodic management frames for larger percentage of clients
    Propagation/channel model: Indoor and outdoor
      Channel D and F for indoor venues
      Modified indoor or outdoor channel model suitable for stadiums

## Slide 8: Simulation should include a high density AP/STA scenario with sticky clients
  Old design choices mean portable devices often do not take advantage of closer APs and keep associated to farther AP’s
  However, sticky clients force usage of low MCS rates, wasting significant medium time
  We propose HEW considers a simulation scenario incorporating sticky clients
    Topology: uniform dense AP/STA distribution
    Traffic model: mobile traffic models for smaller percentage of clients, plus initial/periodic management frames for larger percentage of clients
    Propagation/channel model: Indoor and outdoor
      Channel D and F for indoor venues
      Modified indoor or outdoor channel model suitable for stadiums
    PHY and MAC parameters:
      A percentage of devices behave as sticky clients that have poor choice of AP selection and low MCS