## Slide 1: PAD for Soft AP
Date: 2013-09-15
Authors:

## Slide 2: Abstract
A informative discussion of the Soft AP and what PAD can do to help improve user experience

## Slide 3: Soft AP
Soft AP is short for Software enabled AP. While a Wireless Access Point is specifically made only to work as an AP, SoftAP is used to make a wireless client antenna work as both the AP and client.
With backhaul (Cellular or Wired) it can tether associated STAs to use Internet
There are emerging devices which can also act as Soft AP but not provide Internet tethering
  Camera, Lens, Memory Card, Hard drive, Printer…etc.
According to the latest spec 802.11-2012 it may belong to the category of Infrastructure BSS
  Ambiguity: Though the definition of Infrastructure contains DS, the Infrastructure BSS seems to exclude the DS

## Slide 4: Non-tethering Soft AP
Usually operate in on-demand and temporary fashion
  An intermediate method for P2P services requiring the popular “WiFi/802.11 connectivity”
  The number of members is very limited and the communication distance is short between members
Usually serve as AP by default
  No Advertisement Server
  No Group Owner negotiation
  Easier for general users to understand the status of connection
Manual selection of SSID is required
  If there are more than one known SSIDs nearby, user needs to (have the knowledge to) choose the corresponding network for specific service
Need to launch an App to get services
  E.g. Remote shooting, picture viewing, file browsing, …
  This step is only viable if the correct network has been chosen
  May confuse user if the setting is not instinctive
Currently support single band (2.4GHz)

## Slide 5: PAD for Soft AP
User simply launches an app to obtain the service
  Internet tethering
  Others (assuming P2P services, provided by AP directly)
PAD function discovers and helps STA differentiate and choose the correct network to join
  Indicate provision of Internet connectivity
  Indicate upper layer support
  Lightweight and energy efficient method is desirable
Notes: 8.4.2.94 Interworking element
Bit 4 is the Internet field. The AP or mesh STA sets this field to 1 if the network provides connectivity to the Internet; otherwise it is set to 0 indicating that it is unspecified whether the network provides connectivity to the Internet.

## Slide 6: An additional case to consider in PAD
A STA may already associate with an Internet-providing AP but need some local services not provided by the BSS
  may need post-association discovery to verify the presence of certain service
Pre-association discovery for Other APs is required
  Do PAD when the STA is still in association
  Help STA make necessary switch between different BSSs regarding required services

## Slide 7: Summary
Soft AP and the non-tethering Soft AP are introduced
An additional PAD case to be considered

## Slide 8: Appendix
“3.1 Definitions
Infrastructure: The infrastructure includes the distribution system medium (DSM), access point (AP), and portal entities. It is also the logical location of distribution and integration service functions of an extended service set (ESS). An infrastructure contains one or more APs and zero or more portals in addition to the distribution system (DS).”
“ 4.3.4.2 Extended service set (ESS): The large coverage network
The DS and infrastructure BSSs allow IEEE Std 802.11 to create a wireless network of arbitrary size and complexity. IEEE Std 802.11 refers to this type of network as the ESS network. An ESS is the union of the infrastructure BSSs with the same SSID connected by a DS. The ESS does not include the DS.”