## Slide 1: CID 205 BSSID Color Bits
Date: 2013-09-16
Authors:

## Slide 2: Authors:

## Slide 3: Sensitivity vs Spatial Reuse
There is a tradeoff between sensitivity of a receiver and spatial reuse
  More sensitive receivers are less aggressive regarding channel access
  Less aggressive STAs cause a reduction in spatial reuse when re-use is possible
  Determining when re-use is possible is complex
    Does my transmission interfere with the reception of another exchange?
    How can I determine if it will interfere?
  At least one simple rule can be identified:
  If the channel is being used by another STA within my BSS, then spatial re-use is not possible
    I.e. ignoring DLS, all other traffic in my BSS is with the AP and my exchange too, will be with the AP
  If traffic outside of my BSS is identifiable, then identification of potential opportunities for spatial reuse can be increased

## Slide 4: Identifying Traffic of OBSS
PAID holds information that might be used to identify traffic in OBSS, but not quite:
  UL SIG field contains Partial BSSID information
    dec(BSSID[39:47]) mod(29-1)) +1
    Receiving STAs can identify own BSSID when it is destination
  DL SIG field contains Partial AID identifying STA in my BSS
    (dec(AID[0:8])+dec(BSSID[44:47] xor BSSID[40:43]) * 25) mod(29)
    Receiving STAs cannot identify BSS of source or destination
Would like better information in ID field to help identify OBSS traffic

## Slide 5: Modify PHY SIG PAID Field
To assist in identifying BSS of frames
Place Color Bits and U/L indication in PHY SIG field
Modify existing TXVECTOR PARTIAL_AID
  DOWN DIRECTION:
    1 UPLINK bit, e.g. UP vs DOWN
      Used to determine definition of remaining 9 bits
    3 color bits, selected by AP to avoid overlap with neighbor APs
      Used to identify BSS
    6 PAID bits
      Identifies destination = (dec(AID[0:8])+dec(BSSID[44:47] xor BSSID[40:43]) * 25) mod(26)
  UP DIRECTION:
    1 UPLINK bit, e.g. UP vs DOWN
    9 PBSSID bits

## Slide 6: UPLINK Bit or Not
DIR=down
Color
ID=PAID
Bits:
1
3
6
Color
ID=PBSSID (Up) or PAID (Down)
Bits:
3 or 4
7 or 6
DIR=up
Color
ID=PBSSID
Bits:
1
3
6
DIR=up
ID=PBSSID
Bits:
1
9
OR
No UPLINK:

## Slide 7: UPLINK or Not?
The interesting case is when the color of an OBSS matches the color of MYBSS
i.e. Color bits collision:
  Without UPLINK bit:
    DOWN: One additional bit of ID to resolve color bits collisions
    UP: One additional bit of ID to resolve color bits collisions
  With UPLINK bit:
    DOWN: One less bit of ID to resolve color bits collisions
    UP: 3 additional bits of PBSSID vs 3 color bits – is the probability of color bits collision greater or lesser when the 3 additional bits are PBSSID bits instead of color bits?

## Slide 8: No UPLINK Bit
Receiver sees color match – might be OBSS or MYBSS
  Remaining ID bits might be PBSSID or PAID
  STA checks ID bits against MYBSS_PBSSID
    If match, must assume UL to MY_AP
      But still might be OBSS PAID or PBSSID color bits collision!
    If not match, might be DL to MYBSS_STAx, OBSS_AP, OBSS_STAx
  STA checks ID bits against known OBSS PBSSID values that are not also MYBSS PAID values
    Match means definitive identification of OBSS
Can identify possible MY_PBSSID match (UP)
Can identify some OBSS (UP)
  Need to check a list of ID values to identify OBSS

## Slide 9: UPLINK Bit Present
Receiver sees color match – might be OBSS or MYBSS
  If UP indicated, then remaining ID bits are PBSSID
    STA checks ID bits against MYBSS_PBSSID
      If match, must assume UL to MY_AP, even though might be OBSS PBSSID collision
      If not match, must assume OBSS – always correct
  If DOWN indicated, then remaining ID bits are PAID
    No way to tell if MYBSS or OBSS
    Must assume MYBSS
Can identify possible MY_PBSSID match (UP)
High probability to identify OBSS in color bits collision case with check against one ID value (UP)
  p = 1 - 1/2^9 = 0.998

## Slide 10: UPLINK Bit Summary
With UPLINK bit
  One less bit to resolve color bits collision
  Only need to check one PBSSID value against ID field to identify OBSS
Without UPLINK bit
  One more bit to resolve color bits collision
    Alternatively, one more bit for color
  Need to check multiple PBSSID values against ID field to identify OBSS
    Incomplete list errs conservatively to assumption of MYBSS

## Slide 11: STA Behavior
New Rules:
  If MYBSS Reception shall receive/defer
  If OBSS Reception obey specified CCA level behavior to determine if reception can be dropped and medium indication set to IDLE

## Slide 12: 1 MHz Exception
Exclude 1 MHz Receptions from new rules and structure

## Slide 13: NDP Frame Exception
Each NDP frame has its own unique PHY SIG field definition
The changes in this presentation are not applicable to the NDP frames

## Slide 14: Straw Poll
Do you support the proposed structure for the TXVECTOR parameter PARTIAL_AID and the accompanying rules of behavior for receiving STAs on slides 5 and 11, for non-NDP frames and excluding 1 MHz frames?
Y
N
A

## Slide 15: Draft Changes to D0.2, 9.17b Group ID and Partial AID in S1G PPDUs
Change the name of the subclause to:
  “9.17b Group ID, partial AID, UPLINK and Color in S1G PPDUs”
Duplicate Table 9-19b—Settings for the TXVECTOR parameters PARTIAL_AID
  Relabel the original table by appending “for 1 MHz PPDUs and NDP frames” to the title
  Relabel the new table by appending “for non-1 MHz PPDUs and non-NDP frames” to the title
  In the new table, change “mod 2^9” to “mod 2^6” and change the equation number as appropriate
  Change the note under the table to include a reference to both tables.

## Slide 16: Draft Changes to D0.2, 9.17b Group ID and Partial AID in S1G PPDUs (2)
Add the following text at the end of the subclause:
  A STA transmitting an S1G PPDU that is not a 1 MHz PPDU and is not an NDP frame and that is addressed to an AP shall set the TXVECTOR parameter UPLINK to 1. An AP transmitting an S1G PPDU that is not a 1 MHz PPDU and is not an NDP frame and that is addressed to a STA that is associated with that AP or that is sent by a DLS or TDLS STA in a direct path to a DLS or TDLS peer STA shall set the TXVECTOR parameter UPLINK to 0. The TXVECTOR parameter UPLINK is not present for 1 MHz frames.
  A STA transmitting an S1G PPDU that is not a 1 MHz PPDU and is not an NDP frame and that is addressed to an AP need not include the TXVECTOR parameter COLOR in the TXVECTOR. A STA transmitting an S1G PPDU that is not a 1 MHz PPDU and is not an NDP frame and that is sent by a DLS or TDLS STA in a direct path to a DLS or TDLS peer STA shall set the TXVECTOR parameter COLOR to the value of the COLOR parameter, if present, from the RXVECTOR of the most recently received frame from its associated AP or from the DO of the IBSS of which it is a member that contained a COLOR parameter, or to 0 if no such frame has been received. An AP transmitting an S1G PPDU that is not a 1 MHz PPDU and is not an NDP frame and that is addressed to a STA that is associated with that AP shall set the TXVECTOR parameter COLOR to a value of its choosing within the range 1 to 7 and shall maintain that value for the duration of the existence of the BSS.

## Slide 17: Draft 0.2 changes to 24.2.2 TXVECTOR and RXVECTOR parameters
In Table 24-1—TXVECTOR and RXVECTOR parameters
  Add two new rows as shown:
Parameter | Condition | Value | TXVECTOR | RXVECTOR
UPLINK | NDP_FRAME is 0 and FORMAT is S1G and CH_BANDWIDTH is not equal to CBW1 | 0 or 1 | Yes | Yes
 | Otherwise | Not Present | No | No
COLOR | NDP_FRAME is 0 and FORMAT is S1G and CH_BANDWIDTH is not equal to CBW1 and UPLINK is 1. | Integer in the range 0-7 | Yes | Yes
 | Otherwise | Not Present | No | No

## Slide 18: Draft 0.2 changes to 24.3.8.2
Changes to 24.3.8.2.1.4 SIG definition
In Figure 24-26—SIG-1 structure
  Change the reserved bit at B2 to UPLINK
  Change the PAID field to ID
In Table 24-11—Fields in the SIG field of short preamble
  Change reserved bit B2 to UPLINK
  Change the description of B2 from “set to 1” to “set to the value of the TXVECTOR parameter UPLINK”
  Change PAID to ID
Change the description of B7-15 (ID) to:
  If UPLINK is not present or set to 1, set to the value of the TXVECTOR parameter PARTIAL_AID. PARTIAL_AID provides an abbreviated indication of the intended recipient(s) of the PSDU(see 9.17b (Group ID and partial AID in S1G PPDUs))). If UPLINK is set to 0, B7-B9 are set to the value of the TXVECTOR parameter COLOR and B10-B15 are set to the value of the TXVECTOR parameter PARTIAL_AID.
Make identical changes in 24.3.8.2.2.1.4 SIG-A definition

## Slide 19: Draft 0.2 changes to 24.3.20 PHY receive procedure
    If a valid SIGA parity bit is indicated, and the UPLINK bit is 1 and the ID field value matches the PBSSID of the BSS of which the STA is a member or the UPLINK bit is 0 and the COLOR field value matches the COLOR indicated by the AP to which the STA is associated, then the S1G PHY shall maintain PHY-CCA.indication(BUSY, channel-list) for the predicted duration of the transmitted PPDU, as defined by RXTIME in Equation (24-105), for all supported modes, unsupported modes, Reserved S1G-SIG-A Indication, invalid S1G-SIG-A CRC and invalid SIG-A Length field value. If a valid SIGA parity bit is indicated, and the UPLINK bit is 1 and the ID field value does not match the PBSSID of the BSS of which the STA is a member or the UPLINK bit is 0 and the COLOR field value does not match the COLOR indicated by the AP to which the STA is associated, then the S1G PHY shall maintain PHY-CCA.indication(BUSY, channel-list) for the predicted duration of the transmitted PPDU, as defined by RXTIME in Equation (24-105), for all supported modes, unsupported modes, Reserved S1G-SIG-A Indication, invalid S1G-SIG-A CRC and invalid SIG-A Length field value if the reception meets the minimum CCA sensitivity level specified in 24.3.19.5.4.

## Slide 20: References
[1] xxxx