## Slide 1: Date: 2013-10-11
Proposal for DSRC band coexistence

## Slide 2: Abstract
This proposal aims
  to promote a discussion of a potential compromise solution between the automotive and Wi-Fi industries to address concerns about spectrum sharing.
  to promote dialog and resolution to avoid undue delay in deploying DSRC for safety-of-life services

## Slide 3: Concerns with NPRM Proposal
The NPRM proposal opens all DSRC spectrum for Wi-Fi operations, which may invalidate all DSRC testing done so far and hence cause significant impact (delay) on the coming DSRC rule making
Current DSRC safety channel is placed in Ch172, which is in the middle of the new 160MHz UII channel. Coexistence with DSRC can lead to low usage of the new 160MHz since Ch172 is crowded.
UNII devices may have to detect 10MHz operation of DSRC, which is quite different from radar detection and requires new hardware changes and testing procedure

## Slide 4: A Compromise Proposal with Two Points
Point #1: Where not to share and where to share:
  Upper fraction of the spectrum could be dedicated to DSRC operation
  The spectrum sharing discussion would be contained in the lower fraction of the spectrum
Point #2: How to share:
  20MHz operation for DSRC can make spectrum sharing easier

## Slide 5: Point #1: DSRC should retain exclusive right to 5.895GHz - 5.925GHz spectrum
Wide bandwidth channels desired to support high throughput requirements (802.11ac targeted at 1.7Gbps data rate per user)
  Higher bandwidth channels (80MHz, 160MHz) are very valuable assets for 802.11ac
Ch. 181 (5.895 – 5.915GHz) is of limited importance to Wi-Fi – only adds a new 20MHz channel
We should contain discussions of spectrum sharing to spectrum between 5.850GHz – 5.895GHz
144
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
IEEE channel #
20 MHz
40 MHz
80 MHz
160 MHz
UNII-1
UNII-2
UNII-2
UNII-3
5250
MHz
5350
MHz
5470
MHz
5725
MHz
NEW
96
92
88
84
80
76
72
68
169
173
177
181
5825
MHz
5925
MHz
NEW
Currently available channels
Potential channels
5895
MHz

## Slide 6: Why is this important?
A critically important principle on which we hope all can agree is that the NHSTA decision on DSRC should not be delayed, allowing the community to move toward V2V safety deployment without waiting for technical solutions for spectrum sharing
  Existing research and testing programs on V2V safety are based on exclusive right of the spectrum
  Moving V2V safety to this portion of the spectrum can be a viable option to ensure existing results are still valid, and require only a limited amount of additional testing
It buys time to determine a well-considered technical solution to share in the lower fraction of the spectrum
  Wi-Fi and DSRC industries can jointly determine a solution in this portion of the spectrum with a less stringent time constraint and significantly less controversy

## Slide 7: Point #2: 20MHz DSRC operation in the lower portion can make spectrum sharing easier
The overhead of 10MHz signal detection
  Not decodable by existing Wi-Fi devices
  New hardware has to be developed and tested, following rigorous testing procedures
  Left-over interference has to be characterized and tested for all DSRC applications and potentially all use scenarios
20MHz operation makes the DSRC signals understandable by Wi-Fi devices; transmission priority can be provided to DSRC by existing Wi-Fi mechanisms
  For example, EDCA defined in IEEE 802.11e

## Slide 8: 20MHz Channelization Performance
Comparable performance for most vehicular channels as compared to 10MHz
  20MHz leads to shorter packet transmission and thus better channel tracking in high mobility channel models, as compared to 10Mhz channelization
  20MHz has shorter GI (0.8us) and thus more self-interference when delay spread is longer than GI
Maximum excess delay: 0.5us
Maximum excess delay: 2.5us

## Slide 9: Putting the two points together
Open only the lower fraction of the spectrum to UNII devices
  Leave 20MHz or 30MHz dedicated spectrum for DSRC
  Share the Channel 173 and 177 between DSRC and UNII
  Ensure Chanel 181 is NOT used by UNII devices
For the shared spectrum
  Encourage 20MHz operation  much easier for Wi-Fi to detect and provide higher priority to DSRC signals
  Develop sharing solutions in IEEE (refer to 994r0)
DSRC Band
181
161
165
169
173
177
177
173
DSRC Channels
Wi-Fi Channels
160MHz
80MHz
80MHz
X
Proposed boundary of UNII4

## Slide 10: Current Proposed Spectrum Allocation and OOBE Requirements in NPRM
Available for WLAN
161
DSRC Band
U-NII 4
U-NII Worldwide
U-NII 3
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
-27 - G dBm/MHz
5850
5875
5925
5895
165
169
173
177
181
-17 - G dBm/MHz

## Slide 11: Proposed Scheme 1: Spectrum Allocation and OOBE Requirement
U-NII 3
Available for WLAN
Keep Ch182 and Ch184 for DSRC dedicated use
The same UNII-4 rule as in NPRM, but stops at 5905MHz
161
DSRC Band
U-NII 4
U-NII Worldwide
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
-27 - G dBm/MHz
5850
5875
5925
5895
165
169
173
177
184
182
-17-GdBm/MHz
5905
-27-GdBm/MHz
Notes: Questions:
What is the basis of picking OOBE rule? (Mike)
What is band next to DSRC band? (Mike)
What is the current OOBE rule for DSRC channels? (Check with Amir, Roger, John or Sue)

## Slide 12: Proposed Scheme 2: Spectrum Allocation and OOBE Requirement
U-NII 3
Available for WLAN
Keep Ch180, 182 and 184 for DSRC dedicated use
Relax the OOBE requirement for UNII devices in DSRC band
161
DSRC Band
U-NII 4
U-NII Worldwide
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
-27 - G dBm/MHz
5850
5875
5925
5895
165
169
173
177
184
180
182
-27-GdBm/MHz
-5-GdBm/MHz
-17-GdBm/MHz
Notes: Questions:
What is the basis of picking OOBE rule? (Mike)
What is band next to DSRC band? (Mike)
What is the current OOBE rule for DSRC channels? (Check with Amir, Roger, John or Sue)

## Slide 13: Benefits of the compromise scheme
20MHz to 30MHz dedicated channels for critical DSRC applications
Easier to give higher priority to DSRC in the shared spectrum due to easy detection of 20MHz waveforms
Keep the same number of 80MHz/160MHz channels; lose one 20MHz channel
No need to add new hardware to detect 11p transmissions  20MHz transmissions are easy to detect and decode by existing Wi-Fi chipsets
Much better utility of 160MHz channel if critical safety channel is moving to the dedicated spectrum at higher end of DSRC band
Remove the need for lengthy joint testing and possible technical gridlock
Minimize uncertainty and disruption to DSRC and provide 160MHz channel to Wi-Fi at minimal additional cost

## Slide 14: Appendix

## Slide 15: Technical Issues and Mitigation
Cross-channel interference: does the proposed compromise make the cross channel interference worse?
  Not really. The two 10MHz channels in dedicated DSRC spectrum will see less cross-channel interference as compared to the NRPM proposal or current DSRC channelization
  Cross-channel interference has always been a problem between existing service channel and safety channel; the compromise does not make things worse
High power public safety channel (aka Ch184) and potentially other channels requested by other ITS players:
  Ch184 has not been the focus of existing model deployment
  A good time to revisit the need or spectrum allocation for such channel
    May be combined with the V2x safety channel
    May be assigned to the shared spectrum rather than using the dedicated spectrum
20MHz channelization and performance degradation in shared spectrum: 20MHz channelization does not necessarily lead to performance degradation with the latest receiver technology

## Slide 16: Cross-Channel Interference Comparison (I)
Previous DSRC channel plan
  Ch172 is 5MHz away from the ISM band
  ISM band has OOBE rule of only -20dBr from the PSD limit (33dBm/MHz with 30dBm peak power)
  Ch172 can potentially see maximum 13dBm/MHz interference leakage from ISM band
Available for WLAN
DSRC Band
Frequency [GHz]
5.85
5.725
0 dBr
-20 dBr
FCC 15.247(d)
Total Power ≤ 30 dBm
FCC 15.247(b)(3)
5.875
172

## Slide 17: Cross-Channel Interference Comparison (II)
NPRM channel allocation
  Ch172 overlaps Ch173 (20MHz) and corresponding 40MHz, 80MHz and 160MHz channels
    Remaining interference may exist from spectrum sharing techniques
  Ch172 is right next to Ch169 (20MHz) and 10MHz away from Ch177
    Interference from adjacent channels with potentially no protection
Available for WLAN
161
DSRC Band
U-NII 4
U-NII Worldwide
U-NII 3
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
5850
5875
5925
5895
165
169
173
177
181
-17 - G dBm/MHz
172

## Slide 18: Cross-Channel Interference Comparison (III)
Proposed compromise scheme
  10MHz away from closet Wi-Fi channel (Ch177)
  Maximum interference limited by -17dBm/MHz (-7dBm over 10MHz channel)
  Practical interference from measurement: Ch182 sees -17dBm/MHz+pathloss (35dB attenuation at 10MHz edge); Ch184 sees -27dBm/MHz+pathloss (45dB attenuation at 20MHz edge)
    Can further be improved by limiting the maximum transmit power allowed on Ch177
    48dB free space pathloss for co-located 5.9GHz transmitter/receiver at 1m apart
U-NII 3
Available for WLAN
161
DSRC Band
U-NII 4
U-NII Worldwide
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
-27 - G dBm/MHz
5850
5875
5925
5895
165
169
173
177
182
-17-GdBm/MHz
5905
184

## Slide 19: Cross-Channel Interference between DSRC Channels
In current DSRC channelization, service channel and safety channels are next to each other with no guard band
  When transmitting at service channel, the leakage will contaminate the reception capability on the safety channel
  May be controlled by lowering the maximum allowed power on service channel
May require improved receiver to further mitigate the problem
Proposed compromise does not change or worsen the nature of the problem

## Slide 20: Ch184 and Other Potential DSRC Channels
Ch184 has not been the focus of existing DSRC technology validation process
A good time to revisit the spectrum allocation plan for such channels
  May be combined with the V2x safety channel – reduce the need for a separate radio
  May be assigned to the shared spectrum rather than using the dedicated spectrum