## Slide 1: Proposed direction and priorities for HEW
Date: 2013-11-12
Authors:

## Slide 2: Abstract
This submission presents important technical areas that HEW needs to address to achieve the envisioned efficiency objectives.
We identify problem fields and ask questions to stimulate discussions among HEW participants.
Finally we provide recommendations for the development of the PAR and 5C documents.

## Slide 3: Massive, uncoordinated deployments
802.11 – A technology for everybody
  Simple set-up
  Unlicensed operation
  Cordless extension of a private layer 2 network
1st gen. equipment slows down current operation [1]
  Severe efficiency impact
Too much signaling at low MCSs [2,3]
CSMA/CA doesn’t collapse, but …
  Static Contention Windows & many STAs  lots of collisions
  Throughput with many users slower than equally shared
Static carrier sensing threshold limits performance
  “One fits all” approaches are suboptimal [4]
  Consider adaptive solution

## Slide 4: 802.11 legacy devices
Ethernet has a history of deprecating outdated sections
  How about 802.11?
TGmc revises 802.11-2012
  Inclusion of .11aa, .11ad, .11ae
  Withdrawal of outdated clauses
    FHSS PHY, Clause 14
      Annex I & K
    IR PHY, Clause 15
    SDL, Annex J
Compatibility to .11n & .11ac important
  Decide if 1 & 2 Mb/s 802.11-1997 compatibility is still needed
Should HEW further deprecate older amendments?
  Reuse the good ideas [5]
    Which are good?
  Prioritize those that nobody uses

## Slide 5: All new?
“For this standard, the value of the protocol version is 0. All other values are reserved. The revision level will be incremented only when a fundamental incompatibility exists between a new revision and the prior edition of the standard.” [6]
“Revision level field processing – A MAC entity that receives a frame with a higher revision level than it supports shall discard the frame without indication to the sending STA or to LLC.” [7]
Should HEW start all over? New version?
  Revolution or evolution?
    Same question but process related in [8]
If HEW starts all over, use 64 b addresses
  IEEE SA strongly encourages to make use of EUI-64 [9]

## Slide 6: Wi-Fi Direct
Difficult to handle as it forms yet another OBSS
  Signaling overhead, beacon/probe frames etc.
Unlicensed spectrum open to everyone, but …
  Enterprises and operators carefully design WLANs in their premises
  Wi-Fi Direct disrupts this planning
Enterprises require mechanisms to discourage use of Wi-Fi Direct beyond what is available in the current WFA program

## Slide 7: Bufferbloat [10,11]
Small frames inefficient to transmit
  Frame aggregation as countermeasure
Frame aggregation = buffering
  Buffering increases latency
Buffering everywhere
  OS, driver, NIC, AP, switch, router …
  Prevents packet loss
    High throughput w/ synthetic traffic
Huge buffers severely increase latency
  Any traffic delayed
  If delay ≫ RTT
    TCP’s congestion control doesn’t work
Bufferbloat is a serious problem in today’s networks
  Interaction of MCS and buffer size
Define Active Queue management in HEW

## Slide 8: HEW usage scenarios
Focus on relevant market segments
  “At present, more than 70 percent of mobile traffic is generated indoors.” [12]
    >85 % indoors in 2018 [13]
    Obstructions provide chances for spatial frequency reuse
Improve user experience in 802.11’s dominant market segments
  Solve existing problems in lieu of adding new features
Do not design HEW for yet another niche market

## Slide 9: Enterprise usage
Centralized installations
  Controlled environment
Spectrum sharing “managed” through central controllers
Office space becomes more dynamic
  More wireless links used and needed
Mission critical networks
  Hospitals rely on wireless data, etc.

## Slide 10: Home usage
Home Wi-Fi usage to double by 2015 [14]
Severe OBSS problem in densely populated areas
  Apartments
Uncoordinated spectrum sharing
  Coexistence problem
Use of 802.11ad (60 GHz) in room /CE usage scenarios highly recommended
  Additional spectrum
  Efficient spatial frequency @ 60 GHz
  Tight coupling with <6 GHz WLAN for seamless connectivity throughout home

## Slide 11: Outdoor usage
Mostly LOS conditions
Limited obstructions
  Low spatial frequency reuse possible
Carrier sensing range too large
  Many un co-ordinated networks
  Busy channel condition blocks large areas
Difficult propagation
  Delay spread
  Doppler spread
Different mobility than indoors
Might be difficult to harmonize with indoor needs
Two classes of solutions
  One managed, one not?

## Slide 12: Recommendations
“It is always possible to agglutinate multiple separate problems into a single complex interdependent solution. In most cases this is a bad idea.” [4]

## Slide 13: 1) HEW and legacy 802.11
Consider .11 g, .11n, & .11ac only
  Encourage more greenfield operation
Contemplate deprecating older equipment
  1st and 2nd gen. devices
  802.11a/b
Use and/or modify existing 802.11 features instead of increasing the feature set
  .11k, .11u, .11v, .11r etc.
  See also [5]

## Slide 14: 2) HEW and bufferbloat
Bufferbloat problem is real
  Real traffic is a mixture of different streams
    DNS, HTTP, IMAP, FTP, VoIP, RTP etc.
    In the past, tendency in 802.11 to consider synthetic traffic sources in simulations
    Low latency as important as high throughput – even more important?
Although hardware and software is vendor specific some guidance seems to be inevitable
  HEW to investigate if a common queuing mechanism is needed
    Different vendors in up-/downlink direction  interoperability

## Slide 15: 3) HEW features
Evolve 802.11
  Do not start all over
Improve 802.11 where it has shortcomings
  OBSS
  Small frame efficiency
Solve management frame storms
Combine and mandate existing 802.11 features
  Mandate useful features for HEW STAs [5]
    Examples: .11k, .11u, .11v, .11r, .11y
Find mechanisms to better coexist with Wi-Fi Direct

## Slide 16: 4) HEW usage scenarios
Strengthen 802.11 in its key market segments
  Enterprise
  Home
  Dense indoor hotspots
Consider 2.4 GHz and 5 GHz
  .11ad as complement to HEW
Focus on indoor and pedestrian speeds
Consider benefits of NLOS conditions
  Chances for concurrent transmissions
  Better spatial frequency reuse
  Survey changes to current Carrier Sensing scheme

## Slide 17: References
D. Liu et al., “Operator Oriented Wi-Fi – Problem Analysis and Proposals,” 11-13-0343-00, https://mentor.ieee.org/802.11/dcn/13/11-13-0343-00-0wng-operator-oriented-wi-fi.pptx
M. Cheong et al., “Wi-Fi Interference Measurement in Korea (Part I),” 11-13-0556-01, https://mentor.ieee.org/802.11/dcn/13/11-13-0556-01-0hew-wi-fi-interference-measurements-in-korea.ppt
K. Yunoki and Y. Misawa, “Understanding Current Situation of Public Wi-Fi Usage - Possible Requirements for HEW,” 11-13-0523-02, https://mentor.ieee.org/802.11/dcn/13/11-13-0523-02-0hew-understanding-current-situation-of-public-wifi-usage.pptx
R. Callon, “The Twelve Networking Truths,” IETF RFC 1925, http://tools.ietf.org/html/rfc1925
B. Hart, “A perspective on what any High Efficiency Wireless TG should and should not do,” 11-13-0549-00, https://mentor.ieee.org/802.11/dcn/13/11-13-0549-00-0hew-a-perspective-on-what-any-high-efficiency-wireless-tg-should-and-should-not-do.pptx
IEEE 802.11-2007, “8.2.4.1.2 Protocol Version field”
IEEE 802.11-2007, “9.24.2 Revision level field processing”
A. Myles, “Evolution or revolution?,” 11-04-0247-00, https://mentor.ieee.org/802.11/dcn/04/11-04-0247-00-0wng-evolution-revolution.ppt
IEEE SA, “Guidelines for Use of EUI,” http://standards.ieee.org/develop/regauth/tut/eui.pdf
V. Cerf, V. Jacobson, N. Weaver, and J. Gettys, “BufferBloat: What's Wrong with the Internet?, ” http://portal.acm.org/ft_gateway.cfm?id=2076798&type=pdf
J. Gettys and K. Nichols, “Bufferbloat: Dark Buffers in the Internet,” http://portal.acm.org/ft_gateway.cfm?id=2071893&type=pdf
Ericsson, “Ericsson Radio Dot System revolutionizes indoor coverage,” http://www.ericsson.com/news/130925-ericsson-radio-dot-system-revolutionizes-indoor-coverage_244129227_c
J. Madden, Mobile Experts, “DAS; Absorbing Small Cells and Wi-Fi,” http://mobile-experts.net/product_info.php?products_id=54?osCsid=8b28efe9d56f6aee302a0619d1a7bb0d
iGR, “U.S. Home Broadband & WiFi Usage Forecast, 2012-2017,” https://igr-inc.com/Advisory_And_Subscription_Services/Small_Cell_Architectures/us_home_broadband_wifi_2017.asp