## Slide 1: HLP Wait Time
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Date: 2013-11-07
Authors:

## Slide 2: Abstract
This document explains the usage of dot11FILSHLPWaitTime.

## Slide 3: Comment
CID2865
  "Have multiple questions regarding the paragraph in line 24 on page 90:
  1). How long should the AP wait for HLP packet from DS to the STA before transmitting association response frame?
  No definition about the HLP wait time in D1.0.

## Slide 4: dot11AssociationResponseTimeOut
mc2.0 6.3.7.2.2
  MLME-ASSOCIATE.request
  Specifies a time limit (in TU) by dot11AssociationResponseTimeOut, after which the associate procedure is terminated.
  >= 1
  This parameter is used by non-AP STA for only internal use.

## Slide 5: Proposal
Define dot11FILSHLPWaitTime and FILS HLP Wait Time element
  Configured in AP.
  Transmitted in FILS HLP Wait Time element (new) in Beacon/Probe Resp.
STA sets
  dot11AssociationResponseTimeOut = dot11FILSHLPWaitTime + n (n>=1)
Note:
  AP may not inspect the HLP packet.
  AP does not know whether the HLP response(s) will come or not.
  AP may forward HLP broadcast packet(s) in Assoc. Resp.
  AP may generate HLP packet(s) for the STA such as gratuitous ARP of the gateway.

## Slide 6: FILS HLP Wait Time element
This element is transmitted in Beacon/Probe Response.
FILS HLP Wait Time field indicates the AP’s dot11FILSHLPWaitTime.

## Slide 7: Usage
STA
AP
3rd party
(e.g. DHCP server)
dot11FILSHLPWaitTime
HLP-A
HLP-B
dot11AssociationResponseTimeOut
Association Request
w/HLP-A
HLP-C
HLP-D
HLP-D as normal data frame
Association Response
w/HLP-B and HLP-C

## Slide 8: AP behavior
AP transmits its dot11FILSHLPWaitTime by Beacon/Probe Response.
AP should wait dot11FILSHLPWaitTime after receiving Association Request for HLP packets from the network.
But AP may transmit Association Response before dot11FILSHLPWaitTime.

## Slide 9: STA behavior
STA sets its dot11AssociationResponseTimeOut to dot11FILSHLPWaitTime in Beacon/Probe Response plus n (>=1).
STA shall wait for Association Response until dot11AssociationResponseTimeOut after transmitting Association Request.

## Slide 10: Strawpoll
Do you prefer this resolution?
Result
  Yes:
  No:
  Need more discussion:
  Don’t care: