## Slide 1: HLP MSDU
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Date: 2013-11-07
Authors:

## Slide 2: Abstract
This document explains HLP MSDU in FILS HLP Wrapped Data TLV.

## Slide 3: Comment
CID2157
  "Forwards the HLP(s) to the DS”
  Need more detail. E.g. Reference Annex R2.2 (that takes us to 5.2.2.2; where we see a number of parameters. The HLP field is the concatenation of DA and SA and payload but the 5.2.2.2 service primitive also requires that the DA and SA be passed explicitly. Then the AP needs to extract these parameters from the HLP field (needs language) and pass them explicitly. Since data = MSDU, and I believe (check me) that an MSDU includes DA and SA, I think it is OK to leave (not delete) the DA and SA in the HLP field = MSDU.

## Slide 4: R.2.2
R.2.2 MSDU transfer
R.2.2.1 General
The DS-UNITDATA primitives accept and deliver IEEE Std 802.11 MSDUs, including all the parameters and data as defined in 5.2.2.2 (Semantics of the service primitive). These tuples are called distribution system service data units (DSSDUs).

## Slide 5: 5.2.2.2
5.2.2 MA-UNITDATA.request
  5.2.2.1 Function
    This primitive requests a transfer of an MSDU from a local LLC sublayer entity to a single peer LLC sublayer entity, or multiple peer LLC sublayer entities in the case of group addresses.
  5.2.2.2 Semantics of the service primitive
    The parameters of the primitive are as follows:
    MA-UNITDATA.request (source address, destination address, routing information, data, priority, service class)
    The data parameter specifies the MSDU to be transmitted by the MAC sublayer entity. The length of the MSDU shall be less than or equal to the value shown in Table 8-1 (Maximum MSDU and A-MSDU sizes)
MSDU is exactly same as LLC/SNAP header + payload.

## Slide 6: FILS HLP wrapped data TLV format
D1.0
Combine LLC/SNAP field and HLP field into HLP MSDU field.
Exact contents are completely same.

## Slide 7: Strawpoll
Do you prefer this resolution?
Result
  Yes:
  No:
  Need more discussion:
  Don’t care: