## Slide 1: KDE Container TLV
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Date: 2013-11-07
Authors:

## Slide 2: Abstract
This document explains KDE Container TLV.

## Slide 3: Comment
CID2219
  When are the Key RSC and GTK Transfer TLVs used and when would the FILS KDE Container element be used and why do we have both of these options?
  Define when the Key RSC and GTK Transfer TLVs will be used and when the KDE Container element will be used.
Container for GTK is duplicated in D1.0.
  8.4.2.181 FILS KDE container element
  8.4.2.186.6 GTK Transfer TLV

## Slide 4: Proposal
Remove FILS KDE Container element.
Modify GTK Transfer TLV as KDE Container TLV.
  The contents of KDE Container is same as FILS KDE Container element.

## Slide 5: 8.4.2.186.6 KDE Container TLV
  The KDE Container TLV is used to communicate one or more KDEs in a FILS authentication exchange. The KDE Container TLV may contain one or more KDEs. The format of the KDE Container TLV is shown in Figure 8-401dp (KDE Container TLV format).
  The Type ID field is equal to the KDE Container value in Table 8-183ai (FILS Secure Container TLV).
  The Length field specifies the total number of octets of all the KDEs.
  The encoding of the KDE field is defined in Table 11-6 (KDE) of 11.6.2 (EAPOL-Key frames).

## Slide 6: Strawpoll
Do you prefer this resolution?
Result
  Yes:
  No:
  Need more discussion:
  Don’t care: