## Slide 1: Access Control Enhancement
Date: 2013-11-08
Authors:

## Slide 2: Abstract
This contribution shows that time limitation for low rate frames improve aggregate throughput in a BSS.

## Slide 3: Recap
Even high rate communication degrades its throughput performance when low rate communication exists in parallel. This issue was explained in doc. 13/0801r1(NTT) and 13/1073r0(KDDI).
TDMA like access control mechanism may mitigate this performance degradation by restricting longer time occupation of low rate frames on WLAN.
Performance evaluation in densely STAs deployed BSS is shown in the following slides:

## Slide 4: Time occupation of a 802.11 frame
Assumptions:
11n
1X1 SISO, 20MHzBW
Not considering frame aggregation.
Data rate | Time occupation
6.5Mbps (MCS 0) | 2059 usec
13Mbps (MCS 1) | 1127 usec
19.5Mbps (MCS 2) | 815 usec
26Mbps (MCS 3) | 659 usec
39Mbps (MCS 4) | 503 usec
52Mbps (MCS 5) | 423 usec
58.5Mbps (MCS 6) | 399 usec
65Mbps (MCS 7) | 379 usec
When a STA transmits 1500B IP packet, time occupations at each data rate are:
Calculation detail is on Slide 13.
Apparently, lower rate frames occupy much time.

## Slide 5: Assumed Throughput
Data rate | No. of STAs | Assumed throughput /STA
6.5Mbps (MCS 0) | 10 | 0.19Mbps
13Mbps (MCS 1) | 10 | 0.19Mbps
19.5Mbps (MCS 2) | 10 | 0.19Mbps
26Mbps (MCS 3) | 10 | 0.19Mbps
39Mbps (MCS 4) | 10 | 0.19Mbps
52Mbps (MCS 5) | 10 | 0.19Mbps
58.5Mbps (MCS 6) | 10 | 0.19Mbps
65Mbps (MCS 7) | 10 | 0.19Mbps
Total | 80 | 
Considering 10 STAs communicating under each MCS, assumed throughputs are:
When transmission opportunities among STAs are equal, data amounts per unit time are equal also. So assumed throughputs are equal.
Not considering retry, conflicts or losses.
Results are just derived from time occupation in the previous slide.

## Slide 6: Consideration
Throughputs on each STA are equalized regardless of link data rate. Because transmission opportunities are equally given to each STA at CSMA/CA mechanism.
High rate link can’t perform its available throughput due to lack of transmission opportunities. Do you think it’s a proper manner?
How about equalizing time resource occupancies among STAs instead of equal transmission opportunities?
 Next slide

## Slide 7: Assumed Throughput by equal time allocation for each link
Data rate | No. of STAs | Aggregated occupation | Per each link | Assumed throughput
6.5Mbps (MCS 0) | 10 | 125msec | 12.5msec | 0.07Mbps
13Mbps (MCS 1) | 10 | 125msec | 12.5msec | 0.13Mbps
19.5Mbps (MCS 2) | 10 | 125msec | 12.5msec | 0.18Mbps
26Mbps (MCS 3) | 10 | 125msec | 12.5msec | 0.23Mbps
39Mbps (MCS 4) | 10 | 125msec | 12.5msec | 0.30Mbps
52Mbps (MCS 5) | 10 | 125msec | 12.5msec | 0.36Mbps
58.5Mbps (MCS 6) | 10 | 125msec | 12.5msec | 0.38Mbps
65Mbps (MCS 7) | 10 | 125msec | 12.5msec | 0.40Mbps
Total | 80 | 1000msec |  | 

## Slide 8: Throughput Comparison (Current stds. vs. Equal time allocation)
Data rate | No. of STAs | Current stds. | Equal time | Comparison
6.5Mbps (MCS 0) | 10 | 0.19Mbps | 0.07Mbps | Down
13Mbps (MCS 1) | 10 | 0.19Mbps | 0.13Mbps | Down
19.5Mbps (MCS 2) | 10 | 0.19Mbps | 0.18Mbps | Down
26Mbps (MCS 3) | 10 | 0.19Mbps | 0.23Mbps | Up
39Mbps (MCS 4) | 10 | 0.19Mbps | 0.30Mbps | Up
52Mbps (MCS 5) | 10 | 0.19Mbps | 0.36Mbps | Up
58.5Mbps (MCS 6) | 10 | 0.19Mbps | 0.38Mbps | Up
65Mbps (MCS 7) | 10 | 0.19Mbps | 0.40Mbps | Up
Aggregated throughput (80 STAs) |  | 15.1Mbps | 20.4Mbps | Up

## Slide 9: Summary
Time limitation for low rate frames will improve aggregated throughput on a BSS. It’s equivalent to raise proportion of high rate frames.
However, this consideration showed just an aspect for efficiency improvement. It’s just from simple mathematical evaluations.

## Slide 10: Issues
Mechanism to increase proportion of higher rate frames
Reduction of retry frames
  Many implementations lower data rate when re-transmission increases due to frame errors or losses. It’s conflicting behavior against increasing higher rate frames.
Low rate transmissions at cell edge
Coexistence with current standard’s devices
  Suppressing low rate frames of legacy devices may be needed.
Considerations of OBSS environment
Integration with existing mechanisms
  RTS/CTS, PCF, HCCA, frame aggregation,,,
etc.

## Slide 11: Possible function for HEW
Control for increasing higher rate frames’ proportion

## Slide 12: References
IEEE 11-13/0801r1: Issues of low rate transmission (NTT)
IEEE 11-13/1073r0: Access control enhancement (KDDI)

## Slide 13: Annex: Occupied time calculation
L-STF
L-LTF
L-SIG
HT-
STF
HT-SIG
HT-
LTF
8us
8us
4us
8us
4us
4us
Data
SIFS
L-STF
L-LTF
L-SIG
HT-
STF
HT-SIG
HT-
LTF
8us
8us
4us
8us
4us
4us
ACK
Data frame
ACK frame
DIFS
CW
ACK frame
Next frame
36us
36us
16us
34us
Ave. CW (us) = Cwmin * slot time /2 = 15*9/2 = 64.5
Data length (us) = roundup((service + MAC header + LCP header +
Data(1500B) + FCS + tail)/OFDM symbol)*4
ACK length (us) = roundup((service + ACK + FCS + tail)/OFDM symbol)*4