## Slide 1: DSRC PER versus RSS Profiles
Date: Nov. 8, 2013
Authors:
Brian Gallagher (Denso DIAM ), John Kenney (Toyota ITC)

## Slide 2
DSRC PER versus RSS Profiles
Line-of-Sight Vehicle-to-Vehicle Tests
Borrego Springs, CA
September 13, 2013

## Slide 3: Purpose & Outline
Purpose
  Develop Packet Error Rate (PER) versus Receive Signal Strength (RSS) profiles from vehicle-to-vehicle (V2V) line-of-sight (LOS) tests
  Use prototype DSRC radios from two radio suppliers
Outline
  Test Setup
  Test Environment
  PER and RSS Metrics
  PER versus RSS Scatter Plots
Brian Gallagher (Denso DIAM ), John Kenney (Toyota ITC)

## Slide 4: Test Setup
V2V tests performed on an open road
    September 13, 2013
    In Borrego Springs, CA
  1 mobile receiving (RX) vehicle
    Supplier 1 receiver
    Supplier 2 receiver
    Both receiving on 10 MHz channel 172
  1 static transmitting (TX) vehicle
    Reference transmitter
    Radio from supplier 1
    10 MHz Channel 172
  Rooftop antennas
    5.9 GHz DSRC band
    Omnidirectional
    Magnet-mount
Open road test site
TX
CAR
RX
CAR
ZOOM VIEW: RX CAR
Brian Gallagher (Denso DIAM ), John Kenney (Toyota ITC)

## Slide 5: Test Environment
The RX vehicle
  Moves outbound & inbound, away from and towards the TX vehicle
  Travels at speeds approximately 35 to 40 mph
The environment was line-of-sight throughout drive range
  No obstructions between the TX and RX vehicles
Henderson Canyon Road in Borrego Springs, CA
Number of passes: 6 total (3 outbound, 3 inbound)
Brian Gallagher (Denso DIAM ), John Kenney (Toyota ITC)

## Slide 6: PER and RSS Metrics
PER
  TX vehicle: Broadcasts ~1380 packets per second
    Each packet includes a sequence number
    PLCP length ~400 bytes
  RX vehicle: Calculates PER every 100 ms
    Calculated over ~138 incoming packets
    Calculated based solely on the sequence numbers
    Calculated independently on each supplier’s radio
RSS
  RX vehicle: RSS is recorded from the last packet received in each 100 ms epoch
Receive Logs
  Captured on each supplier’s radio hardware
  Updated every 100 ms
  Contains: Calculated PER and Recorded RSS
Brian Gallagher (Denso DIAM ), John Kenney (Toyota ITC)

## Slide 7
  PER versus RSS Scatter Plot: Supplier 1

## Slide 8
  PER versus RSS Scatter Plot: Supplier 2