## Slide 1: Summary and Discussions of Proposals on Potential PHY Technologies in HEW
Date: 2013-10-31
Authors:

## Slide 2: Motivations
The focus of HEW study group includes “Improving spectrum efficiency”
  Besides MAC enhancement, we probably also need consider improvements from PHY layer.
  PHY enhancement is proven helpful on user experience and CE market expansion
A dozen of proposals on potential PHY technologies have been presented in HEW study group
  To summarize and organize the proposed PHY technologies
  To initiate discussions on feasibility, performance gain and complexity of proposed PHY technologies
  To identify promising PHY technologies for HEW and help quantify the performance enhancement target of the PAR

## Slide 3: Proposals of PHY Technology in HEW and 11AC
In-Band Full duplex: [1] [2] [3]
Further exploit beam-forming: [4] [5] [6]
Sub-channel based OFDMA [7] [8]
Co-operative Transmissions [9] [10]
PHY Changes for Outdoor Applications [11][12][13]
Others [14] [15]

## Slide 4: In Band Full Duplex
[1] and [2] introduced the latest progress from academia on full duplex technology
  Full-duplex Technology using cancellation yield some good results
    Antenna-level cancellation: 25 to 40 dB;
    RF/IF/analog: 20 to 30 dB;
    Digital baseband: 20 to 30 dB
[3] suggested some MAC protocols based on in-band Full Duplex Technologies

## Slide 5: Discussions of In-Band Full Duplex
Pros
  Double spectral efficiency
  Easy fix of hidden node problem
Challenges:
  Feasibility
    Antenna level cancellation and RF-IF analog cancellation rely on the known phase of Tx signal
      Local scattered Tx signals have random phases
      Local scattered Tx signals can still be 90-100dB stronger than RX signal
  Concerns on Cost of digital baseband cancellation
    Current 11ac design requires 10-bits ADC
    30dB cancellation needs extra 5-bits for ADC.
    15-bits high speed ADC is very expensive and baseband processing of 15-bits input is also costly.

## Slide 6: Further Exploits of Beam-forming
[4] discussed potential beam-forming enhancement ideas with the following benefits:
  increase likelihood of channel access under dense deployment condition
  reduce interference to OBSS
  reduce collision during reception
  increase likelihood of spatial re-use in dense deployment scenario, leading to higher network throughput
[5] evaluated the performance benefits of TxBF under OBSS environment
  Tx BF shows great performance gain against CCI/collisions
  Suggestions
    Make TxBF a mandatory baseline feature for HEW AP;
    Consider TxBF and RxBF enhancement on interference mitigation, even AP coordinated BF
[6] showed that UL MU-MIMO offers significant network throughput advantages over SU-MIMO.

## Slide 7: Discussions on Further Exploits of Beam-forming
Pros
  Beam-forming is an proven useful technology in 802.11n/ac
  Sector/beam-forming mitigate interferences (within BSS or OBSS)
  UL MU-MIMO: improves uplink throughput
Concerns
  Tx Beam-forming preamble may cause CCA mechanism failure
  AP with sector antenna (sectored BSS): How a non-AP STA transmits in a sectored BSS?
  UL MU-MIMO:
    Synchronization among STAs
    Power control is required

## Slide 8: Sub-channel Based OFDMA
[7] discussed OFDMA as a potential technique
  Frequency reuse to alleviate OBSS problem
  OFDMA with 11ac channelization for back compatibility
    20 MHz would be the smallest resource unit
Similar ideas have been proposed in [8] in 11ac
  [8] showed significant throughput improvement of a BSS composed of mixed clients (11a/n and 11ac)
  Downlink OFDMA only without extra requirement on STA Synchronization
Discussions
  Uplink OFDMA requires Synchronization and power control
  How much frequency selectivity gain by using Sub-channel OFDMA?

## Slide 9: Co-operative Transmissions
[9] discussed the feasibility of using coordinated transmission between adjacent APs
  CoMP has been adopted in LTE
  Suggestions: Coordinated power allocation, Coordinated frequency band allocation, Joint Transmission based one joint pre-coding
[10] proposed a two-way coding joint design of pre-coder and decoder to improve the network flexibility and channel efficiency

## Slide 10: Discussions on Co-operative Transmission
Pros
  AP/STA coordination could enhance the network throughput and efficiency
  Many kinds of coordination schemes with different complexity and gains
Questions and Concerns
  What kind of coordination should be considered?
  How much enhancement we can expect from co-operative transmission?
  Two-WAY coding scheme [10]:
    Phase 1 requires synchronization of STAs
    Only useful when two STA needs to exchange information

## Slide 11: PHY Changes for Outdoor Applications
[11] and [12] showed performance loss under UMa channel models due to the long delay spread. It suggests that CP of 802.11n/ac needs be enlarged.
[13] considered the back compatibility with legacy devices if longer CP is used.
  Proposed solution is to keep legacy preamble part and redesign the new part.

## Slide 12: Discussions on PHY Changes for Outdoor Applications
Pros
  Better support long range outdoor applications
Questions
  Current consensus is to guarantee performance under UMi channel model.
    Do we need to change CP length even in UMi channel models?
  If performance degradation is allowed under UMa channel, how much degradation is acceptable? How large we want outdoor HEW BSS be?
Concerns of Long GI
  Causes mid-packet detection failure for 11ac devices
  Reduces network efficiency
    For a BSS with mixed STAs, at least beacon may need transmitted using long GI.

## Slide 13: Other Proposals
[14] showed that HARQ can provide significant gains in throughput in low SNR conditions and therefore can improve BSS edge data rates
  Pro
    3dB gain in low SNR case
  Concerns
    Packet-based HARQ requires large buffer to store LLRs of whole packet
[15] suggested massive MIMO as a potential technology
  Concerns
    Cost and complexity of using massive MIMO need to be considered
    Necessary of Massive MIMO?

## Slide 14: Summary
We categorized PHY technology proposals and briefly discussed pros, concerns and challenges of proposed PHY technology.
The goal is to identify promising PHY technologies
  Maybe multiple promising technologies and/or a combination of multiple promising technologies
  Helps to quantify the PHY enhancement in the PAR
This contribution is to stir discussions on potential PHY technologies
  Your feedback or contributions on this topic is very welcome!

## Slide 15: Reference
[1] IEEE 802.11-13/0764r1, “Full-duplex Technology for HEW”, André Bourdoux, etc.
[2] IEEE 802.11-13/0765r1, “Co-time Co-frequency Full Duplex for 802.11 WLAN”, Hongliang Bian, etc.
[3] IEEE 802.11-13/1122r1, “Considerations for In-Band Simultaneous Transmit and Receive (STR) feature in HEW”, Rakesh Taori, etc.
[4] IEEE 802.11-13/0877r1, “HEW Beamforming Enhancements”, James Wang, etc.
[5] IEEE 802.11-13/1126r0, “Beamforming Under OBSS Interference”, Hongyuan Zhang, etc.
[6] IEEE 802.11-09/0852, “UL MU-MIMO for 11ac”, Richard Van Nee, etc.
[7] IEEE 802.11-13/0871r0, “Discussion on Potential Techniques for HEW”, Timo Koskela, etc.
[8] IEEE 802.11-10/0317r1, “DL-OFDMA for Mixed Clients”, Brian Hart, etc.
[9] IEEE 802.11-13/1157r3, “Feasibility of Coordinated Transmission for HEW”, Yunzhou Li, etc.
[10] IEEE 802.11-13/0630, “Two-Way Coding by Beam-Forming for 802.11 WLAN”, Zhigang Wen, etc.
[11] IEEE 802.11-13/0536r0, “HEW SG PHY Considerations For Outdoor Environment”, Wookbong Lee, etc.
[12] IEEE 802.11-13/0843r0, “Further evaluation on outdoor Wi-Fi ”, Wookbong Lee, etc.
[13] IEEE 802.11-13/1057r0, “Legacy Support on HEW frame structure”, Jinyoung Chun, etc.
[14] IEEE 802.11-13/0852, “Potential approach to improve WLAN BSS edge performance”, Juho Pirskanen, etc.
[15] IEEE 802.11-13/1046r2, “Discussion on Massive MIMO for HEW”, Zhanji Wu, etc.