## Slide 1: Discussions on Penetration Loss
Date: 2013-11-02
Authors:

## Slide 2: Introduction
Penetration Loss should be considered on almost all the simulation scenarios presented in [1]
  For residential scenario, wall/floor penetration happens
  For Enterprise Scenario, cubic wall penetration happens
  For outdoor scenario, building/house wall penetration happens
Penetration loss is different for different materials and for different frequencies

## Slide 4: Outdoor-to-Indoor and indoor-to-outdoor Penetration Loss
  Measurements and Information:
    In [2], it is shown that the measured penetration loss are
      Brick exterior wall: 14.5dB
    In [3], LTE-advanced simulation setup uses fixed penetration the loss as 20dB
    In ITU [4], Baseline evaluation configuration parameter for Macro suburban uses the fixed penetration loss as 20dB
    In [7], 20dB at 5GHz exterior wall/floor penetration loss is suggested.

## Slide 5: Indoor Wall Penetration Loss
Indoor walls
  For residential indoor wall penetration
  For Enterprise cubic wall penetration
Our measurements at 2.4GHz
Office
Room
A
B
C
D
E
35[m]
Tx
>21dB
<21dB
>12dB
~12dB
<12dB
>7dB
<7dB
23dB
17dB
12dB
7dB
3dB
Average SNR
Range of SNR

## Slide 6: Measurement in WFA [5]
In US, sheertrock/wood frame wall are generally used in famly houses.
In EU and China, Brick wall is more popular.

## Slide 7: Indoor Wall Penetration Loss (cont’s)
Base on our measurements, we saw averagely <5dB indoor wall penetration loss.
  We did not count the path loss in our measurement.
In [2], the measured penetration loss of interior wall is 4.7dB
In [5], for different walls, it is between 3 to 6dB.
Other literatures show that 5GHz has <0.5dB more penetration loss than 2.4GHz.

## Slide 8: Floor Penetration Loss
In [6], a floor penetration loss is measured in 1.8GHz and shows that roughly 18dB for the first floor.
We probably need find more measurements to finalize the floor penetration loss.

## Slide 9: How to Model the Penetration Loss?
ITU channel model the penetration by a random variable with a std
  Walls/floor are built with different materials and with different thickness.
Other simulation setups use fixed parameters for penetration loss
  Maybe simpler for network simulations
More discussion probably is required.

## Slide 10: References
“HEW SG Simulation Scenarios”, IEEE 802.11-13/1001r3, Simone Merlin, etc.
“5.85-GHz Radio Path Loss and Penetration Loss Measurements In and Around Homes and Trees”, IEEE COMMUNICATIONS LETTERS, VOL. 2, NO. 3, MARCH 1998.
“Comparison of LTE Advanced HetNets and Wi-Fi”, Qualcomm
“ETSI TR 136 931 V9.0.0 (2011-05)”
” Introduction to Indoor Propagation and Video Range Testing”, WFA 2007, Graham Smith. https://groups.wi-fi.org/apps/org/workgroup/videomarketing/documents.php
“Channel models for D2D performance evaluation “, 3GPP TSG-RAN WG1 #72bis, R1-131620
“HEW Simulation Methodology”, IEEE 802.11-13/1081r0, Sayanta Choudhury, etc.