## Slide 1: Outdoor Channel Model Simulation Follow-up
Date: 2013-11-11
Authors:
Name | Affiliations | Address | Phone | email
Hongyuan Zhang | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-1837 | hongyuan@marvell.com
Mingguang Xu | Marvell Semiconductor |  |  | 
Yan Zhang | Marvell Semiconductor |  |  | 
Hui-Ling Lou | Marvell Semiconductor |  |  | 
Yakun Sun | Marvell Semiconductor |  |  | 
Sudhir Srinivasa | Marvell Semiconductor |  |  | 
Bo Sun | ZTE Corporation |  |  | sun.bo1@zte.com.cn

## Slide 2: Introduction
In [2], outdoor channel model was discussed and the consensus was to guarantee that HEW works well with UMi channel, and still works under UMa (connection is supported but reduced performance is possible).
  Use ITU model.
In [1] we simulated UMi channels using SCM modeling, comments received include
  Should use ITU mode instead of SCM, and compare the two models.
  Also check UMa using ITU model
Here we follow-up the discussions with updated link-level simulation results using ITU model.

## Slide 3: Link Level Simulations for ITU Models
Use ITU UMi-NLOS and UMi-LOS channel models as defined in [3].
  Channel snapshots are independent, with bulk-normalization.
  For LOS, K factor is log-normal distributed using ITU model parameters
    Approx. 9 dB mean.
Also tried ITU UMa channels.
11ac 20MHz, 1x1, MCS 0, 2, 4, 7 representing BPSK, QPSK, 16QAM and 64QAM, try different channels.
  No RF impairments, perfect sync, actual CE.
All assuming normal GI (0.8us).

## Slide 4: Power Delay Profiles for Different Channels—UMi
Averaged over 1000 independent channel snapshots

## Slide 5: PER Results for ITU-UMi vs D-NLOS

## Slide 6: Power Delay Profiles for Different Channels—UMa
Averaged over 1000 independent channel snapshots

## Slide 7: PER Results for ITU-UMa vs D-NLOS

## Slide 8: Results Discussions
Comparing ITU-UMi results with SCM-UMi results in [1]:
  NLOS results are slightly worse, but generally in-line
  LOS results are better
  If using 10% PER as criteria: NLOS can sustain up to MCS2, LOS can sustain up to MCS7.
ITU-UMa results:
  NLOS can only sustain MCS0.
  LOS may get some middle range MCS (MCS2 or 3)

## Slide 9: About the Outdoor Model Criteria in [2]
“HEW design shall ensure that Wi-Fi works well under UMi”
  Question-1: should we quantify what “works well” mean (e.g. PER can reach 10% with TBD PHY & Simulation parameters)?
  Question-2: should we introduce the concept of LOS probability in link-level simulations, and different LOS-probability for different MCSs?
“HEW design should ensure that Wi-Fi still works under UMa (connection is supported but reduced performance is possible)”
  Question-1: should we quantify at what performance level we may claim that “connection is supported”?

## Slide 10: References
[1] 11-13-1125-03-0hew-outdoor-channel-model-discussions, Hongyuan Zhang, et. al.
[2] 11-13-1135-04-0hew-summary-on-hew-channel-models, Jianhan Liu, et. al.
[3] Report ITU-R M.2135-1 (12/2009) Guidelines for evaluation of radio interface technologies for IMT Advanced