## Slide 1: Discussion on OFDMA in HEW
Date: 2013-11-11
Authors:

## Slide 2: Abstract
This contribution discusses on OFDMA in HEW

## Slide 3: Motivation
11ac introduced 80/160MHz wider bandwidth operation, but, it is difficult to get a real benefit due to [1][2]
  Commonly used secondary channels in neighbor BSSs
  Restriction on non-continuous (with primary) channel assignment
    DL MU-MIMO can achieve higher throughput by multiplexing packets in space domain, but, flexible multiplexing capability is getting important in high dense environment
  Multiplexing capability in space domain can be extended to others, e.g. frequency domain
We consider OFDMA to maximize resource utilization in wider bandwidth and to maximize multiplexing flexibility

## Slide 4: A potential technique: OFDMA
Goal
  Enhancement on channel utilization efficiency through assigning multi-channels to multi-users
OFDMA can enable following features
  Alleviating high dense condition by
    Concurrent channel access from multiple users
    Increase flexibility of channel utilization
  Compatibility with other enhancing technologies, e.g. frequency reuse
Main differences from legacy channel utilization
  Multiple users can access to medium in multi-channels within a TXOP
  In wider bandwidth operation, non-contiguous channels can be used within a given FFT size

## Slide 5: How can channel utilization be enhanced by OFDMA?
STA1
STA2
STA3
STA1
Target BSS
OBSS
OBSS
Target BSS
Hearable interfering source
OFDMA
Legacy operation
Wasted channels,
even idle
Can assign available channels to users (or a user)
FFT
FFT
Channel efficiency analysis was shown in [1]

## Slide 6: Discussion: OFDMA link
Issue on DL-only OFDMA and feasibility of UL
DL
  AP can manage packets for users and transmit them simultaneously
    It’s like extending stream-domain in DL MU-MIMO to channel-domain for transmitting multiple packets
  It would be good to protect TXOP duration for OFDMA transmission from legacy devices (or from UL packet in DL-only OFDMA case)
UL
  Both time-synchronization and clear channel access for packets need to be satisfied
    It is difficult to expect when users prepare packets and want to transmit them
    Channel states couldn’t be easily guaranteed, even packets are prepared
  Need further discussion (on solutions and its feasibility)

## Slide 7: Discussion: Activity on primary channel
Issue on how to activate EDCA TXOP, backoff, and NAV assertion
Up to 11ac
  Solely based on activity in the primary channel
  Extension to adjacent secondary channels for wider bandwidth operation; a backoff mechanism on the primary channel
HEW with (DL) OFDMA
  Option by maintaining primary channel based access
    It can enable simple implementation to have a reference channel in a system
      One backoff mechanism in the primary channel would be fine; primary channel needs to be guaranteed and assigned first
  Option by preferred channel based access
    No critical gain with band selection would be expected if subband granularity is sufficiently large (e.g. 20MHz); Need further discussion

## Slide 8: Discussion: Scheduling
Issue on scheduling for OFDMA
OFDMA with basic Wi-Fi architecture and further extension to scheduling
  In DL, AP could manage packet transmission without critical scheduling overhead, e.g.,
    Set a TXOP for OFDMA transmission (RTS/CTS, etc)
    Let the OFDMA packet composition depend on each channel state; Non-continuous channels within FFT size can be used if idle
  Scheduling may be required for some enhanced features/functionalities: but need to consider overhead increase
    E.g. In DL MU-MIMO, the management frames to set up multi-packet Tx can be a burden on degrading MU-MIMO gain

## Slide 9: Discussion: Granularity of subband
Issues | Pros | Cons
User multiplexing capability | - Alleviating high-dense condition by finer user multiplexing in frequency - Performance enhancement even in 20MHz-only channel condition (practically higher BW size wouldn’t be easily guaranteed) | Burden on signaling overhead; without band scheduling, it is difficult to expect significant gain
Overhead for short packet | - Padding overhead may be relatively small; depending on traffics - Packing gain may be too small in current FFT size (64 for 20MHz, which is quite smaller than cellular system)*; depending on FFT size | N/A
CCA complexity /overhead | N/A | Probably higher with various CCA BW granularity; depending on PPDU design and CCA rule
Impact on Frame structure | Possibility of more optimized frame structure for HEW | Burden on new design from implementation point of view
Baseline: 20MHz subband for easy extension to OFDMA
<Analysis when using subband less than 20MHz >
e.g. TCP ACK: ~100bits, VoIP packet with AMR 12.2kbps: ~360bits

## Slide 10: Conclusion
We discussed some feasibilities of OFDMA as one of candidate techniques to enhance efficiency in HEW
Our observation shows followings are feasibly recommended
  DL-OFDMA
  Primary channel based access (base-line), preferred channel based access (FFS)
  Minimize scheduling overhead
  Subband granularity: 20MHz (base-line), smaller subband (FFS)
Need to discuss further on following issues
  Feasibility on
    UL-OFDMA
    Preferred channel based access
    Subband granularity smaller than 20MHz
    Etc.
  System-level performance verification based on established evaluation methodology

## Slide 11: Reference
[1] 13/1058 “Efficient Wider Bandwidth Operation”, Suwook Kim (LG Electronics)
[2] 13/0871 “Discussion on Potential Techniques for HEW”, Timo Koskela (Renesas Mobile Corporation)