## Slide 1: Discussion on HEW PAR
Date: 2013-11-11
Authors:

## Slide 2: Introduction
Main contents of PAR (Project Authorization Request) are divided into two parts:
  Scope
    which captures key requirement(s)
  Additional Explanatory Notes
    which complements PAR scope
This contribution suggests a scope of HEW PAR and proposes to provide guidance on HEW design in additional explanatory notes

## Slide 3: What to describe in ‘scope’?
There has been discussion on key requirement(s)
  System perspective requirement such as Area Throughput [1] [3]
  User perspective requirement such as Average User Throughput and 5-th percentile user throughput [2] [3]
We agree to capture enhancement in both system-perspective and user-perspective in scope of HEW PAR
Since the PAR scope in Orange’s contribution [4] has captured both perspectives well, we don’t touch PAR scope in this contribution

## Slide 4: What to describe in ‘Additional Explanatory Notes’? - Guidance on HEW design
11ac has clearly described PAR
  What to improve (i.e., maximum single link throughput and maximum multi-STA throughput)
  How much improved (i.e., 1 Gbps for multi-STA) in PAR scope
  How to improve (i.e., MU-MIMO)
    “The project may include the capability to handle multiple simultaneous communications.” in PAR Additional Explanatory Notes
However in HEW,
  What to improve: based on discussion so far, probable to generally describe about system and user throughput enhancement
  How much improved: very difficult to describe since we don’t have reference performance values
  How to improve: so unclear compared to 11ac.

## Slide 5: What to describe in ‘Additional Explanatory Notes’? - Guidance on HEW design
We propose to add guidance on HEW design in additional explanatory notes

## Slide 6: What to describe in ‘Additional Explanatory Notes’? - Guidance on HEW design
Why?
  To provide some flavors on HEW technical directions
  To complement general HEW PAR scope
What?
  Fundamental technology on which HEW system design can be built up
  Mainstream technology which members highly agree to consider
We propose to include one fundamental and mainstream high-level technology direction (which may implicitly include several technologies) here to clarify potential technical directions.

## Slide 7: Proposal on Additional Explanatory Notes - Guidance on HEW design
The project may add and enhance the capability to handle multiple simultaneous communications in both the spatial and frequency domains, in both the UL and DL, and across multiple BSS.

## Slide 8: Straw Poll #1
Do you support to include the guidance on HEW design propsal in slide 7 in Additional Explanatory Notes of HEW PAR as the baseline?
  Yes
  No
  Abstain

## Slide 9: Reference
[1] 11-13/1097r0 “Functional Requirements for HEW PAR”
[2] 11-13/1116r0 “Discussion on HEW Functional Requirements”
[3] 11-13/1137r2 “The Definition of Performance Metrics for HEW”
[4] 11-13/1366r2 “Some propositions to progress towards the PAR definition”