## Slide 1: Frame Formats for PAM
Date: 2013-11-12
Authors:

## Slide 2: Abstract
This presentation suggests frame formats for PAM(Pre-Association Message) to announce the service information by broadcasting or multicasting before association. The frame formats are provided to discuss to be included in the specification framework.

## Slide 3: Format for PAM Frame
Element name | Size (octet) | Description
PAM revision number | 1 | Increase if any service information is revised.
PAM interval | 1 | Interval for PAM multicasting/broadcasting in a certain unit time.
Service Information 1 | variable | Service information for a service
Service Information … | Variable | Service information for a service
Service Information n | variable | Service information for a service

## Slide 4: Format for Service Information
Sub-element name | Size (octet) | Description
SDP ID | 1 | Service Discovery Protocol ID (e.g. 1 for Bonjour, 2 for UPnP, 3 for Web Service Discovery, and …)
SID | 6 | Service Identifier (hash value of a service identifier)
Subtype (optional) | Variable | Subtype string (e.g. TXT record of Bonjour)
Service Info. Data (optional) | Variable | Upper layer data
Description (optional) | Variable | Human readable description of the service
Channel ID (optional) | 1 | The channel in which the service is available if this element is present. It denotes the band and the frequency. If it is not present, the service available in the same channel.
BSSID (optional) | 4 | BSSID which the service is available if it is present. If it is not present, the service available in the same channel.

## Slide 5: Straw Poll : Format for PAM frame
Do you agree that the specification framework shall include frame formats for multicasting or broadcasting frame to announce service information?
  Yes
  No
  Abstain