## Slide 1: Renewing 2.4 GHz
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco | +1 408 5253346 | brianh@cisco.com

## Slide 2: Summary
  Problem
    2.4 GHz is regarded as a junk band
    Too much traffic, too many Bluetooth devices / Zigbee devices
    Detailed analysis shows considerable medium time consumption due to mgmt frames (Probe Req/Rep, Beacons sent at 1 Mbps) and control frames (RTS/CTS, CTS2self sent at 1 Mbps) and collisions
  Solution
    Reduce usage of DSSS/CCK rates
    Reduce usage of non-1/6/11/14 channels
    Port narrowband 11ac features (256QAM, VHT sounding, MU-MIMO, 8SS) to 2.4 GHz
  Summary
    Ensure that the HEW scope supports these directions

## Slide 3: Problem: 2.4 GHz is regarded as a junk band
  Spectrum is not like a fishery – it doesn’t get fished out. Spectrum renews itself at every moment at every location.
  Detailed analysis shows considerable medium time consumption due to mgmt frames (Probe Req/Rep, Beacons sent at 1 Mbps) and control frames (RTS/CTS, CTS2self sent at 1 Mbps)
    KDDI 13/758, 7Signal 13/545, etc
  How can we can minimize this traffic, in order to renew 2.4 GHz?

## Slide 4: Solution: Minimize Mgmt Traffic Overheads (1/2)
  Recommendation 1: HEW STAs transmit Beacons, Probe Requests and Probe Responses at OFDM rates
    With two exceptions:
      A HEW AP may respond at DSSS/CCK rates to a probe request that indicates that DSSS/CCK are the only supported rates
      A HEW client may actively scan at DSSS/CCK rates only after actively scanning at OFDM rates when a) no APs respond or b) the APs that respond include the Use_Protection field in the ERP element equal to 1 (i.e. DSSS/CCK-only AP or STA is nearby)
    Recommendation 1 should lead to a 6-fold reduction in mgmt traffic
    Side-effect: DSSS/CCK-only passive-scanning-only clients cannot detect HEW APs. However, there are very few DSSS/CCK-only passive-scanning-only clients, getting fewer, and many existing APs have been more aggressive than this for many years (disallowing DSSS/CCK-only clients from associating) so any impact is expected to be slight. HEW and 11ai efforts to discourage DSSS/CCK rates can complement efforts at WFA

## Slide 5: Solution: Minimize Ctrl Traffic Overheads
  Recommendation 2: Unless Use_Protection is set, HEW STAs transmit MAC protection at OFDM rates
    Recommendation 2 should lead to a 6-fold reduction in MAC protection traffic
    NOTE: a DSSS/CCK PPDU has the property that, if transmitted on channel n, the PPDU is oftentimes correctly received on channel n+-1, n+-2 etc.
    Side-effect: an OFDM control frame sent on channel n+-1 (e.g. ch7) does not cause virtual carrier sense to be set on a STA on channel n (e.g. ch6). This in turn implies that HEW APs select non-overlapping channels (and other APs should be encouraged by WFA to do the same)

## Slide 6: Solution: Minimize Mgmt Traffic Overheads (2a/2)
  Recommendation 3: Allowed channels for HEW APs are limited to channels 1, 6, 11 and 14 (and WFA should encourage all APs to follow this convention)
    Recommendation 3 allows more reliable virtual carrier sense in an OFDM-dominated world.
    Over time, Recommendation 3 also leads towards a further 3-5x reduction in probing traffic. This is because today we see clients sending a probe request on ch1, then ch2, then ch3 (all the while consuming medium time on ch1), then ch4/5/6/7/8 (all the while consuming medium time on ch6), etc. As clients see fewer and fewer APs on channels 2-5, 7-10, they can cycle through channels 1/6/11/(14) more and more times relative to the number of times that they cycle through the other channels
    Seen today (US): 1 2 3 4 5 6 7 8 9 10 11 / repeat
    Proposed for near future (US): 1 6 11 / 1 6 11 / 1 6 11 / 1 6 11 / 1 2 3 4 5 6 7 8 9 10 11 / repeat
    Proposed for far future (US) 1 6 11 / repeat

## Slide 7: Solution: Minimize Mgmt Traffic Overheads (2b/2)
  Constraining the allowed channels at 2.4 GHz will be a challenge for the industry:
    the benefits take time to accrue
    vendors differentiate themselves by their channel selection algorithms, and greatest differentiation comes from greatest freedom
    some countries can use 1/5/9/13 (although 1/6/11 is very common and getting more common due to the selection by Wi-Fi Direct for 1/6/11 to be the social channels)
  But, the calculus is changing: a) MAC protection with OFDM PPDUs doesn’t work in partially overlapped channels, b) non-overlapped channels significantly reduce painful probing overhead, c) Zigbee, AFH Bluetooth Classic and BLE are not going away, and they benefit from consistent Wi-Fi gaps (e.g. BLE advertising channels avoid OFDM at 1/6/11), d) Wi-Fi Direct settled on 1/6/11 as the social channels
  The world will be better off if Wi-Fi allows channels 2-5, 7-10, and 12-13 to fall into disuse. IEEE HEW and 11ai efforts can complement activities at WFA.

## Slide 8: 802.11ac does not support 2.4 GHz, but not always for good technical reasons
  Many 11ac techniques are valuable even when confined to 20 MHz operation:
    256 QAM
    VHT sounding
    MU-MIMO
    8SS
  These features can easily be adopted at 2.4 GHz by existing dual-band 11n/11ac devices (no baseband HW changes, minimal RF changes)
  802.11ac features can be deployed in a vendor specific manner at 2.4 GHz today of course, but we should ultimately offer IEEE-compliant, WFA-certified products to users.

## Slide 9: Suggested PAR Scope Language
  “including peak throughput* and efficiency+ improvements for 2.4 GHz”
  “HEW is permitted to provide reduced& interoperability with DSSS/CCK-only devices”
  *i.e. 256QAM, 8SS, VHT sounding
  +i.e. Mgmt and MAC protection frames at OFDM rates, non-overlapping channels, MU-MIMO, VHT sounding
  &e.g. no connectivity for DSSS/CCK-only passive-scanning-only clients

## Slide 10: Summary
  Ensure the PAR&5C allows HEW, in conjunction with 11ai and WFA, to
    Discourage use of DSSS/CCK for mgmt frames (6x less overhead)
    Discourage use of DSSS/CCK for ctrl frames (6x less overhead)
    Limit HW AP channels to 1/6/11/(14) (effective virtual carrier sense; enables 3-5x less overhead over time)
  Ensure the PAR&5C allows HEW to
    Port narrowband 11ac features to 2.4 GHz such as 256QAM, VHT sounding, MU-MIMO, 8SS
  Let the renewal of 2.4 GHz begin!