## Slide 1: Traffic Modeling for HEW Simulation
Date: 2013-11-12
Authors:

## Slide 2: Motivation
HEW group tries to improve performance such as efficiency and QOE for the real world scenario
Traffic modeling becomes very important to simulate the real use scenarios
Huai-Rong Shao, et.al. (Samsung)

## Slide 3: Traffic Modeling Framework
Two levels for simulation:
  Level one
    Application Traffic Modeling [2,3]
      Specify the traffic characteristics of an application
      E.g., Local file transfer, HTTP web browsing, Lightly Compressed video, Online gaming, etc.
  Level two
    STA Application Profiles [4]
      Mixing of applications at STAs
      E.g., STA 1 has a profile of video streaming + web browsing, and STA 2 has a profile of video conferencing + ftp
    Profile Configuration (Addressed by this presentation)
      Pattern of the application events, i.e., when to start the applications in the simulation and how long for each application
      E.g., for a STA, video streaming application starts at time 0 and web browsing starts at time 8

## Slide 4: Example 1: TCP Traffic Configuration
TCP configuration for file transfer [2]
Widely used by different simulators
TCP Configuration Parameters in Simulators | 
MSS | Ethernet (1500 bytes)
Receive Buffer (Bytes) | 65535
Receive Buffer Adjustment | None
Delayed ACK Mechanism | Segment/Clock based
Max. ACK Delay (Sec) | 0.05
Slow Start Initial Count (MSS) | 1
Fast Retransmit | Enabled
Duplicate ACK Threshold | 3
Fast Recovery | Reno
Window Scaling | Enabled
Selective ACK (SACK) | Disabled
ECN Capability | Disabled
Segment Send Threshold | Byte Boundary
Active Connection Threshold | Unlimited
Karn’s Algorithm | Enabled
Nagle Algorithm | Disabled
Initial Sequence Number | Auto Complete
Initial RTO (sec) | 3.0
Min RTO (sec) | 1.0
Max RTO (sec) | 64
RTT Gain | 0.125
Deviation Gain | 0.25
RTT Deviation Coefficient | 4.0
Timer Granularity | 0.25

## Slide 5: Example 2: HTTP Traffic Modeling
The parameters of HTTP file transfer in [2]:
  SM: Size of main object in page
  Nd: Number of embedded objects in a page
  SE: Size of an embedded object in page
  Dpc: Reading time
  Tp: Parsing time for the main page
The table on the right highlights the components and their distributions
  Approximate mean data rate of (10KB+48KB)/31 = 12.31 kbps

## Slide 6: Modeling for Various Video Traffic Types
[3] provides models for
  Wireless Display: lightly compressed video
  Buffered video streaming
  Video conferencing
Details discussed during this week

## Slide 7: Application Event Modeling
How to simulate the event timing of individual application traffic for all STAs to simulate real world scenario
  When to generate which traffic types
  Duration of the applications, etc.
Different use scenarios may need different application event models
  Classroom, Home, Railway station, Stadium, etc.
  Some may completely random and some may have peak patterns

## Slide 8: Application Event Patterns
Most popular pattern is Random pattern
  A Random pattern occurs where there are many users, each generating a little bit of traffic and requesting network access randomly
  Currently Poisson model is widely used
    VoIP calls from Cisco measurement [5]
    User accesses to Web Pages [6]
The second pattern is Peaked pattern
  A peaked pattern has big spikes from the mean
    Some use scenarios like training arrival, class starting may go to this pattern
  Hyper-exponential model can be used
    VoIP calls from Cisco measurement [5]
Time
Application requests
Application requests
Time
Time

## Slide 9: Summary
HEW simulation needs both application traffic models and application profiling/configuration models
  We have various applications traffic models [2,3] proposed
    More traffic types may be added in the future
  Application profiling/configuration
    Based on [4], add application event models
Propose to add application event models to Simulation Scenario document (802.11-13/1001)
    Poisson model and Hyper-exponential model

## Slide 10: Reference
[1] “HEW SG Simulation Scenarios”, IEEE 802.11-13/1001r4, Simone Merlin, etc.
[2] “Internet Traffic Modeling”, IEEE 802.11-09/1317r1, Sai Nandagopalan, etc.
[3] “Video Traffic Modeling”, IEEE 802.11-13/1305r0, Guoqing Li, etc.
[4] “Simplification of HEW Traffic Model Simulations”, IEEE 802.11-13/0847r1, William Carney, etc.
[5] “Traffic Analysis for Voice over IP”, http://www.cisco.com/en/US/docs/ios/solutions_docs/voip_solutions/TA_ISD.html#wp1030552
[6] “A Poisson Model for User Accesses to Web Pages”, Computer and Information Sciences -- ISCIS 2003, Sule Gunduz, etc.
Huai-Rong Shao, et.al. (Samsung)

## Slide 11
Thank you!