## Slide 1: HEW Considerations for the Vehicular Environment
Date: 2013-11-11
Authors:

## Slide 2: Abstract
WiFi is a widely available communication method
In recent years WiFi is being incorporated in vehicles both as an AP for customer’s internet access purposes and as a data bearing method for the vehicle’s infotainment systems
The use of WiFi in vehicles is constantly growing and the usage growth rate will increase as WiFi will gradually assume more roles in the vehicle’s communication portfolio
The automotive environment is different in some aspect from the standard environment in which WiFi usually operates, hence these aspects must be addressed in parallel to WiFi’s increasing usage in vehicles

## Slide 3: Mobility Support
Mobility support for HEW has been discussed in previous submissions [1]
Vehicle to infrastructure and vehicle to vehicle communication are rapidly growing areas in the automotive world
Mobility support can be divided into two cases:
  Low / medium mobility: speed < 50 km/h Some Examples:
    Dense urban city driving
    Vehicles heading towards each other with a speed of 25 km/h
    Vehicle to pedestrian communication
  High mobility: speed < 200 km/h
    Open road driving
    Vehicles heading towards each other with speed of 100 km/h

## Slide 4: Vehicle Channel Model
In-car channel model:
  In-car communication has been presented as a use case
  This use case assumes [1]:
    Devices in a car are operating in close proximity (typical distances between STAs and AP are < 5m)
    Transmissions are mostly LOS.
    There might be interferences from the neighbor cars.
  We need to further assume the following environment restrictions affecting the communication:
    Large metal surfaces, metal can effect
    Variety of materials
    Frequency dependent reflection / penetration
    Emanating EM noise – especially from the engine compartment
    No line of sight with large attenuation

## Slide 5: Vehicle Channel Model Cntd.
Car to car channel model:
  Mobility considerations
    Higher delay spread
    Higher Doppler
  Signal directivity
    Due to the metal can effect, the signal emanates from the car mostly through the windows

## Slide 6: Car to Car Communication
Fast burst mode communication between moving cars
  Exchange data between moving cars when they are in close proximity to each other
  Very fast link setup and authentication for short data packets
  Good SNR

## Slide 7: WiFi based Positioning and Ranging
WiFi Geo-Location in Mall has been previously suggested [2]
WiFi based positioning and ranging can also significantly increase positioning accuracy in urban canyons
  Ranging support (Time of Flight measurement)
  Mobile and urban environment

## Slide 8: References
[1] IEEE 11-13/0534r1, “Direction and Use Cases for HEW”, HanGyu Cho (LG Electronics)
[2] IEEE 11-13/0554r0, “Usage Models for HEW”, Minho Cheong (ETRI)