## Slide 1: Airport Capacity Analysis
Date: 2013-11
Authors:

## Slide 2: Background
13/1012r4 Described Dynamic Sensitivity Control DSC and provided a throughput calculation for a hypothetical Cell Structure network.
  3005Mbps vs. 397Mbps
This presentation looks at the Airport Terminal Use Case.

## Slide 3: 1b Airport/train stations - public access and cellular offload
Pre-Conditions
High density users access internet through multiple operators’ WLAN network. The venue owner possibly manages or controls multiple operators’ WLAN networks uniformly for the purpose of users’ QoS.
Environment
The environment is very complex and may suffer severe interference.
Each AP serves 120 devices in a 200m2 area. The inter-AP distance is in the range of 15~20m. Single/multiple operators.
Applications
Video based applications: TV, VOD, Video conference; VHD highly compressed (100 Mbps): 50% of users
VPN applications (20 Mbps): 10% of users
Game online; 100 Mbps, < 100 ms jitter; < 100 ms latency: 10% of users
Internet access: email, twitter, web surf, IM. (20 Mbps): 30% of users
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple operators.
Interference with unmanaged networks (P2P)
Interference with cellular (e.g. TD-LTE) in in-device coexistence scenario (e.g. User equipments running Wi-Fi and TD-LTE at the same time.)
Use Case
Travelers are using the network to surf websites, watch movies, play online games and access cloud services.
Laurent Cariou (Orange)

## Slide 4: Channels
Ref:Wikipedia

## Slide 5: Denver Airport Terminal B

## Slide 6: How many people at the gates?
Airbus 380 seats 580 in 3 classes (can seat 853 in one class)

## Slide 7: Numbers
Number of Gates = 40
Ave Passengers per Gate = 200
Percentage gates in use. peak = 60%
Total = 4800 passengers in Terminal
Assume 60% waiting at Gates, 40% in eating areas
USERS

## Slide 8: Capacity Requirement
From “Use Case 1b”, for 120 users per AP
  50% using 100Mbps (VHD) = 100/60 = 1.67Mbps per user
  10% using 20Mbps (VPN) = 20/12 = 1.67Mbps per user
  10% using 100Mbps (Gaming) = 100/12 = 8.34Mbps per user
  30% using 20Mbps (Internet)= 20/36 = 0.56Mbps per user
Total traffic for 120 users = 240Mbps
For 4800 users about 40 APs required (42 in example below)
APs

## Slide 9: What is Practical PHY Rate and Throughput?
Requirement is 240Mbps
  170Mbps Downlink
  70Mbps Uplink
With EDCA Overhead say 480Mbps required
  340Mbps Downlink
  140Mbps Uplink
PHY Rates (40MHz BW)
  Downlink 8SS, 64 QAM ¾ , Short GI = 1080Mbps PHY Throughput ~596Mbps (65k agg.)
  Uplink 2SS, 64 QAM ¾, Short GI = 270Mbps PHY Throughput ~205Mbps (65k agg.)
  Next QUESTION: IS 10 Channels OK?

## Slide 10: RF Considerations
40 MHz BW 64QAM ¾
  Typical RX sensitivity is -70dBm
  Allow 5dB margin, use -65dBm
TX power 18dBm
Assume 0dBi gain antennas
  +2dBi at AP, -2dBi at STA
Range 150m Free Space (LOS), 40m indoor model
  APs mounted high would tend to LOS but with obstruction losses (e.g. people and antenna directivity), say10dB, the LOS is 60m.
  Assume 40 – 60m range

## Slide 11: AP Layout
Regular spacing of APs fits the requirement
10 Channels gives 200m between APs, no overlap

## Slide 12: Points
Get Out Statement – “I am not an expert at layouts for enterprise or hotspots (I have never done it) so my example analysis may have flaws.”
BUT on the face of it
11ac APs with 40MHz BW will provide enough capacity and coverage to meet this particular case example.
What’s missing?
  Need for fast handoff between APs for Mobile Users.
    Is 11r, OKC, or 11ai sufficient?
    Can 11ai be improved for ‘handoff’ rather than initial link?