## Slide 1: Airport Capacity Analysis
Date: 2014-01
Authors:

## Slide 2: Background
This presentation looks at the Airport Terminal Use Case
Use Case Dense Apartments 13/1487r2
  “Single” apartment complex 2.4 to 2.96 improvement in throughput per apartment (using DSC and Channel; Selection)
  “Double” apartment complex 3.3 to 4.12 improvement in throughput per apartment (using DSC and Channel; Selection)
Airport Capacity 13/1489r4
  Can be satisfied by existing technology
E-Education 14/0045
  Improvement of 2.28 in throughput per classroom using DSC
Pico Cell 14/0048
    Improvement of 7.58 in in capacity using DSC in cell cluster pattern (see 13/1290)
    “Street” Pico cell can be satisfied with existing technology
DSC is explained in 13/1012 and 13/1290

## Slide 3: 1b Airport/train stations - public access and cellular offload
Pre-Conditions
High density users access internet through multiple operators’ WLAN network. The venue owner possibly manages or controls multiple operators’ WLAN networks uniformly for the purpose of users’ QoS.
Environment
The environment is very complex and may suffer severe interference.
Each AP serves 120 devices in a 200m2 area. The inter-AP distance is in the range of 15~20m. Single/multiple operators.
Applications
Video based applications: TV, VOD, Video conference; VHD highly compressed (100 Mbps): 50% of users
VPN applications (20 Mbps): 10% of users
Game online; 100 Mbps, < 100 ms jitter; < 100 ms latency: 10% of users
Internet access: email, twitter, web surf, IM. (20 Mbps): 30% of users
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple operators.
Interference with unmanaged networks (P2P)
Interference with cellular (e.g. TD-LTE) in in-device coexistence scenario (e.g. User equipments running Wi-Fi and TD-LTE at the same time.)
Use Case
Travelers are using the network to surf websites, watch movies, play online games and access cloud services.
Laurent Cariou (Orange)

## Slide 4: Channels
Ref:Wikipedia

## Slide 5: Denver Airport Terminal B

## Slide 6: How many people at the gates?
Airbus 380 seats 580 in 3 classes (can seat 853 in one class)

## Slide 7: Numbers
Number of Gates = 40,Ave Passengers per Gate = 200
Percentage gates in use, number using Wi-Fi?
  Assume peak = 60%,
  Total = 4800 passengers using Wi-Fi in Terminal
Assume 60% waiting at Gates, 40% in eating areas
USERS

## Slide 8: Capacity Requirement
Revised figures* for “Use Case 1b”, 120 users per AP
  50% using 15Mbps (VHD) = 15*60 = 900Mbps
  10% using 10Mbps (VPN) = 10*12 = 120Mbps
  10% using 10Mbps (Gaming) = 10*12 = 120Mbps
  30% using 10Mbps (Internet)= 10*36 = 360Mbps
  Total traffic for 120 users = 1500Mbps (12.5Mbps per user)
For 4800 users about 40 APs required (42 in example below)
APs
* As suggested by Philip Barber during Telecon presentation

## Slide 9: What is Practical PHY Rate and Throughput?
Requirement is 1500Mbps per AP
  1.2Gbps Downlink
  300Mbps Uplink
PHY Rates at 40MHz (10 Channels)
  Downlink 8SS, 40MHz, 256 QAM 5/6, Short GI = 1617Mbps Throughput ~1.36Gbps DL only (520k/8k aggregation, 2.285ms pkts)
  Uplink 2SS, 40MHz, 256 QAM 5/6, Short GI = 404Mbps PHY Throughput ~357Mbps UL only (260k aggregation, 4.696ms pkts)
Aside: Throughput restricted by max length (5.464ms) and default TXOP Limit (4.090ms). TXOP Limit could be raised.
What is the composite traffic result? ~790Mbps DL and ~125Mbps UL
With EDCA overhead, expect ~560Mbps DL and ~90Mbps UL per AP

## Slide 10: What Do These Results Tell Us?
Can’t meet demand if 120 users per AP with current 11ac, need to reduce Users per AP.
  DL, 560Mbps capacity, 10Mbps per user = 56 users/AP
  UL, 90Mbps capacity 2.5Mbps per User = 36 users/AP Note: This assumes a STA is only 2SS capable
  Need to see if 36 users per AP is practical.
Alternative would be to assume STA has higher >2SS

## Slide 11: RF Considerations
40 MHz BW 256 QAM 5/6 (10 Channels)
  Typical RX sensitivity is -65dBm
  Allow 5dB margin, use -60dBm
TX power 18dBm
  Assume +2dBi at AP, -2dBi at STA antennas
Range 40m Free Space (LOS), 23m indoor model (no obstruction)
  APs mounted high would tend to LOS but with obstruction losses (e.g. people), say10dB, the LOS is reduced to 13m.
    Assume 23m range of AP for now

## Slide 12: AP Layout
APs spaced at 23m allow for a 10 channel scheme.
This provides 14 APs covering area for 576 users
i.e. 41 users per AP
Use of directional antennas would allow closer spacing of APs.
Conclusion is that it is possible using 11ac

## Slide 13: Points
Need to check if the numbers and distribution of users is valid.
Need to check if the traffic (12.5Mbps per User) is valid
BUT - on the face of it, (if the 120 users per AP is changed)
11ac APs at 40MHz BW could (in theory) provide enough capacity and coverage to meet this particular case example. (Antenna directivity would certainly make it possible, but is in ballpark anyhow)
What’s missing?
  Need for fast handoff between APs for Mobile Users
  APs handle distribution of STAs efficiently

## Slide 14: Conclusions
Could argue that 8SS MU-MIMO is tough in practice but this was the ‘new’ technology invented for 11ac.
Channel re-use can be easily achieved using directional antennas on APs. This would allow even closer locations than the 23m used in example.
  This may allow use of 256 QAM 3/4 rather than 5/6.
To work requires
  STAs to association to the ‘best’ AP
  STAs to handoff to APs when mobile.
Need to analyze each Use Case to find the “Gap”