## Slide 1: Resolution Policies for Remaining Comments
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Date: 2014-01-07
Authors:

## Slide 2: Abstract
This document describes the resolution policies for the remaining comments assigned to Hitoshi Morioka.
The CIDs are 3242, 2389, 2998, 3078, 3367, 3388, 2090 and 2613.

## Slide 3: CID3242
Comment
  It is odd that the GTK is not wrapped with AES key wrap, as is done elsewhere in 802.11. While this field is covered by the AEAD encryption, best practices as defined by NIST would have the key wrapped even when covered by AEAD.
Proposed Change
  Either add key wrapping or include a note as to why the GTK does not need to be key wrapped.
Resolution Policy
  Add key wrapping for GTK. The key wrapping method will be imported from existing EAPOL-Key key wrapping.

## Slide 4: CID2389, 2998, 3078, 3367, 3388
Comment
  These comments pointed out the lack of Annex B (PICS).
Proposed Change
  Add description in Annex B.
Resolution Policy
  I already presented in 11-13/1503r0 and I got feedback.
  I’ll implement the feedback in the next revision.

## Slide 5: CID2090
Comment
  "The choice is determined by the STA based on what IP Address assignment methods are supported by the AP.” This smacks of multiple options for political rather than technical reasons. If there is genuinely no good technical reason, expect the market to be confused and support neither of them.
Proposed Change
  Either justify why there are two optional methods, or make one of them mandatory.
Resolution Policy
  Remove “FILS IP address configuration”. (clause 8.4.2.186.2-4, 10.44.4.2 and modify related sentences)
  Because the all information carried by “FILS IP address request TLV” (8.4.2.186.2), “FILS IP address response TLV” (8.4.2.186.3) and “FILS DNS Information TLV” (8.4.2.186.4) can be carried by the higher layer packets such as DHCP, ARP, RA and NA.
  By this modification, the higher layer setup method (frame format and protocol sequense) can be unified.
  It will affect the resolution for CID2172 and 2176.
  I asked the technical reason of “FILS IP address configuration” to George Cherian by e-mail two times (10th Dec. and 17th Dec.), but I have not gotten the response yet.

## Slide 6: CID2613
Comment
  Example usage of "FILS HLP wrapped data TLV" should be introduced.
Proposed Change
  Add examples usage of "FILS HLP wrapped data TLV" as a new Annex. See 11-13/1047r0.
Resolution Policy
  Add the example usage based on 11-13/1047r0 according to the resolution for CID2090.
  Or reject the comment as “out of scope”.
    Send liaison to IETF(?)