## Slide 1: Large-Scale Characteristics of 45 GHz Based on Channel Measurement
Authors/contributors:
Date: March 19, 2014
Presenter: Haiming WANG
Name | Company | Address | Phone | Email
Haiming WANG | SEU/CWPAN | 2 Sipailou, Nanjing 210096, China | +86-25-5209 1653-301(ext.) | hmwang@seu.edu.cn
Jin ZHU |  |  |  | jinzhu@emfield.org
Wei HONG |  |  | +86-25-5209 1650 | weihong@seu.edu.cn
Nianzu ZHANG |  |  | +86-25-5209 1653-320(ext.) | nzzhang@seu.edu.cn
Shiwen HE |  |  | +86-25-5209 1653-3121(ext.) | hesw01@seu.edu.cn

## Slide 2: Abstract
This presentation gives large-scale characteristics of 45 GHz band based on channel measurement.

## Slide 3: Outline
Channel Measurement Scheme
  Transmission Scenarios
  Channel measurement setup
Large-Scale Characteristics at 45 GHz band
  Path-loss Fading
  Shadow Fading

## Slide 4: Transmission Scenarios
Conference room
Cubicle room
Living room

## Slide 5: Layout
Cubicle Room
Living Room
Conference Room

## Slide 6: Channel Measurement Setup
A PC is used to not only control the rotary table with an RS-232 port but also control the signal generator and vector network analyzer (VNA) with LAN ports.
The signal generator transmits CW signal at each frequency, then Rx power and channel frequency response are obtained by the VNA. The positions of Tx and Rx antennas and measured data are simultaneously recorded.

## Slide 7: Antennas for Channel Measurement
Type II: Open-ended waveguide (OEW) antenna with 6-dBi gain
Type I: Horn antenna with 23.7-dBi gain
Angle (degree)
Pattern (dB)
H-Plane
E-Plane

## Slide 8: Antennas for Channel Measurement
Type Ⅲ: SIW antenna with 3-dBi gain
Three antennas are linear polarized
Gain
Angle (deg)
Angle (deg)
Gain
Maximum Gain
Maximum Gain
Gain

## Slide 9: Scenarios
Three indoor environments: Conference room, Cubicle room, Living room
Two sets of scenarios: AP-STA, STA-STA; LoS, NLoS
Six antenna configurations:
  Tx and Rx: Horn, Co-pol;
  Tx and Rx: Horn, Cross-pol;
  Tx and Rx: OEW, Co-pol;
  Tx and Rx: OEW, Cross-pol;
  Tx and Rx: SIW, Co-pol;
  Tx and Rx: SIW, Cross-Pol

## Slide 10: Scenarios
NLoS setup of Conference room and Living room :
  A metal board is placed between TR antennas
  Both antennas are directed to the wall with same incident angle
OLoS setup of Cubicle room:
  Transmit antenna is placed next to the door
  Receive antenna is placed at the sitting position

## Slide 11: Path-Loss Model
Two Path-Loss channel models are compared
where and n denote the reference distance and PL exponent, respectively and is the shadowing fading.

## Slide 12: Conference Room

## Slide 13: Fitting plot-Conference room-AP
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Carrier frequency：44.955GHz
Height of Tx antenna is 1.95 m while height of Rx antenna is 1 m.
TR distance is from 1 m to 9 m with 9 positions.
Forty points are measured with interval 0.5 cm at each position.

## Slide 14: Fitting plot-Conference room-AP
(a) Tx and Rx: Horn, Cross-Pol
(c) Tx and Rx: SIW, Cross-Pol
(b) Tx and Rx: OEW, Cross-Pol
Cross polarization loss can be observed from the illustration.
Cross polarization loss decreases as antenna beam width increases.
Large beam width antenna has larger amplitude fluctuation.
20 dB
25 dB
25 dB
15 dB
3 dB
3 dB

## Slide 15: Fitting plot-Conference room-AP
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Fitting of Path-loss fading for five different frequencies.
Path-loss increases as frequency increases.
Reflection of the table causes a more obvious multipath effect than other two indoor environments.

## Slide 16: Fitting plot-Conference-NLoS-AP
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Reflection causes an additional fading of more than 20 dB due to longer transmitting distance.
The variation of received power in NLoS scenario is much more obvious than LoS scenario.
16 dB
13 dB
18 dB
15 dB
26 dB
20 dB

## Slide 17: Fitting plot-Conference room-STA
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Frequency ：44.955GHz
Heights of Tx antenna is 1.45 m while Rx 1 m.
TR distance is from 1 m to 9 m with 9 positions.
40 points are measured with interval 0.5cm at each position.

## Slide 18: Fitting plot-Conference room-STA
(a) Tx and Rx: Horn, Cross-Pol
(c) Tx and Rx: SIW, Cross-Pol
(b) Tx and Rx: OEW, Cross-Pol
Cross polarization loss can be observed from the illustration.
Cross polarization loss decreases as antennas beam width increases.
Wider beam width antenna has larger fluctuation.
28 dB
32 dB
19 dB
20 dB
5 dB
1 dB

## Slide 19: Fitting plot-Conference room-STA
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Fitting of Path-loss fading for five different frequencies.
Path-loss increases as frequency increases.
The regularity related to distance caused by multipath effect of table reflection is obvious in narrow beam antenna.

## Slide 20: Fitting plot-NLoS-STA
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Reflection causes an additional fading due to longer transmitting distance.
Variation of received power in NLoS scenario is much more obvious.
20 dB
11 dB
15 dB
13 dB
17 dB
15 dB

## Slide 21: Cubicle Room

## Slide 22: Fitting plot-Cubicle room-AP
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Frequency ：44.955GHz
Heights of Tx antenna is 1.95 m while Rx 1 m.
TR distance is from 1 m to 8 m with 14 positions.
5×5 points are measured with interval 1cm at each position.
The fitted line agree well with free space fading model.

## Slide 23: Fitting plot-Cubicle room-AP
(a) Tx and Rx: Horn, Cross-Pol
(c) Tx and Rx: SIW, Cross-Pol
Cross polarization loss can be observed from the illustration.
The loss decreases as antennas beam width increases.
Wider beam width antenna has larger fluctuation.
(b) Tx and Rx: OEW, Cross-Pol
25 dB
21 dB
21 dB
21 dB
12 dB
12 dB

## Slide 24: Fitting plot-Cubicle room-AP
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
Fitting of Path-loss fading for five different frequencies.
Path-loss increases as frequency increases.
Fluctuation appears as wide beam width antennas are used for reflection mainly from the ground.
(b) Tx and Rx: OEW, Co-Pol

## Slide 25: Fitting plot-Cubicle room-STA
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Frequency ：44.955GHz
Heights of Tx antenna is 1.45 m while Rx 1 m.
TR distance is from 1 m to 8 m with 14 positions.
5×5 points are measured with interval 1cm at each position.
The fitted line agree well with free space fading model.

## Slide 26: Fitting plot-Cubicle room-STA
(a) Tx and Rx: Horn, Cross-Pol
(c) Tx and Rx: SIW, Cross-Pol
Cross polarization loss can be observed from the illustration.
The loss decreases as antennas beam width increases.
Wider beam width antenna has larger fluctuation.
(b) Tx and Rx: OEW, Cross-Pol
23 dB
22 dB
23 dB
22 dB
1 dB

## Slide 27: Fitting plot-Cubicle room-STA
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
Fitting of Path-loss fading for five different frequencies.
Path-loss increases as frequency increases.
Fluctuation appears as wide beam width antennas are used for reflection mainly from the ground.
(b) Tx and Rx: OEW, Co-Pol

## Slide 28: Living Room

## Slide 29: Fitting plot-Living room-AP
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Frequency ：44.955GHz
Heights of Tx antenna is 1.45 m while Rx 1 m.
TR distance is from 2 m to 8 m with 12 positions.
5×5 points are measured with interval 1cm at each position.
The fitted line agree well with free space fading model.

## Slide 30: Fitting plot-Living room-AP
(a) Tx and Rx: Horn, Cross-Pol
(c) Tx and Rx: SIW, Cross-Pol
(b) Tx and Rx: OEW, Cross-Pol
Cross polarization loss can be observed from the illustration.
The loss decreases as antennas beam width increases.
Wider beam width antenna has larger fluctuation.
23 dB
23 dB
21 dB
23 dB
2 dB
2 dB

## Slide 31: Fitting plot-Living room-AP
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Fitting of Path-loss fading for five different frequencies.
Path-loss increases as frequency increases.
Fluctuation appears as wide beam width antennas are used for reflection mainly from the ground.

## Slide 32: Fitting plot-Living room-STA
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Frequency ：44.955GHz
Heights of Tx antenna is 1.45 m while Rx 1 m.
TR distance is from 2 m to 8 m with 12 positions.
5×5 points are measured with interval 1cm at each position.

## Slide 33: Fitting plot-Living room-STA
(a) Tx and Rx: Horn, Cross-Pol
(c) Tx and Rx: SIW, Cross-Pol
(b) Tx and Rx: OEW, Cross-Pol
Cross polarization loss can be observed from the illustration.
The loss decreases as antennas beam width increases.
Wider beam width antenna has larger fluctuation.
28 dB
28 dB
18 dB
19 dB
5 dB

## Slide 34: Fitting plot-Living room-STA
(a) Tx and Rx: Horn, Co-Pol
(c) Tx and Rx: SIW, Co-Pol
(b) Tx and Rx: OEW, Co-Pol
Path-loss fitting of five different frequencies.
Path-loss increases as frequency increases.

## Slide 35: Shadow Fading Distribution in Cubicle Room
Three dotted lines represent measurement deviation from fitted values of three antennas
Shadow fading agrees well with the log-normal distribution
Horn
OEW
SIW

## Slide 36: Conclusion
The n value increases when the antenna beam width increases
In NLoS scenario, the n value is around zero, indicating a homogeneous distribution of field strength in the room
The measured path loss is close to the theoretical path loss in free space when Tx and Rx both use antennas with co-polarization.
The average additional loss due to cross-polarization is about 24 dB, 22 dB and 2.6 dB for horn, OEW and SIW antennas, respectively.
Standard deviation increased when larger HPBW antenna is configured in the measurement
Standard deviation of reference path-loss constant Ac is more stable than PL(d0)

## Slide 37: Future Work
Continue large-scale channel measurement in scenarios of obstruction and movement.
Resume the small-scale channel measurement in all three transmission scenarios.
Finish the channel models based on our channel measurement.

## Slide 38: Conference Room Characteristics
Environment | Scenario1 | Scenario2 | Antenna | Pol | Frequency average |  |  | 
 |  |  |  |  | n | PL0 | σ | Ac
Conference_room | LoS | STA-STA | P-P | co | 1.139749 | 73.82214 | 0.35163 | 40.74653
 |  |  |  | cross | 1.511144 | 97.52996 | 0.588878 | 64.45435
 |  |  | O-O | co | 2.630479 | 61.0116 | 0.78206 | 27.93598
 |  |  |  | cross | 1.577574 | 87.18569 | 0.886897 | 54.11007
 |  |  | S-S | co | 2.56263 | 63.11556 | 0.927394 | 30.16818
 |  |  |  | cross | 1.845868 | 67.78648 | 1.139117 | 34.8391
 |  | AP-STA | P-P | co | 1.304055 | 70.27431 | 0.415879 | 37.1987
 |  |  |  | cross | 2.938059 | 88.46472 | 1.023065 | 55.38911
 |  |  | O-O | co | 2.245392 | 63.76319 | 1.396849 | 30.68758
 |  |  |  | cross | 1.972381 | 85.43296 | 1.468228 | 52.35734
 |  |  | S-S | co | 2.476442 | 62.29575 | 0.893249 | 29.34837
 |  |  |  | cross | 2.389663 | 62.17207 | 1.645918 | 29.22468
 | NLoS | STA-STA | P-P | co | 0.309017 | 91.40559 | 1.4048 | 58.45821
 |  |  |  | cross | 0.305875 | 124.8957 | 1.476564 | 91.94828
 |  |  | O-O | co | 1.419084 | 84.64103 | 1.428556 | 51.69365
 |  |  |  | cross | -0.15111 | 104.8941 | 1.242671 | 71.94672
 |  |  | S-S | co | 1.155316 | 86.4047 | 1.474105 | 53.45732
 |  |  |  | cross | 0.089013 | 93.49527 | 0.758909 | 60.54789
 |  | AP-STA | P-P | co | -0.08935 | 97.37172 | 1.278552 | 64.42434
 |  |  |  | cross | -0.03463 | 121.7664 | 1.450245 | 88.819
 |  |  | O-O | co | 0.183341 | 93.58295 | 1.039485 | 60.63557
 |  |  |  | cross | 1.015959 | 95.8668 | 0.6578 | 62.91942
 |  |  | S-S | co | 0.626734 | 89.42338 | 1.039081 | 56.476
 |  |  |  | cross | 0.218608 | 94.19642 | 1.172416 | 61.24904
H-H: horn to horn; O-O: OEW to OEW; S-S: SIW-SIW; co: co-polarization; cross: cross-polarization

## Slide 39: Cubicle Room Characteristics
H-H: horn to horn; O-O: OEW to OEW; S-S: SIW-SIW;OLoS: obstructed line of sight
Environment | Scenario1 | Scenario2 | Antenna | Pol | Frequency average |  |  | 
 |  |  |  |  | n | PL0 | σ | Ac
Cubicle_room | LoS | STA-STA | P-P | co | 1.79569 | 68.73988 | 0.0638 | 35.66426
 |  |  |  | cross | 1.606904 | 91.79041 | 0.112075 | 58.71479
 |  |  | O-O | co | 1.987251 | 68.57695 | 0.735821 | 35.50133
 |  |  |  | cross | 1.587652 | 92.96078 | 1.345013 | 59.88516
 |  |  | S-S | co | 2.482227 | 66.32985 | 0.885278 | 33.38247
 |  |  |  | cross | 2.390764 | 67.77112 | 1.42207 | 34.82373
 |  | AP-STA | P-P | co | 2.005008 | 65.94193 | 0.115975 | 32.86631
 |  |  |  | cross | 1.55109 | 91.45427 | 0.205535 | 58.37865
 |  |  | O-O | co | 1.9603 | 64.61183 | 0.7977 | 31.53622
 |  |  |  | cross | 2.326209 | 86.84695 | 1.174327 | 53.77134
 |  |  | S-S | co | 2.155971 | 64.73363 | 1.060874 | 31.78625
 |  |  |  | cross | 1.976314 | 69.33096 | 1.3203 | 36.38358
 | NLoS | STA-STA | P-P | co | 2.095542 | 69.22941 | 0.702625 | 36.1538
 |  |  |  | cross | 0.934477 | 100.3316 | 0.826368 | 67.25597
 |  |  | O-O | co | 1.476295 | 74.5536 | 1.634227 | 41.47799
 |  |  |  | cross | 1.229472 | 94.59532 | 0.621439 | 61.5197
 |  |  | S-S | co | 2.178841 | 74.30523 | 0.952263 | 41.35785
 |  |  |  | cross | 2.167594 | 84.23814 | 0.841976 | 51.29075
 |  | AP-STA | P-P | co | 2.46548 | 63.2624 | 0.326308 | 30.18679
 |  |  |  | cross | 2.632257 | 82.60221 | 0.18978 | 49.52659
 |  |  | O-O | co | 1.935346 | 66.71061 | 0.414967 | 33.63499
 |  |  |  | cross | 2.892114 | 79.22749 | 0.912131 | 46.15187
 |  |  | S-S | co | 1.7684 | 70.30398 | 0.455573 | 37.3566
 |  |  |  | cross | 1.44843 | 85.58861 | 1.366867 | 52.64123

## Slide 40: Living Room Characteristics
Environment | Scenario1 | Scenario2 | Antenna | Pol | Frequency average |  |  | 
 |  |  |  |  | n | PL0 | σ | Ac
Living_room | LoS | STA-STA | P-P | co | 2.231738 | 64.62093 | 0.109134 | 31.54532
 |  |  |  | cross | 1.993172 | 92.27755 | 0.12008 | 59.20193
 |  |  | O-O | co | 2.412787 | 62.80727 | 0.513327 | 29.73165
 |  |  |  | cross | 2.115442 | 86.9178 | 1.313205 | 53.84218
 |  |  | S-S | co | 2.544253 | 62.50163 | 2.073575 | 29.55425
 |  |  |  | cross | 2.596201 | 64.2595 | 2.245281 | 31.31212
 |  | AP-STA | P-P | co | 2.075801 | 65.70149 | 0.043349 | 32.62588
 |  |  |  | cross | 2.024144 | 88.83036 | 0.157892 | 55.75475
 |  |  | O-O | co | 2.406526 | 63.84632 | 0.355291 | 30.7707
 |  |  |  | cross | 3.110935 | 81.87936 | 1.955085 | 48.80375
 |  |  | S-S | co | 2.286152 | 65.19459 | 2.053458 | 32.2472
 |  |  |  | cross | 2.516595 | 65.90757 | 2.686096 | 32.96019
 | NLoS | STA-STA | P-P | co | -0.43859 | 99.56027 | 0.546746 | 66.48465
 |  |  |  | cross | -0.46102 | 123.9658 | 0.806784 | 90.89018
 |  |  | O-O | co | 0.657759 | 93.34336 | 1.488326 | 60.26774
 |  |  |  | cross | 0.31636 | 104.366 | 1.410035 | 71.29041
 |  |  | S-S | co | 0.19743 | 94.47523 | 1.29829 | 61.52784
 |  |  |  | cross | -0.28265 | 100.3553 | 1.152425 | 67.40792
 |  | AP-STA | P-P | co | 1.524857 | 84.94494 | 0.286436 | 51.86933
 |  |  |  | cross | 0.097595 | 128.5621 | 0.681437 | 95.48653
 |  |  | O-O | co | 0.387018 | 92.98406 | 1.944789 | 59.90845
 |  |  |  | cross | 0.533777 | 102.8803 | 1.938324 | 69.8047
 |  |  | S-S | co | 0.204226 | 95.09873 | 1.037752 | 62.15135
 |  |  |  | cross | -1.54134 | 107.258 | 1.714575 | 74.31063
H-H: horn to horn; O-O: OEW to OEW; S-S: SIW-SIW