## Slide 1: PHY abstraction in system level simulation for HEW study
Date: 2014-01-20
Authors:

## Slide 2: Outline
Effective SNR Mapping and parameter fitting results
Fitting result sensitivity to bandwidth
Parameterise PER over PDU length
Frequency-domain modelling of interference
Temporal-domain modelling of interference

## Slide 3: Effective SNR Mapping
  Mapping a vector (SNR) to a scalar; four candidate methods
  EESM
  RBIR
  RBIR-BICM
  MMIB
  Share a similar processing flow
  The function is in the form:
  Map per sub-carrier SNR to a bit rate equivalence
  Take average over the per-subcarrier bit rate equivalence
  Map the averaged bit rate equivalence back to an effective SNR
  All methods need fitting for α and β
    For different MCS, FEC type and fading channel scenario
    Parameters need to be calibrated by fitting the simulated PER curves

## Slide 4: Selection of Mapping function
 | EESM | RBIR/RBIR-BICM | MMIB
Function for Φ | Closed-form | Tabulated | Closed-form; but not available for 256QAM
Function for Φ-1 | Closed-form | Tabulated | Tabulated; but not available for 256QAM
Curve fitting | Large search range for (α, β) | Limited search range for (α, β) | Limited search range for (α, β) Extra curve fitting for function Φ
For the complexity issue, MMIB will not be evaluated in this presentation

## Slide 5: Function Φ (normalised by bit per symbol)

## Slide 6: Simulation conditions/assumptions
  PPDU configuration
  VHT 40 MHz frame BCC FEC with single spatial stream
  MCS 0-9
  PDU length 1K bytes
  Channel condition
  Static frequency-selective channel type (B and D)
  Receiver assumption
  Ideal channel estimation
  Single tap equalisation
  Floating point Viterbi decoder

## Slide 7: BCC fitting results (Chan D)

## Slide 8: LDPC fitting results (Chan D)

## Slide 9: BCC fitting results (Chan B)

## Slide 10: LDPC fitting results (Chan B)

## Slide 11: Sensitivity to bandwidth
Fitting results obtained on 40 MHz are tested on 20 and 80 MHz cases
For 80 MHz, BCC has small but noticeable mismatch; LDPC has no significant mismatch
For 20 MHz, BCC has noticeable mismatch; LDPC has small mismatch for some MCSs

## Slide 12: 80 MHz Bandwidth (BCC Chan D)

## Slide 13: 80 MHz Bandwidth (LDPC Chan D)

## Slide 14: 20 MHz Bandwidth (BCC Chan D)

## Slide 15: 20 MHz Bandwidth (LDPC Chan D)

## Slide 16: Impact of PDU length
For the same MCS, FER varies depending on PDU length; but BER does not

## Slide 17: Parameterize FER on PDU length (1)
Alt. 1. Tabulate PER on MCS, PDU length
  Need to store a set of curves and interpolate for other length

## Slide 18: Parameterize FER on PDU length (2)
  Alt. 2. Map BER to FER using a model function
    Map SNR to BER(Pe) based on 1000B PDU
    FER ~ 1-(1- Pe)L/D, fitting D per MCS

## Slide 19: Interference modelling – frequency selectivity
In general, the interference is frequency selective;
However, modelling frequency selectivity interference in system level simulator is expensive
  Frequency selectivity modelling involves CIR generation and FFT processing;
  There may exist multiple interferers
May not be significant different from a white-noise interference modelling
  With respect to average power, the null subcarrier is deeper than the peak subcarrier in the interference spectrum
  With same power, instant white-noise has greater dynamic range than interference signal

## Slide 20: Instant interference power density
The interference power density peak matters more than the null

## Slide 21: Compare interference models
Interference power is defined w.r.t. to noise power

## Slide 22: Interference modelling – temporal dynamics
In OBSS, the interfering signal may not be aligned with intended signal in time;
  interfering signal may appear at any time with respect to the intended signal
Assessing the packet reception once either at the preamble and the end of the frame is pessimistic
  Due to aggregation, some MPDUs may be correctly received
Accurately modelling the temporal dynamic interference is costly
A good balance is to assess the reception for each MPDU duration in an A-MPDU

## Slide 23: Summary
Effective SNR Mapping
  All methods discussed give similar accuracy, RBIR/RBIR-BICM have advantage of small search space
  Parameters in the mapping function are not sensitive for 40 and 80 MHz bandwidths but for 20 MHz bandwidth
Parameterise PER over PDU length
  Fitted BER vs. FER mapping function can avoid storing too many FER tables
Frequency-domain modelling of interference
  White-noise model is sufficient
Temporal-domain modelling of interference
  Multiple check point in a frame
  Time resolution up to MPDU duration

## Slide 24: Reference
[1] “PHY Abstraction for System Simulation”, IEEE 802.11-04/0174
[2] “PHY Abstraction for HEW Evaluation Methodology”, IEEE 802.11-13/1059r0
[3] “PHY Abstraction for HEW System Level Simulation”, IEEE 802.11-13/1131r0
[4] “PHY Abstraction for HEW System Level Simulation”, IEEE 802.11-13/1390r0

## Slide 25
Thank you!