## Slide 1: Pico Cell Use Case Analysis HEW SG
Date: 2014-01
Authors:

## Slide 2: Background
This presentation looks at the Pico cell HEW Use Case.
See also:
Use Case Dense Apartments 13/1487r2
  “Single” apartment complex 2.4 to 2.96 improvement in throughput per apartment (using DSC and Channel; Selection)
  “Double” apartment complex 3.3 to 4.12 improvement in throughput per apartment (using DSC and Channel; Selection)
Airport Capacity 13/1489r4
  Can be satisfied by existing technology
E-Education 14/0045
  Improvement of 2.28 in throughput per classroom using DSC
Pico Cell 14/0048
    Improvement of 7.58 in in capacity using DSC in cell cluster pattern (see 13/1290)
    “Street” Pico cell can be satisfied with existing technology
DSC is explained in 13/1012 and 13/1290

## Slide 3: Objective
To look at the prime HEW Use Cases and see what is theoretically possible using known techniques.
Then to determine if there is a “gap” that can lead to a requirement for HEW.

## Slide 4: 4b Pico-cell street deployment - public access and cellular offload
Pre-Conditions
Street deployment for cellular offload purpose (potentially co-location with cellular network small cells) or for city neighborhood blanket coverage.
Environment
Most outdoor street deployments will be made with placement below rooftop (3 - 10m: typical location of cellular network pico cells): lamp poles, hanged on cables, stuck to walls. It will be mostly side coverage (omni or directional).
Inter-AP distance between 150 and 200 meters for blanket coverage. Shorter distance in higher density zones.
Applications
User traffic mix is similar to cellular traffic mix.
Mix of VOIP, Best effort FTP, Internet access, Web video, teleconferencing.
Throughput assumption: longtime/stable throughput per user >= 20 Mbps
Real-time Video Analytics & Augmented Reality
User Generated Content (UGC) Upload & Sharing with a higher proportion in public event zones.
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple operators.
Interference with stand-alone private APs from surrounding buildings. (at 2.4GHz, between 15 to 20 APs in all 3 channels (beacons already occupy 20% of channel)
Interference with unmanaged networks (P2P and private mobile APs such as mobile routers and tethering smartphones)
      Interference with 2G-3G-LTE, especially in case of co-site deployments, and in-device coexistence scenario.
Use Case
Users connect to hotspot, perform a mixture of applications, including VOIP calls, FTP, Internet access, video conference.
Some users are in mobility (walking down the street).
Laurent Cariou (Orange)

## Slide 5: Channels
Ref:Wikipedia

## Slide 6: Data Throughput requirement
20Mbps per user? That is higher than the “Airport”, propose use Airport numbers
  12.5Mbps per user: 10Mbps DL, 2.5Mbps UL
Density of users?
  Assume 0.5 people per square meter; assume 50% using Wi-Fi
  0.25 (Wi-Fi) users per square meter

## Slide 7: Pico Cell
First we will consider an open space case

## Slide 8
In 13/1290r1 it was shown that using DSC allowed a 7 segment cell pattern.
Hence, 40MHz channels
Improvement of 7.58 in capacity with DSC

## Slide 9: SU-MIMO
What is practical capacity of one AP SU-MIMO?
  256 QAM 5/6 40MHz 2SS:
    404Mbps per AP raw (11ac SU-MIMO). Max TP depends on aggregation
    For 0.25 users per square meter, # users = Area/4
    Throughput per User = Max TP x 4 x 0.7 /Area, Mbps/user
    Hence, Area = (Max TP x 4 x 0.7) / 12.5 square meters
    For various aggregation, we can determine the Max TP and hence the area.

## Slide 10: Cell Size
Check: 20users at 12.5Mbps = 250Mbps
250 / 0.7 = 357Mbps
Tiny cells, only 9 - 17ft radius!!
    Area = (Max TP x 4 x 0.7) / 12.5 square meters
    0.25 Users per square meter

## Slide 11: What about MU-MIMO?
DL could use MU-MIMO?
Assume:
  256 QAM 5/6 8SS at 40MHz ,1617Mbps PHY Rate, 262k aggregation
  256 QAM 5/6 2SS at 40MHz , 404Mbps PHY Rate, 131k aggregation
Result is ~600Mbps DL and ~170Mbps UL
Equivalent to about 60 users.
Area of cell is then 240m2 or 8.74m radius (29 feet) or APs sited at distances of ~60 feet apart (nowhere near the 100m target)
7 Segment cell only allows one AP per cell so cannot use greater than 40MHz

## Slide 12: Discussion on Open Case
Irrespective of DSC, or cell structure, one AP is only capable of serving about 60 users
  7 channel cell pattern (assuming 40MHz BW)
  10Mbps DL, 2.5Mbps UL
Area covered depends upon the user density.
  At 0.25 users per m2, cell size is about 30ft radius (Area 2600 ft2)
  APs spaced at 60ft (~20m)
This is well short of Use Case, but could be done

## Slide 13: Pico Cells
Now consider a street case

## Slide 14: Sidewalk Pico Cell
A sidewalk 5m wide.
Need to establish the value of L

## Slide 15: Range and throughput analysis
Best range that satisfies the required throughput
64 QAM 5/6 80MHz (4 channels) 45m range (L=90m)
OK = DL and UL throughputs are satisfied
Mixed traffic at 8SS and 2SS set at the required rates
*
*5dB margin used

## Slide 16: 80 MHz channel example
AP 4 does not exert CCA on AP1
  if AP1 sets CCA threshold to -65dBm
STA B does not exert CCA on STA A
Separating APs by ~90m satisfies Use Case throughput
(Seems only 2 channels, but other side of street means 4 channels required)
Note: AP to AP is LOS, STA to STA is NLOS

## Slide 17: Discussion
If Use Case refers to open area, then the cell sizes using 11ac (and DSC) are small.
  7 segment re-use means 40MHz BW is best can be used.
  Cell radius is ~10m
  Dependent upon user density
    Is 0.25 users per square meter about right?
  Result would be improved if more obstruction losses were included.
  If Use Case refers to Sidewalks, then Use Case can be satisfied. 80MHz channels can be used.

## Slide 18: Points (General points for most use cases?)
The throughput is directly related to the channel BW which is directly related to the channel re-use pattern
  Is channel re-use the main concentration?
  Do we factor in use of directional antennas to improve re-use?
Can throughput be improved over 11ac?
  Difficult to see major OFDM based improvements
Could EDCA Overhead be reduced?
  TDMA?
  Mixed CSMA/TDMA?
How effective in practice will aggregation be? Can we assume that high aggregation will be used?