## Slide 1: Some Findings from Real World Measurement
Date: 2014-01-17
Authors:

## Slide 2: Abstract
This submission shows some issues in real highly dense deployment case in Japan.
Management frames, especially Beacon and Probe Response, consume much time resources.
Retry frame is also one of the issues at cell edge.
Texts for PAR are proposed at the end of this submission.

## Slide 3: Pico-cell Street Deployment
It’s one of the most congested intersection in Japan.
HEW may be applied to this situation as targeting pedestrians stopping at traffic lights.
Frame observations here

## Slide 4: Breakdown of Frames (CH1)
name | Qtty | %Qtty | %Time
Association Req. | 932 | 0.3% | 0.1%
Association Res. | 758 | 0.2% | 0.1%
Reassociation Req. | 699 | 0.2% | 0.1%
Reassociation Res. | 688 | 0.2% | 0.1%
Probe Req. | 5892 | 1.8% | 1.5%
Probe Res. | 44793 | 13.8% | 10.8%
Timing Advertisement | 699 | 0.2% | 0.1%
Unknown(reserved) | 700 | 0.2% | 0.0%
Beacon | 56339 | 17.4% | 12.4%
ATIM | 639 | 0.2% | 0.1%
Disassociate | 742 | 0.2% | 0.1%
Authentication | 821 | 0.3% | 0.1%
Deauthentication | 742 | 0.2% | 0.1%
Action | 1746 | 0.5% | 0.1%
Action No Ack | 742 | 0.2% | 0.1%
Unknown(reserved) | 705 | 0.2% | 0.1%
subtotal | 117637 | 36.3% | 25.5%
name | Qtty | %Qtty | %Time
Unknown(reserved) | 788 | 0.2% | 0.1%
Unknown(reserved) | 761 | 0.2% | 0.1%
Unknown(reserved) | 736 | 0.2% | 0.1%
Unknown(reserved) | 718 | 0.2% | 0.1%
Unknown(reserved) | 788 | 0.2% | 0.1%
Unknown(reserved) | 731 | 0.2% | 0.1%
Unknown(reserved) | 682 | 0.2% | 0.0%
Control Wrapper | 680 | 0.2% | 0.0%
Block Ack Request | 1273 | 0.4% | 0.1%
Block Ack | 11548 | 3.6% | 0.2%
PS-Poll | 673 | 0.2% | 0.0%
RTS | 8125 | 2.5% | 0.2%
CTS | 8349 | 2.6% | 0.2%
ACK | 59467 | 18.3% | 2.3%
CF-End | 782 | 0.2% | 0.1%
CF-End + ACK | 692 | 0.2% | 0.1%
subtotal | 96793 | 29.9% | 3.6%
name | Qtty | %Qtty | %Time
Data | 1772 | 0.5% | 0.4%
Data + CF-Ack | 735 | 0.2% | 0.1%
Data + CF-Poll | 694 | 0.2% | 0.1%
Data + CF-Ack/CF-Poll | 742 | 0.2% | 0.1%
Null (no data) | 9199 | 2.8% | 0.6%
CF-Ack (no data) | 734 | 0.2% | 0.1%
CF-Poll (no data) | 750 | 0.2% | 0.1%
CF-Ack + CF-Poll | 706 | 0.2% | 0.1%
QoS Data | 88044 | 27.2% | 20.2%
QoS Data + CF-Ack | 642 | 0.2% | 0.1%
QoS Data + CF-Poll | 673 | 0.2% | 0.1%
QoS Data + CF-Ack/CF-Poll | 690 | 0.2% | 0.1%
QoS Null (no data) | 2294 | 0.7% | 0.1%
Reserved | 625 | 0.2% | 0.0%
QoS CF-Poll (no data) | 702 | 0.2% | 0.0%
QoS CF-Ack + CF-Poll | 690 | 0.2% | 0.1%
subtotal | 109692 | 33.8% | 21.9%
Management Frames
Control Frames
Data Frames
Total : 324122 frames, 51.0% occupied
(Duration : 10 min.)
Majorities over 10% are shaded.

## Slide 5: Breakdown of Frames (CH108)
name | Qtty | %Qtty | %Time
Association Req. | 175 | 0.1% | 0.0%
Association Res. | 557 | 0.2% | 0.0%
Reassociation Req. | 105 | 0.0% | 0.0%
Reassociation Res. | 120 | 0.0% | 0.0%
Probe Req. | 2657 | 0.8% | 0.1%
Probe Res. | 48318 | 15.1% | 3.6%
Timing Advertisement | 134 | 0.0% | 0.0%
Unknown(reserved) | 139 | 0.0% | 0.0%
Beacon | 63461 | 19.8% | 4.8%
ATIM | 122 | 0.0% | 0.0%
Disassociate | 235 | 0.1% | 0.0%
Authentication | 666 | 0.2% | 0.0%
Deauthentication | 975 | 0.3% | 0.0%
Action | 3164 | 1.0% | 0.1%
Action No Ack | 138 | 0.0% | 0.0%
Unknown(reserved) | 105 | 0.0% | 0.0%
subtotal | 121071 | 37.8% | 8.7%
name | Qtty | %Qtty | %Time
Unknown(reserved) | 168 | 0.1% | 0.0%
Unknown(reserved) | 139 | 0.0% | 0.0%
Unknown(reserved) | 147 | 0.0% | 0.0%
Unknown(reserved) | 135 | 0.0% | 0.0%
Unknown(reserved) | 138 | 0.0% | 0.0%
Unknown(reserved) | 121 | 0.0% | 0.0%
Unknown(reserved) | 137 | 0.0% | 0.0%
Control Wrapper | 119 | 0.0% | 0.0%
Block Ack Request | 2473 | 0.8% | 0.1%
Block Ack | 40253 | 12.6% | 0.4%
PS-Poll | 127 | 0.0% | 0.0%
RTS | 20117 | 6.3% | 0.2%
CTS | 24697 | 7.7% | 0.2%
ACK | 44781 | 14.0% | 0.5%
CF-End | 109 | 0.0% | 0.0%
CF-End + ACK | 119 | 0.0% | 0.0%
subtotal | 133780 | 41.8% | 1.4%
name | Qtty | %Qtty | %Time
Data | 2705 | 0.8% | 0.0%
Data + CF-Ack | 109 | 0.0% | 0.0%
Data + CF-Poll | 124 | 0.0% | 0.0%
Data + CF-Ack/CF-Poll | 127 | 0.0% | 0.0%
Null (no data) | 10140 | 3.2% | 0.1%
CF-Ack (no data) | 128 | 0.0% | 0.0%
CF-Poll (no data) | 136 | 0.0% | 0.0%
CF-Ack + CF-Poll | 129 | 0.0% | 0.0%
QoS Data | 51087 | 16.0% | 2.6%
QoS Data + CF-Ack | 69 | 0.0% | 0.0%
QoS Data + CF-Poll | 69 | 0.0% | 0.0%
QoS Data + CF-Ack/CF-Poll | 72 | 0.0% | 0.0%
QoS Null (no data) | 113 | 0.0% | 0.0%
Reserved | 84 | 0.0% | 0.0%
QoS CF-Poll (no data) | 107 | 0.0% | 0.0%
QoS CF-Ack + CF-Poll | 70 | 0.0% | 0.0%
subtotal | 65269 | 20.4% | 2.8%
Total : 320120 frames, 12.9% occupied
Management Frames
Control Frames
Data Frames
(Duration : 10 min.)
Majorities over 10% are shaded.

## Slide 6: Findings
Management Frames
  Probe Response and Beacon are majorities.
  Active scanning is used for 5GHz band.  Is it right way?
Control Frames
  Time occupancy is very small.
  Block ACK, RTS and CTS are more used in 5GHz band.
Data Frames
  QoS Data (EDCA mechanism) is commonly used.
  What are Null frames for?
General findings
  Time occupancy is lower in 5GHz band obviously.

## Slide 7: Considerations for Management Frames
Unnecessary probe exchanges should be reduced by operation, for example:
  Restricting use of wildcard SSID in Probe Request
  Using SSID List IE for specifying target APs
  Reduced Neighbor Report IE of 11ai to promote Passive Scanning
Reduction of time occupancy by Beacon should also be considered. But it should be carefully studied to avoid side effects.
  Using higher data rate?
  Extending beacon interval?

## Slide 8
Other issues about Management Frames
 |  | CH1 | CH108
Beacon |  | 56339 | 63461
 | Observed BSSIDs | 86 | 17
Probe Request |  | 5892 | 2657
 | broadcasted | 4763 | 2513
 | w/ wildcard SSID | 2634 | 1460
 | unicasted | 1129 | 144
Probe Response |  | 44793 | 48318
 | retry | 29140 (65.1%) | 34162 (70.7%)
Others |  | 10613 | 6635
(Duration : 10 min.)
(1)
(2)
Observed BSSIDs are much more in CH1. But observed Beacons are much less, almost 1 Beacon per BSSID a second.
Retry rates of Probe Response are very high. It may be because of far distance between AP and STA. And also why is Active scanning available in 5GHz band?

## Slide 9: Example of Probe Responses
Frame No. | Time | Transmitter | Receiver | RSSI (dBm) | Rate (Mb/s) | Info
404 | 1.971281 | AP-xxx | STA-zzz | -63 | 6 | Probe Response, SN=55, FN=0, Flags=........C, BI=100, SSID=foo
405 | 1.97134 |  | AP-xxx | -87 | 6 | Acknowledgement, Flags=........C
406 | 1.971785 | AP-xxx | STA-zzz | -65 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
407 | 1.971839 |  | AP-xxx | -87 | 6 | Acknowledgement, Flags=........C
408 | 1.972284 | AP-xxx | STA-zzz | -62 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
409 | 1.972671 | AP-xxx | STA-zzz | -63 | 6 | Probe Response, SN=54, FN=0, Flags=....R...C, BI=100, SSID=bar
410 | 1.972729 |  | AP-xxx | -84 | 6 | Acknowledgement, Flags=........C
411 | 1.976873 | AP-xxx | STA-zzz | -66 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
412 | 1.976891 |  | AP-xxx | -85 | 6 | Acknowledgement, Flags=........C
413 | 1.977403 | AP-xxx | STA-zzz | -62 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
414 | 1.977421 |  | AP-xxx | -86 | 6 | Acknowledgement, Flags=........C
415 | 1.977907 | AP-xxx | STA-zzz | -61 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
416 | 1.977926 |  | AP-xxx | -84 | 6 | Acknowledgement, Flags=........C
417 | 1.978409 | AP-xxx | STA-zzz | -63 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
418 | 1.978427 |  | AP-xxx | -84 | 6 | Acknowledgement, Flags=........C
419 | 1.979014 | AP-xxx | STA-zzz | -66 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
420 | 1.979033 |  | AP-xxx | -85 | 6 | Acknowledgement, Flags=........C
421 | 1.979512 | AP-xxx | STA-zzz | -62 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
422 | 1.97953 |  | AP-xxx | -85 | 6 | Acknowledgement, Flags=........C
423 | 1.97995 | AP-xxx | STA-zzz | -61 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
424 | 1.979966 |  | AP-xxx | -85 | 6 | Acknowledgement, Flags=........C
425 | 1.980545 | AP-xxx | STA-zzz | -63 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
426 | 1.980564 |  | AP-xxx | -86 | 6 | Acknowledgement, Flags=........C
427 | 1.981118 | AP-xxx | STA-zzz | -66 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
428 | 1.981138 |  | AP-xxx | -84 | 6 | Acknowledgement, Flags=........C
429 | 1.981632 | AP-xxx | STA-zzz | -63 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
430 | 1.981651 |  | AP-xxx | -84 | 6 | Acknowledgement, Flags=........C
431 | 1.982209 | AP-xxx | STA-zzz | -61 | 6 | Probe Response, SN=55, FN=0, Flags=....R...C, BI=100, SSID=foo
432 | 1.982228 |  | AP-xxx | -85 | 6 | Acknowledgement, Flags=........C
Sequence number isn’t accumulated.
Retry
STA is transmitting ACK frames. It may not reach at AP because of weak signal.

## Slide 10: Retry frames
Many retry other than Probe Response were observed, too.
Following two slides show its examples. One of the cause of retries might be far distance between AP and STA, cell edge or sticky client issue.
Large BSS use case is problematic for high efficiency. It has large cell edge area which would cause retry frame issue.

## Slide 11
Frame No. | Time | Transmitter | Receiver | RSSI (dBm) | Rate (Mb/s) | Info
133740 | 243.345396 | STA-xxx | AP-zzz | -83 | 6 | Request-to-send, Flags=........C
133741 | 243.347095 | STA-xxx | AP-zzz | -83 | 6 | Request-to-send, Flags=........C
133742 | 243.351056 | STA-xxx | AP-zzz | -80 | 6 | Request-to-send, Flags=........C
133743 | 243.354063 | STA-xxx | AP-zzz | -80 | 6 | Request-to-send, Flags=........C
133744 | 243.361967 | STA-xxx | AP-zzz | -83 | 6 | Request-to-send, Flags=........C
133745 | 243.364457 | STA-xxx | AP-zzz | -85 | 6 | Request-to-send, Flags=........C
133746 | 243.366747 | STA-xxx | AP-zzz | -85 | 6 | Request-to-send, Flags=........C
133747 | 243.367891 |  |  | -84 | 6 | Unrecognized (Reserved frame), Flags=o.mP.M.T.
133748 | 243.370905 | STA-xxx | AP-zzz | -82 | 6 | Request-to-send, Flags=........C
133749 | 243.380189 | STA-xxx | AP-zzz | -79 | 6 | Request-to-send, Flags=........C
133750 | 243.380536 | STA-xxx | AP-zzz | -80 | 6 | Request-to-send, Flags=........C
133751 | 243.382168 | STA-xxx | AP-zzz | -81 | 6 | Request-to-send, Flags=........C
133752 | 243.388183 | ap-1 | Broadcast | -68 | 6 | Beacon frame, SN=1230, FN=0, Flags=........C, BI=100, SSID=foo1
133753 | 243.388587 | ap-2 | Broadcast | -68 | 6 | Beacon frame, SN=1229, FN=0, Flags=........C, BI=100, SSID=foo2
133754 | 243.388943 | ap-3 | Broadcast | -68 | 6 | Beacon frame, SN=1229, FN=0, Flags=........C, BI=100, SSID=foo3
133755 | 243.389238 | ap-4 | Broadcast | -68 | 6 | Beacon frame, SN=1229, FN=0, Flags=........C, BI=100, SSID=foo4
133756 | 243.389636 | ap-5 | Broadcast | -68 | 6 | Beacon frame, SN=1229, FN=0, Flags=........C, BI=100, SSID=foo5
133757 | 243.390004 | ap-6 | Broadcast | -66 | 6 | Beacon frame, SN=1229, FN=0, Flags=........C, BI=100, SSID=foo6
133758 | 243.390453 | ap-7 | Broadcast | -68 | 6 | Beacon frame, SN=1229, FN=0, Flags=........C, BI=100, SSID=foo7
133759 | 243.390829 | sta-aaa | ap-8 | -79 | 24 | 802.11 Block Ack, Flags=........C
133760 | 243.392051 | sta-aaa | ap-8 | -79 | 24 | Request-to-send, Flags=........C
133761 | 243.392065 |  | sta-aaa | -71 | 24 | Clear-to-send, Flags=........C
133762 | 243.392071 | ap-8 | sta-aaa | -71 | 24 | 802.11 Block Ack, Flags=........C
133763 | 243.393371 | STA-xxx | AP-zzz | -81 | 6 | Request-to-send, Flags=........C
133764 | 243.399712 | STA-xxx | AP-zzz | -83 | 6 | Request-to-send, Flags=........C
133765 | 243.401103 | STA-xxx | AP-zzz | -84 | 6 | Request-to-send, Flags=........C
133766 | 243.409042 | STA-xxx | AP-zzz | -80 | 6 | Request-to-send, Flags=........C
133767 | 243.411952 | STA-xxx | AP-zzz | -82 | 6 | Request-to-send, Flags=........C
133768 | 243.420519 | STA-xxx | AP-zzz | -83 | 6 | Request-to-send, Flags=........C
133769 | 243.423547 | STA-xxx | AP-zzz | -80 | 6 | Request-to-send, Flags=........C
133770 | 243.429086 | STA-xxx | AP-zzz | -82 | 6 | Request-to-send, Flags=........C
133771 | 243.435752 | STA-xxx | AP-zzz | -83 | 6 | Request-to-send, Flags=........C
133772 | 243.435766 |  | STA-xxx | -81 | 6 | Clear-to-send, Flags=........C
133773 | 243.439449 | AP-zzz | Broadcast | -82 | 6 | Beacon frame, SN=1129, FN=0, Flags=........C, BI=100, SSID=foo8
STA is transmitting RTS again and again.
AP doesn’t reply CTS.
AP may not have received RTS.
Example of RTS retransmissions
Finally CTS was transmitted.

## Slide 12: Example of Deauthentication retransmissions
No. | Time | Transmitter | Receiver | RSSI (dBm) | Rate (Mb/s) | Info
169709 | 312.689705 | AP-xxx | STA-zzz | -81 | 6 | Deauthentication, SN=258, FN=0, Flags=........C
169710 | 312.689824 | AP-xxx | STA-zzz | -80 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169711 | 312.690029 | AP-xxx | STA-zzz | -80 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169712 | 312.690111 | AP-xxx | STA-zzz | -82 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169713 | 312.690255 | AP-xxx | STA-zzz | -80 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169714 | 312.690382 | AP-xxx | STA-zzz | -80 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169715 | 312.690504 | AP-xxx | STA-zzz | -79 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169716 | 312.690626 | AP-xxx | STA-zzz | -80 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169717 | 312.690751 | AP-xxx | STA-zzz | -80 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169718 | 312.690877 | AP-xxx | STA-zzz | -81 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169719 | 312.691031 | AP-xxx | STA-zzz | -79 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169720 | 312.691191 | AP-xxx | STA-zzz | -79 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169721 | 312.691333 | AP-xxx | STA-zzz | -79 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
169722 | 312.691466 | AP-xxx | STA-zzz | -80 | 6 | Deauthentication, SN=258, FN=0, Flags=....R...C
No ACK from STA probably
Sending Deauthentication frames to a STA already left?

## Slide 13: Summary
Too many Management frames occupy time resources in the current real world.
Retry frames caused by STAs at cell edge or by sticky clients are also issues for effectiveness.
In order to reserve more time resources for data frames, the following approaches should be considered:
  Reduction of unnecessary Management frames
    Some operations may provide solutions.
  Reduction of retry frames
     Texts for PAR are proposed in the next slide.

## Slide 14: Straw Poll
Do you support to include the following sentences at the end of Explanatory Notes of PAR?
“This project may also include the capability to optimize radio resource usage based on the individual radio conditions of STAs. It would be essential both for increasing radio resource efficiency, and for improving user experience.”
(It has been proposed as CID 255 of CC11 (13/1529r2))
Y/N/A =

## Slide 15: References
13/545r1 (7 signals)
13/556r0 (ETRI)
13/847r0, 13/1176r0 (Cisco)
13/523r2 (KDDI)

## Slide 16: Backup: Throughput Measurement (Download) in front of the coffee shop
Chart: 
| 0.772222222222222 | 0.773611111111111 | 0.774305555555555 | 0.775 | 0.775694444444444 | 0.776388888888889 | 0.776388888888889 | 0.777083333333333 | 0.777777777777778 | 0.778472222222222 | 0.786111111111111 | 0.786805555555555 | 0.7875 | 0.788194444444444 | 0.788194444444444 | 0.788888888888889 | 0.789583333333333 | 0.790277777777778 | 0.792361111111111 | 0.793055555555556 | 0.800694444444444 | 0.801388888888889 | 0.802083333333333 | 0.802777777777778 | 0.803472222222222
CH1 | 0.65 | 2.47 | 3.62 | 1.57 | 3.12 | 2.8 | 4.21 | 3.64 | 1.41 | 4.44
CH108 | 27.25 | 20.46 | 10.91 | 16.56 | 20.59 | 14.09 | 23.76 | 23.88 | 30.97 | 28.42
LTE | 16.98 | 13.82 | 12.99 | 12.82 | 15.66
(Mbps)