## Slide 1: Outdoor AP measurement in Tokyo
Date: 2015-01-21
Authors:

## Slide 3: Abstract
Carried out outdoor AP measurement in Tokyo for simulation scenario.
The measurement results were not fully captured in the current simulation scenario (11-13/1001r5).
Shall we capture real world environment in the simulation scenario?
Any volunteers to carry out measurement in other countries.
Acknowledgements
  This measurement was carried out under the committee of Association of Radio Industries and Businesses (ARIB) of Japan.

## Slide 4: Motivation
We believe inter-AP distance is smaller in real outdoor environment.
Carried out AP measurement around Tokyo.
 | Scenario Name | Topology | Management | Channel Model | Homogeneity | ~Traffic Model
1 | Residential | A - Apartment bldg. e.g. ~10m x 10m apts in a multi-floor bldg ~10s of STAs/AP, P2P pairs | Unmanaged | Indoor | Flat | Home
2 | Enterprise | B - Dense small BSSs with clusters e.g. ~10-20m inter AP distance, ~100s of STAs/AP, P2P pairs | Managed | Indoor | Flat | Enterprise
3 | Indoor Small BSS Hotspot | C - Dense small BSSs, uniform e.g. ~10-20m inter AP distance ~100s of STAs/AP, P2P pairs |  |  |  | 
 |  |  |  |  |  | Mobile
4 | Outdoor Large BSS Hotspot | D - Large BSSs, uniform e.g. 100-200m inter AP distance ~100s of STAs/AP, P2P pairs | Managed | Outdoor | Flat | Mobile
4a | Outdoor Large BSS Hotspot + Residential | D+A | Managed + Unmanaged |  | Hierarchical | Mobile + Home
Simulation scenario (11-13/1001r5)

## Slide 5: Measurement point around Tokyo
All measurement points (35 points) are outdoor.
Measurement results are in 2.4GHz band.
Tokyo, downtown
Tokyo, residential
Kanagawa
(Yokohama, Kawasaki and Yokosuka)

## Slide 6: To estimate inter-AP distance
Option B
From operator’s website
Option A
From actual measurement
Pros
Easy to know # of APs in a area and to calculate inter-AP distance.
Cons
Don’t know signal of all APs in the website can be observed.
https://play.google.com/store/apps/details?id=com.farproc.wifi.analyzer&hl=en
Pros
Easy to know # of APs observed at that point (including indoor ones ).
Cons
Don’t know how much distance from the AP.
We combined options A and B.
© Mapion MAP data © ZENRIN
http://sasp.mapion.co.jp/m/docomo_wifi/35.6645653_139.7597406_8000/?citycode=13103

## Slide 7: Steps to estimate inter-AP distance
Unmanaged
APs
Step 1 : Measure RSSI, MAC address etc for each AP
Step 2 : Cal. # of APs per operator eg, N=5 APs for Operator A
Step 3 : Go to operator A’s website and draw circle with radius r such that # of APs within circle becomes N = 5.
Eg, radius r =50m
Step 4 : Calculate inter-AP distance with hexagonal cell based on N and r.
Measurement point at step 1
r=50m
Inter-AP distance is
N=5 APs
Same density
* SSID with quite similar MAC address is considered as multi SSID.
© Mapion MAP data © ZENRIN
http://sasp.mapion.co.jp/m/docomo_wifi/35.6645653_139.7597406_8000/?citycode=13103

## Slide 8: Results of inter-AP distance per operator
Measurement Area | Tokyo, downtown | Tokyo, residential | Kanagawa
Inter-AP distance (m) per operator | 48.1 (averaged over 13 points) | 52.4 (averaged over 2 points) | 55.7 (averaged over 8 points)
Tokyo, downtown
Tokyo, residential
Kanagawa
(Yokohama, Kawasaki and Yokosuka)

## Slide 9: Observations from outdoor measurement
Outdoor inter-AP distance per operator is about 50m.
  Current inter-AP distance in simulation scenario 4 is 130m (TBD).
  Indoor AP is included BUT its signal was observed outdoor.
Other observations
  Multiple operators are using same channel.
    Multi operator environment is necessary.
  Many unmanaged (~12) APs were observed across channels.
    Tethering devices might be included.
    Unmanaged environment is necessary.
Simulation scenario 4a is the closest but real environment has smaller inter-AP distance.

## Slide 10: AP deployment in other countries from website
We didn’t carry out the measure in those cities but inter-AP distance seems smaller than current scenario (130m)?
Map data © 2014 Cibercity, Google
http://maps.fon.com/mapContent?lt=48.871472551785864&ln=2.2907056557884165&zm=17
50m
Paris, near triumphal arch (FON)
Map data © 2014 3D Cities, SA, Google
http://maps.fon.com/mapContent?lt=38.718233531625536&ln=-9.122463847423559&zm=18
50m
Lisbon (FON)
50m
Seoul, near Myeong-dong (olleh)
http://zone.wifi.olleh.com/en/#none
http://www.wifiworld.co.kr/main.s2
Seoul, near Myeong-dong (LG U+)
50m

## Slide 11: Conclusions
Carried out outdoor AP measurement around Tokyo.
Outdoor inter-AP distance was about 50m.
  Current simulation scenario only supports 130m.
Simulation scenario 4a is the closest but real environment has smaller inter-AP distance.
Any volunteers to carry out the measurement in other countries?

## Slide 12: Backup

## Slide 13: Comparison to current simulation scenario
Scenario | Inter-AP distance | Interference from unmanaged AP | Interference from other managed APs (OBSS interference)
Scenario 3 (Indoor) | 7m or 12m | P2P model is supported with R=3. | OBSS interference is currently not captured in this scenario
Scenario 4 (Outdoor) | 130m 50m in our measurement | Residential model with unmanaged APs is supported. (Specified as in 4a) | Captured by an overlap of 3 operators, using relatively similar grid but channel selection offset
Simulation scenario (11-13-1001r5)
Do we need to modify the simulation scenario?
Any volunteers to carry out the measurement in other countries