## Slide 1: OFDM-IDMA Uplink Communication
Date: 2014-01-20
Name | Affiliations | Address | Phone | email
Shingo Yoshizawa | Kitami Institute of Technology | Koen-cho 165, Kitami, Hokkaido, 090-8507 Japan | +81-157-26-9284 | yosizawa@mail.kitami-it.ac.jp
Leonardo Lanante | Kyushu Institute of Technology | 〒820-8502 Kawazu 680-4, Iizuka City, Fukuoka Japan | +81-948-29-7692 | leonardo@dsp.cse.kyutech.ac.jp
Hiroshi Ochi | Kyushu Institute of Technology | 〒820-8502 Kawazu 680-4, Iizuka City, Fukuoka Japan | +81-948-29-7692 | ochi@cse.kyutech.ac.jp

## Slide 2: Abstract
HEW SG’s main goal is to provide efficiency improvements in high traffic density scenarios.
Uplink multi-user schemes can improve uplink system level efficiency.
This contribution introduces a promising uplink multi-user scheme for HEW.

## Slide 3: Orthogonal vs Non-Orthogonal Multiple Access Schemes
Machine to Machine (M2M) Networks
  High Spectral Efficiency of Multiple Access
  Large Numbers of Communication Users
Orthogonal Multiple Access Scheme
  TDMA, FDMA, OFDMA
  Expense Radio Resources due to Scheduling and Channel Allocation
Non-Orthogonal Multiple Access Scheme
  CDMA, IDMA
  Potential to Support Larger Number of Users
  No Need to Scheduling and Channel Allocation

## Slide 4: IDMA (Interleave Division Multiple Access)
Features
  Multiple access scheme where users are distinguished by different interleavers.
  Low Cost in Multi-user Detection (MUD)
    IDMA: O(K), CDMA: O(K2) for K Users
  High Power and Spectral Efficiency
    Can be made to have low PAPR and multiple streams per user is possible
  Intra-Cell and Cross-Cell Interference Mitigation
  Suitable for Wide or Narrow Band Transmission
OFDM-IDMA
  Advantageous in Synchronization and Channel Equalization compared to single carrier IDMA.

## Slide 5: OFDMA vs OFDM-IDMA
Coded bits for user1
Coded bits for user2
Coded bits for user3
Coded bits for user4
time
subcarriers
Coded bits for user1
Coded bits for user2
Coded bits for user3
Coded bits for user4
time
subcarriers
OFDM-IDMA
OFDMA

## Slide 6: OFDM-IDMA Transmitter Model
Repetition Code
Interleaver
for user k
PSK
Modulation
IFFT
Cyclic Prefix
Transmitter for user k
Transmitter
for user-1
Channel
for user 1
Transmitter
for user-k
Transmitter
for user-K
Channel
for user k
Channel
for user K

## Slide 7: OFDM-IDMA Receiver Model
Remove
Cyclic
Prefix
FFT
Decoder
ESE
(Elementary Signal Estimator)
Deinterleaver
Interleaver
for user-1
Decoder
Deinterleaver
Interleaver
for user-k
Decoder
Deinterleaver
Interleaver
for user-K
Receiver

## Slide 8: OFDM-IDMA Uplink Scenario
1 AP (up to 4 Antennas) and 16 STAs (1 Antenna)
Frame Format
  Based on IEEE802.11n SISO PHY (40 MHz BW)
    STF(Short Training Field), LTF(Long Training Field), DATA
  AP Channel Estimation from UL Users’ LTFs
STF
LTF
DATA
DATA
DATA
DATA
User 1
STF
LTF
DATA
DATA
DATA
DATA
User 2
STF
LTF
DATA
DATA
DATA
DATA
User 3
STF
DATA
DATA
DATA
LTF
DATA
User 4
AP
STAs

## Slide 9: Antenna Diversity
Maximal Ratio Combining (MRC)
  Post-FFT Processing by Combining Log-Likelihood Ratios (LLRs)
FFT
ESE
FFT
ESE
FFT
ESE
FFT
ESE
Decoder
Decoder
Diversity Branches
LLRs
Int.
Int.
Deint.
Deint.
Σ
Σ

## Slide 10: Simulation Parameters
Bandwidth | 40 MHz
Number of OFDM Subcarriers | 128
Number of Data Subcarriers | 108
OFDM Symbol Length | 4 μs (Cyclic Prefix:0.8 μs)
Modulation | BPSK
Packet Size | 512 bits
Repetition Code Length | 16
Number of Users | 16
Number of Iterations in MUD | 10
Number of AP Antennas | 1, 2, 3, 4
Channel Model | One Path Fading
Total Data Rate | 27 Mbps (1.68 Mbps per User)

## Slide 11: BER Performance
16-User OFDM-IDMA over Fading Channels for 1, 2, 3, and 4 AP Antennas

## Slide 12: Conclusion
OFDM-IDMA uplink scenario and frame format have been presented.
  Incorporated with the IEEE802.11a/g/n/ac Standard
Effect of antenna diversity in OFDM-IDMA has been reported.
  Realization of Simple and Effective Post-FFT MRC
  Eb/N0 7-8 dB Gain for 4 Antennas
Future work
  Provide a more detailed implementation feasibility study
  Simulation results in realistic channel conditions

## Slide 13: References
[1] Peng Wang, Jun Xiao, Li Ping, “Comparison of orthogonal and non-orthogonal approaches to future wireless cellular systems,'' IEEE Vehicular Technology Magazine, pp. 4-11, Vol. 1, Issue 3, pp. 4-11, Sept. 2006.
[2] Li Ping, Qinghua Guo, Jun Tong, “The OFDM-IDMA approach to wireless communication systems,” IEEE Wireless Communications, Vol. 14, Issue. 3, pp. 18-24, June 2007.
[3] Hidehiro Matsuoka and Hiroki Shoki, “Comparison of pre-FFT and post-FFT processing adaptive arrays for OFDM systems in the presence of co-channel interference,” IEEE PIMRC 2003, pp. 1603-1604, Sept. 2003.