## Slide 1: Discussion on HEW PAR
Date: 2014-01-19
Authors:

## Slide 2: Abstract
  This contribution discusses on backward compatibility which is one of the open issues in the current PAR discussion.

## Slide 3: Backward compatibility
  The ability of one new system to interwork with another old system
HEW AP
HEW STA
Legacy STA
HEW AP
HEW STA
Legacy STA
X
Mixed Mode
Greenfield Mode
Backward compatible!
Non-backward compatible!

## Slide 4: Issues on backward compatibility
Issue #1: Which modes does HEW support?
  Option 1: Mixed mode
  Option 2: Mixed mode and Greenfield mode
Issue #2: What does legacy mean?
  Option 1: 11n and 11ac devices only
  Option 2: OFDM devices, i.e., 11a/g/n/ac devices
  Option 3: all legacy devices, i.e., 11a/b/g/n/ac devices

## Slide 5: Issue #1: Which modes does HEW support?
Most of top-five scenarios are ‘mixed mode’ in nature.
  Three public scenarios, i.e., airport/train station, public transportation, and pico-cell street, are natively mixed mode.
  Dense apartment building is probably mixed mode.
  E-education scenario may be possible to operate in greenfield mode (e.g. only HEW-based smart pads are ‘on’ during class time)
Is 11n ‘greenfield mode’ successful?
  Not used in market
  Not so much gain only from legacy preamble omission
Current PAR draft seems to include ‘greenfield mode’ [1]
  “… include a mode of operation ensuring backward compatibility…”
  It was captured in the PAR draft without discussion.
We propose not to include ‘greenfield mode’ in HEW without clear reason
  To avoid wasteful effort on additional mode

## Slide 6: Issue #2: What does legacy mean?
  Many comments not supporting backward compatibility with 11b in HEW.
  11n already doesn’t support backward compatibility with 11b.
Unanimous agreement on backward compatibility with 11n and 11ac
If HEW interworks with 11n and 11ac, there is no additional cost to make HEW interwork with 11a and 11g
  11n and 11ac supports backward compatibility with 11g and 11a, respectively by maintaining legacy preamble.
  No reason not to support backward compatibility with 11a and 11g
We propose to support backward compatibility with 11a/g/n/ac
  Wi-Fi Alliance (WFA) can provide guidance on backward compatibility when HEW is certified.

## Slide 7: Proposed PAR text changes
5.2.b. Scope of the project:
  …..
  The new amendment shall include a mode of operation ensuring ensure backward compatibility and coexistence with legacy IEEE802.11 OFDM devices

## Slide 8: References
[1] IEEE802.11-13/1410r3 hew-draft-par-and-5c