## Slide 1: HEW Evaluation Metrics
Date: 2014-01-20
Authors:
Name | Affiliation | Address | Email
Yonggang Fang | ZTE |  | yfang@ztetx.com
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Kaiying | ZTE |  | lv.kaiying@zte.com.cn
Zhendong Luo | CATR |  | luozhendong@catr.cn
Meng Yang | CATR |  | yangmeng@catr.cn

## Slide 2: Background
HEW Evaluation Metrics (1)
  Evaluation metrics is important to evaluate WLAN system performance and to achieve the goal of HEW
  [1] lists the evaluation metrics for HEW and suggests to use it to evaluate the performance of WLAN for the scenario defined in [2].
    Link level evaluation metrics
    QoE evaluation metrics
    Network level evaluation metrics
  [4] suggests defining the goal and metrics first for creating a PAR
    area throughput and average throughput per STA with efficiency improvement relative to 11n/ac
    user quality of experience
      minimum average data rate,
      maximum connection setup delay, maximum packet transmission delay

## Slide 3: Background
HEW Evaluation Metrics (2)
  In the response LS [3], WFA suggests to consider the evaluation metrics
    Cell edge (5%), average (50%) and area (aggregate) throughputs
    Fairness (inverse standard deviation of per-user throughputs)
    Outage rate (% of users with links unable to achieve 5Mbps throughput – a normal minimum satisfactory rate)
    Support possible technology proposals that may demonstrate enhanced differentiation / prioritization of traffic flows / classes within a scenario
    Evaluate the performance of scenarios for operator networks:
      OBSS between networks in multiple management entities (inc. hidden node problem)
      outdoor performance (inc. larger delay spreads, and high MCS / MIMO)
      impact of management traffic (inc. from “idle STAs”) – probe request/response, RRM signaling
      efficient use of complete 2.4/5 GHz (inc. tradeoff between channel bandwidth and OBSS contention)

## Slide 4: Background
HEW Evaluation Metrics (3)
  [5] also suggests to include the area throughput as one of the evaluation metrics in PAR.
  [6] lists metrics of interests for consideration
    Average data throughput per station and per system.
    Average access delay,
    collision probability
  [7] suggests the evaluation metrics in the evaluation methodology document:
    Aggregate area throughput [bps/m2] for specified scenarios
    Average per-STA throughput in all participating BSS
    5% point in the throughput for measuring cell edge performance
    Time constraint throughput for delay sensitive applications

## Slide 5: Proposals
Clearly define evaluation metrics for evaluating HEW achievement. Metrics could contain
  Qualitative definition
  Quantative definition
The metrics is to evaluate
  User experience
  Network capacity
  Reliability
The metrics should be included in either the evaluation methodology or the simulation scenario document.

## Slide 6: HEW Evaluation Metrics
Throughput Metrics (1)
  Per-STA DL/UL throughput:
    This metrics is used to measure the user experience in different simulation scenario.
    Definition: measure 5 percentile STA DL/UL throughput at the edge of cell and 50 percentile medium STA DL/UL throughput for different service categories, over multiple BSS in a given area.
    Per-STA DL/UL throughput is measured at MAC SAP, starting from MAC receiving a packet from high level till the transmission being confirmed.
STA
Busy
xIFS
Backoff
RTS
MPDU
CTS
MPDU
BA
Transmission duration measurement

## Slide 7: HEW Evaluation Metrics
Throughput Metrics (2)
  Per-BSS aggregated DL/UL throughput
    This metrics is used to measure the capacity of BSS in different simulation scenario.
    Definition: Per-BSS aggregated DL/UL throughput is measured by aggregating per-STA DL/UL throughput in BSS.
    Discussions
      the area throughput (bps/m2) is equivalent to per STA average throughput [8].
      the area throughput may not be good to reflect network capacity in different scenario
      Suggest to replace area-throughput with per-BSS throughput

## Slide 8: HEW Evaluation Metrics
Latency Metrics (1)
  Initial link setup latency
    This metric is to measure the delay in the initial link setup.
  Handoff latency
    This metric is to measure the delay in the link re-establishment as STA moves from one BSS to another.
    [Discussion] Those two metrics are used by TGAi to reduce the setup time.
  Transmission latency.
    This metric is to measure the transmission delay, i.e. medium acquisition time before the MPDU is transmitted. It could reflect an aspect of MAC efficiency.
    Definition: the transmission latency is measured from the time that MAC receives a packet till the time that PHY starts transmitting.

## Slide 9: HEW Evaluation Metrics
Latency Metrics (2)
  Discussion
    Some real time applications are delay sensitive. Per-STA throughput measurement could not directly reflect the user experience for those applications.
    In high density scenario, the transmission latency might be large and need to be evaluated.
STA
TXOP
TXOP
latency
AP/STA
TXOP
TXOP
…….

## Slide 10: HEW Evaluation Metrics
Reliability Metrics
  Robustness
    The robustness is used to measure the link performance especially in the interference environment such as high density scenario. It can also be used to evaluate the performance of MCS adaptation.
    Definition: First transmission success and re-transmission ratio.
  Outage
    It is used to measure the network performance especially in the cell edge and high density scenario. It may be useful for the admission control.
    Definition: percentage of STAs with the per-STA throughput less than 5Mbps [3]
    [Discussion] It could be derived from the per-STA throughput CDF.

## Slide 11: Summary
We suggest to define evaluation metrics
  Per-STA throughput and per-BSS throughput
  Transmission latency
  Reliability measurement

## Slide 12: References
11-13-1054-01-0hew-evaluation-metrics
11-13-1000-02-0hew-simulation-scenarios
11-13-1443-00-0hew-liaison-from-wi-fi-alliance-on-hew-use-cases
11-13-1404-00-0hew-thoughts-on-par
11-13-1366-02-0hew-some-propositions-to-progress-towards-the-par-definition
11-13-1401-00-0hew-outdoor-system-level-assessments-for-hew-sg
11-13-1359-00-0hew-hew-evaluation-methodology
11-13-0805-02-0hew-on-definition-of-dense-networks-and-performance-metric
802.11 Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications