## Slide 1: Requirements for Next Generation mmWave Systems
Date: 2014-01-21
Authors:

## Slide 2: Abstract
This presentation discusses application requirements for next generation mmWave wireless systems.

## Slide 3: Current state of 802.11ad
802.11ad provides for up to 7 Gb/s at low power
  There is a complete SoC with < 250 mW peak power
  Commercially available implementations with up to 4 Gb/s
  Multiple vendors have announced products or product development
Small form factor
  Complete implementation including antennas in < 12 mm x 12 mm
802.11ad complements 802.11ac in mobile devices
  802.11ad offers low power, small form factor for short range
  802.11ac provides legacy compatibility and better performance than 802.11n
  Fast session transfer allows seamless 802.11 experience

## Slide 4: Applications
Mobile applications are expanding area
  Billions of devices every year
  Tablets and smart phones will be volume leaders
  Wireless connectivity enables these devices
Mobile devices have different constraints
  Small form factor required
  Limited room for antennas
  Restricted peak and average power available
Backwards compatibility is a key factor
  Build on existing infrastructure with 802.11a/b/g/n

## Slide 5: High-speed Wireless Applications
One of the key applications is to cut the cable
Data rates for cables keep increasing:
  USB
    3.0 – 4 Gb/s, full duplex (5 GS/s with 8b/10b coding)
    3.1 – 8 Gb/s, full duplex (bonds 2 channels)
  Thunderbolt
    1 – 10 Gb/s, full duplex (10.3125 GS/s with 64b/66b coding)
    2– 20 Gb/s, full duplex (bonds 2 channels)
  Uncompressed video
    1080p, 24 bit, 60 Hz – 3 Gb/s
    4k, 24 bit, 60 HZ – 12 Gb/s

## Slide 6: New requirements
Build on 802.11ad’s current success
Higher data rates - > 40 Gb/s throughput
  MIMO
  Channel bonding
Enable lower power modes
  Evaluate modulation for peak power reduction
  Low power SC mode is an example
  Improvements for average power reduction

## Slide 7: Conclusions
Mobile devices and applications are increasing rapidly
Wired connectivity speed is continuing to increase
Wireless needs to keep up
802.11 should start looking at the next generation of mmWave systems

## Slide 8: Straw poll
What should be the next data rate for 802.11 in the 60 GHz band?
  20 Gb/s
  40 Gb/s
  100 Gb/s
  No new work in 60 GHz band