## Slide 1: PHY Abstraction for HEW System Level Simulation
Date: 2014-01-20
Authors:

## Slide 2: Introduction
Physical layer abstraction is a key enabling technique for system simulation.
A few flavors of effective SINR mapping have been overviewed and evaluated in [1].
Remaining questions about ESM performance to be answered this meeting.
  High modulation
  LDPC

## Slide 3: ESM for PHY Abstraction
Effective SINR is an average mapped equalizer-output SINR over all subcarriers.
  Hedge factors alpha and beta can be used to calibrate and compensate any residual errors.
OFDM transmission is modeled as an AWGN channel with one effective SINR.

## Slide 4: Effective SINR Mapping Functions
PHY Abstract | SINR Mapping | 
EESM | Exponential mapping | 
CM based RBIR | Mutual information assuming CM | 
BICM based RBIR | Mutual information assuming BICM | 
MMIB | Mutual information per bit | 

## Slide 5: Performance of PHY Abstraction
11ac, 1x1, 8000 bit per packet, MCS0-9, BCC and LDPC
  Channel D-NLOS, AWGN
PHY abstraction:
  RBIR/RBIR-BICM for MCS0-9, MMIB for MCS0-7
  EESM is not covered
  No tune-up for PHY abstraction (α=1, β=1).
Effective SNR vs. PER curves for D-NLOS are referenced to that of AWGN channels.
  The closer, the better!
Observations:
  All three methods (MMIB, RBIR-CM, RBIR-BICM) provides good PER results referenced to AWGN.
  ESM performs better for LDPC than BCC
    D-NLOS LDPC PER curves are closer to AWGN.

## Slide 6: BCC
Small mismatch between effective SNR vs. PER for fading channels (D-NLOS) vs. AWGN.

## Slide 7: LDPC
Negligible mismatch between effective SNR vs. PER for fading channels (D-NLOS) vs. AWGN.

## Slide 8: Observation
MMIB/RBIR are both good candidates for physical layer abstraction.
RBIR assuming CM and BICM performs very close (closer than previously shown in [1]).
ESM based PHY abstraction performs better (closer to AWGN) for LDPC than BCC.
MMIB/EESM is less ready to use for various kinds of modulation and coding schemes.

## Slide 9: Summary
Studies show ESM as good methods for performance prediction.
Suggest to use RBIR/RBIR-BICM as PHY abstraction methods in the system simulation.

## Slide 10: References
[1] 11-13-1390-00-0hew-phy-abstraction-for-hew-system-level-simulation