## Slide 1: Suggested PAR Changes
Date: 2014-01-20
Authors:

## Slide 2: Abstract
This document provides some comments on the 802.11 HEW Draft PAR & 5C Document based on 13/1410r3.

## Slide 3: Comment Areas
Reliability
Latency
Mobile

## Slide 4: RELIABILITY

## Slide 5: Comment on 5.5 and 8.1
In 13/1410r3:
In section 5.5 ‘Need for the Project’, P3L40: “With the real-time performance requirements of some of these applications, WLAN users demand improved reliability in delivering their applications. ”
  Comment: While ‘reliability’ is desirable, what does it mean here in the context of densely deployed real-time applications in the presence of interference? If we mean to say ‘reliably’ meeting real-time performance requirements, it is better to not add ‘reliability’ as a metric.
  Suggested Change: “WLAN users increasing demand that With the real-time performance requirements of some of these applications are met in dense deployments and in the presence of interference , WLAN users demand improved reliability in delivering their applications.”

## Slide 6: Comment on 5.5 and 8.1 (cont’d)
In 13/1410r3:
In section 8.1 ‘Additional Explanatory Notes’, P5L23, as one of the three categories of objectives to improve WLAN efficiency: “Increased robustness to outdoor propagation characteristics and increase uplink transmission reliability”
  Comment: How is ‘reliability’ different from robustness? In the referenced Simulation Scenarios document 11-13-1001r5, only ‘robustness’ is mentioned and not ‘reliability’.
  Suggested Change: “Increased robustness to in outdoor propagation environments characteristics and increase uplink transmission reliability”

## Slide 7: Latency

## Slide 8: Comment on 8.1 and 5.2b
In 13/1410r3:
Section 5.2b ‘Scope of the project’: “average throughput per station ” is the only metric mentioned.
Section 8.1 ‘Additional Explanatory Notes’, P4L39: “These metrics, along with the satisfaction of the packet delay and the packet loss requirements of applications, will directly correspond to user experience in identified scenarios.”
  Comments: ‘delay’ is described as another metric on par with average throughput per station, but it is not alluded to in the scope.
  Suggested Change in 5.2.b: “at least two (2) times improvement in applicable metrics such as the average throughput per station ”

## Slide 9: Mobile

## Slide 10: HEW’s Role in Mobile Offloading
In 13/1410r3 :
Section 8.1 clearly identified: ‘indoor and outdoor hotspots’ as a main expected usage model, which includes offloading operator mobile traffic as a primary application.
Mobile devices account for the bulk of WLAN traffic growth in recent years and the trend will continue. HEW needs more visibility into the future of mobile offloading.
In addition, we all know 3GPP is investigating operating in the unlicensed bands. We need more information and not design HEW in the blind.
Suggested Change:
  Add to the end of Section 8.1 “This amendment should take into account developments in 3GPP related to future mobile offload and coexistence needs.”
  In 7.2 “Joint Development” , Replace “No” with “Yes, liaison should be establish with 3GPP to better understand future mobile offload and coexistence needs.”