## Slide 1: Possible Agreements for the Design
Date: 2014-1-23
Authors:

## Slide 2: Abstract
11aq has discussed various design options and for some points there were consensuses. This presentation tries to enumerate potential agreements on the design options for PAD. The agreed design options might be incorporated into the specification frame document.

## Slide 3: Overview: Design Areas
Beacon: service discovery capability bit/element
Probe:
  Option 1: service discovery capability information in probe response frame same as in beacon
  Option 2: efficient service query and response with service ID
Announcement: new less frequent broadcasting frame for service announcement with service IDs
Query and Response:
  Option 1: tunnelling service discovery protocols by encapsulating into GAS frames
  Option 2: efficient service discovery with service ID as well as Option 1
Service Discovery Proxy: agent managing service information database and end points of the tunnel

## Slide 4: Beacon
Define a new service discovery capability element.
The new IE may includes
  ULP ID(s): Service discovery protocol ID(s)
  Service Type Mask.
It must be very short.

## Slide 5: Probe
Option 1
  Send probe response frame with service discovery capability information
Option 2
  Add a new IE for PAD.
  Efficient query with a service ID in probe request frame.
  AP which could provide the access to the service sends back a probe response frame.
  Reasonably short service ID is required (e.g. 6 octets).
  Third party STAs could recognize what services are available by overhearing the probe response which includes service ID.
  Service discovery proxy in ESS manages service information database.
  Probe frames could be minimized by the leverage of service announcement.

## Slide 6: Announcement
Create a new frame for one-way service announcement from AP to STA.
The frame could be a public action frame.
AP broadcasts the service announcement frame periodically.
But the frame will be less frequent than beacon frame for reducing traffic.
The announcement frame has the converted form of unsolicited service announcements of service discovery protocols with the use of service IDs.

## Slide 7: Query and Response
Option 1
  A new GAS-based query and response protocol which is similar to ANQP but not same as ANQP will be defined.
  802.11aq will tunnel service discovery protocols transparently. (but minor changes or compression or dummy IP are unavoidable)
  This means service providers, which talk legacy service discovery protocols in the infrastructure network, are not required to be changed to be discovered by the STAs in the pre-associated state.
  The new service transaction protocol could accommodate legacy service discovery protocols as well vendor-specific service discovery protocols without the introduction of service ID.
  GAS comeback request/response seem to be good for delayed responses which is due to service discovery latency.
Option 2
  Efficient service discovery with service ID(s) as well as Option 1
  But this is different from the query with service ID in probe frame in the sense that this is a unicast query.

## Slide 8: Service Discovery Proxy
Service discovery proxy a.k.a. service transaction proxy resides in ESS, either on AP or a separate server, and STA.
Service discovery proxy understands service discovery protocols, so new service registration mechanism is not required.
Service discovery proxy composites service ID(hash value) with a certain ID in service announcement packets or by parsing some parts of service query/ response of the service discovery protocols(i.e. attributes).

## Slide 9: Scenario 1: Typical tunneling
A STA receives a beacon frame which carries service discovery capability element which includes an ULP ID from an AP.
The STA sends service query encapsulated in a service transaction frame to the AP.
A service discovery proxy decapsulates the query and forwards it to the infrastructure network.
The service discovery proxy gets a service discovery response from service provider and tunnels to the STA.

## Slide 10: Scenario 2: Query in probe request
A STA sends a probe request frame including a service query with a service ID.
A service discovery proxy in the infrastructure network responses that the service is available via an AP.
The STA associates with the AP.

## Slide 11: Scenario 3: Two-step discovery
A STA sends a probe request frame including a service query with the service ID which means “IP Printer” but not specifying device driver version number.
A service discovery proxy in the infrastructure network responses that the service is available via an AP.
The STA sends encapsulated service query which asks the device driver version number to the AP, and the service discovery proxy tunnels the specific question to the network.
The service discovery proxy gets a response from the network and sends back an encapsulated response to the STA.

## Slide 12: Discussions