## Slide 1: Service Discovery Proxy at STA
Date: 2014-2-25
Authors:

## Slide 2: Abstract
Service Discovery Proxies are under discussion of 11aq. This presentation is provided to understand the behaviour of STAs for discovering services. Service Discovery Proxy at the end of the tunnel in a STA decapsulates frames embedding service discovery packets or gets service announcements, and forwards them to Service Discovery Plug-ins and finally to applications.

## Slide 3: Two Service Discovery Scenarios at STA
Manual Network Selection
  SDProxy(Service Discovery Proxy) updates Service Information Database.
  Available services are displayed for each of SSIDs at a WLAN connection manager.
  An user decides to associate a network which provides a certain service.
Application-driven Network Selection
  An user selects a print wizard on an application.
  The wizard with a Service Discovery Plug-in requests a service query for IP Printer to SDProxy.
  SDProxy returns SSIDs which provide IP Printing service after looking up of Service Information Database.
  The user selects a network among the SSIDs, then the wizard requests a detailed query to find printer driver version number.
  SDProxy sends the query to the AP of the network and gets the result of it.
  The printer wizard looks into the printer driver version numbers in the result and decides to join the network, and requests the association to WLAN connection manager.

## Slide 4: PAD Architecture at STA
Service Discovery Proxy
Service Discovery Plug-in for PAD
Service Announcement
Service Querying
Service Information Database
Application / PAD Connection Manager
WLAN Connection Manager
Wireless Network
Legacy Service
Discovery Library

## Slide 5: Service Discovery Proxy
SDProxy listens service announcements on the air in the pre-association sate and updates service information database.
SDProxy gets the request for simple PAD service query from applications or WLAN connection manager and returns the result after looking up of Service Information Database.
  If SDProxy finds out Service Information Database is out of date or the request mandates active service scan, it could send out probe request frames with PAD service query.
SDProxy gets the request for detailed PAD service query and sends the encapsulated query to an AP. It returns the query response from the AP to the application which requested.
SDProxy translates service identifiers from service discovery protocol specific identifier to 6-Octect PAD service ID and vice versa.

## Slide 6: Service Discovery Plug-in for PAD
Service Discovery Plug-in could be provided to applications as a form of library.
Application should be rewritten to be capable of PAD considering it could establish a new WLAN connection.
It speaks the language of the specific service discovery protocol, e.g. Bonjour, to get the query from the application. It hides simple service IDs.
It gets results for the query from SDProxy and returns them to the application in the language.

## Slide 7: Discussions