## Slide 1: IEEE802.11 Response to 6N15614- January 2014
+1 (321) 751-3958
5488 Marvell Lane,
Santa Clara, CA, 95054
Name
Company
Address
Phone
email
Bruce Kraemer
Marvell
bkraemer@
marvell
.com
Date: 2014- January -28
Authors:
Abstract: Information on network monitoring and control services mentioned in 6N15614
Notes: November 2011

## Slide 2: IEEE802.11 Response to 6N15614
JTC1/SC6/WG1

## Slide 3: 6N15614
Proposing a study period on “WLAN Network Optimization Technology”
Correctly notes that existing 802.11k ‘Radio Resources Management’ amendment may provide some elements of proposed solution
Questions the applicability of IEEE802.11z as relevant to the proposed solution
Does not reference IEEE802.11v as potentially relevant to the proposed solution

## Slide 4: Discussion
802.11z defines mechanisms for direct Station-to-Station connections while simultaneously maintaining AP/infrastructure connectivity
  It is not relevant to the proposed scope of study in 6N15614
802.11v defines PHY/MAC layer mechanisms that enable management of attached stations in a centralized or in a distributed fashion (e.g. monitoring, configuring, and updating) through a layer 2 mechanism
  Is highly relevant to the proposed scope of study
802.11k and 802.11v specifications were previously developed to address the proposed scope of study and are included in ISO/IEC 8802-11-2012.
  A standards-based solution therefore exists and a new study should consider new problem areas that are not addressed by without existing standards

## Slide 5: 802.11v Capabilities vs. Issues noted in 6N15614
Coverage and Capacity
  802.11v provides BSS Transition Management for network load balancing to address the “excessive clients connected to a single AP” situation
Noise and Interference
  802.11v provides Collocated Interference Reporting to allows a requesting STA to receive information concerning the collocated interference being experienced by another STA. This augments the 802.11k RPI Histogram report, used to identify interference that may be present.
Connectivity problems
    802.11v provides Diagnostic and Event Request and Report Procedures to identify authentication, association issues in addition to device configuration errors
Roaming issues
    802.11v provides BSS Transition Management for network load balancing and roaming, and Diagnostic and Event Reporting to report roaming issues

## Slide 6: Conclusions
802.11k and 802.11v together provide a standards-based solution for issues noted in 6N15614
Further clarification of the problem to be studied is suggested