## Slide 1: Multicast Considerations for HEW
Date: 18/03/2014
Authors:

## Slide 3: Abstract
Discuss the unique characteristics of dense deployment scenarios receiving the same contents
  In particular: Video distribution via multicast
Propose simulation scenarios to cover the multicast communication usage model that is critical to realizing the specific use cases

## Slide 4: Introduction
Possible usage model in HEW
  Many people in a stadium or concert arena watch the same video (e.g., stream of a football game or close-up of performer) with their phones/tablets.
  An advertisement or dedicated content in an airport such as news channels with respect to each country is broadcasted only to the people who want to receive it.
  Students in a classroom watch single contents of a textbook.
Technical conditions:
  Dozens/hundreds of STAs within a short distance (Dense environment)
  Simultaneous, single video contents distribution.
To ensure the contents are delivered with quality and low latency, high efficiency communication is essential
  Thus, this usage model should be
  in the target scope of HEW and
  provided for in the corresponding
  evaluation methodology.

## Slide 5: Multicast Enhancement to Achieve the Intended HEW Usage Model
Unicast is NOT suited to distribute the same content to vast number of STAs in close proximity
  Multicast is preferred in terms of the usage model and highest efficiency
11aa provides enhanced multicast, however, by itself, it may not be sufficient to cover use case envisioned by HEW
  Additional multicast enhancements in HEW should be considered
    For example, 11aa scheme may not provide high efficiency that HEW is targeting
    Efficient multicast communication in “a highly dense environment” should be covered
    Further discussions in HEW for more efficient solutions for same content distribution scenario
    For example but not limited to, multicast enhancement on IEEE802.11-2012 and/or 11aa or using a new enhancement

## Slide 6: Summary
To fully address the highly dense use cases such as Stadiums, Arenas, Airports, Malls, and stations, potential multicast enhancements in HEW should be explored.

## Slide 7: Proposals
It is necessary to extend simulation scenarios (11-13/1001r5) to cover multicast communication usage model

## Slide 8: Existing Simulation Scenario 3
Traffic model (per each BSS) - TBD |  |  |  |  | 
# | Source/Sink | Name | Traffic definition | Flow specific paramters | AC
Dowlink |  |  |  |  | 
D1 | AP/STA1 to AP/STA10 | Highly compressed video (streaming) | T2 |  | 
D2 | AP/STA11 to AP/STA20 | Web browsing | T4 |  | 
D3 | AP/STA21 to AP/STA30 | Local file transfer | T3 |  | 
Uplink |  |  |  |  | 
U1 | STA1/AP to STA10/AP | Highly compressed video (streaming) – UL TCP ACKs… |  |  | 
U2 | STA11/AP to STA20/AP | Web browsing: – UL TCP ACKs… |  |  | 
U3 | STA21/AP to STA30/AP | Local file transfer | T3 |  | 
TCP based streaming does not allow multicast
The # of STAs is too small
for the usage model

## Slide 9: Proposed Amendment to Simulation Scenario 3
Traffic model (per each BSS) - TBD |  |  |  |  | 
# | Source/Sink | Name | Traffic definition | Flow specific paramters | AC
Dowlink |  |  |  |  | 
D1 | AP/STA1 to AP/STA10 | Highly compressed video (streaming) | T2 |  | 
D2 | AP/STA11 to AP/STA20 | Web browsing | T4 |  | 
D3 | AP/STA21 to AP/STA30 | Local file transfer | T3 |  | 
D4 | AP/STA31 to AP/STA 70 | Multicast Video Streaming | T8 |  | 
Uplink |  |  |  |  | 
U1 | STA1/AP to STA10/AP | Highly compressed video (streaming) – UL TCP ACKs… |  |  | 
U2 | STA11/AP to STA20/AP | Web browsing: – UL TCP ACKs… |  |  | 
U3 | STA21/AP to STA30/AP | Local file transfer | T3 |  | 
U4 | STA/AP31 to STA/AP 70 | - |  |  | 
New source/sink and traffic for multicast streaming should be defined
There should be no data traffic from U4

## Slide 10: Existing Simulation Scenario 3
Traffic Model # | Traffic model name | Description | Application traffic (Forward / Backward) | Application Load (Mbps) (Forward / Backward) | A-MPDU Size (B) (Forward / Backward)
T1 | Local file transfer | FTP/TCP transfer of large file within local network | FTP file transfer / FTP TCP ack | Full buffer / 0.1 | Max A-MPDU / 64
T2 | Lightly compressed video |  |  |  | 
T3 | Internet streaming video/audio |  |  |  | 
T4 | 4k video streaming |  |  |  | 
T5 | Online game server |  |  |  | 
T6 | Management: Beacon |  |  |  | 
T7 | Managgeemnt: Probe requests |  |  |  | 
None of the proposed traffic models assumes one-way traffic base on UDP/IP and does not match multicast video streaming

## Slide 11: Proposed Amendment to Simulation Scenario 3
Traffic Model # | Traffic model name | Description | Application traffic (Forward / Backward) | Application Load (Mbps) (Forward / Backward) | A-MPDU Size (B) (Forward / Backward)
T1 | Local file transfer | FTP/TCP transfer of large file within local network | FTP file transfer / FTP TCP ack | Full buffer / 0.1 | Max A-MPDU / 64
T2 | Lightly compressed video |  |  |  | 
T3 | Internet streaming video/audio |  |  |  | 
T4 | 4k video streaming |  |  |  | 
T5 | Online game server |  |  |  | 
T6 | Management: Beacon |  |  |  | 
T7 | Managgeemnt: Probe requests |  |  |  | 
T8 | Multicast Video Streaming | UDP/IP transfer of compressed video streaming | UDP packet transfer/Nothing | 3-6Mbps/Nothing | 
A new traffic model for multicast streaming should be defined

## Slide 12: Proposal for New Traffic Model Descriptions
We define Multicast Video Streaming Traffic Model
  Multicast Video Streaming is one-way video traffic from AP to STAs
  The video traffic is generated from a video server, and traverses multiple hops in the internet before arriving at AP for transmission to STA.
multicast streaming
Station layer model
AP generates video frames at application layer.
Because the traffic from AP to station has experienced network jitter,
it can be modelled the same way as the traffic model of video streaming.
The video traffic goes through UDP/IP layer and then to MAC layer.
Video traffic generation
Traffic model from AP to station: use the same steps in video streaming traffic model
Evaluation metrics
MAC throughput, latency
We assume bit rate for video streaming 6 Mbps (1080/30p AVC) and 3 Mbps (1080/30p HEVC)

## Slide 13: Backup

## Slide 14: Expected number of multicast receiving STAs
Scenario 3 (Stadium use case, R=12m)
Assume there are 2.2 seats per 1m2.
Assume audience of 5% seats uses multicast service.
-> about 40 STAs are expected to receive multicast video packets in each cell (BSS).
R=12m
There are about 2.2 seats/m2 in typical stadium.