## Slide 1: Discussions on HEW Functional Requirements
Date: 2014-03-16
Authors:
Notes: doc.: IEEE 802.11-06/0528r0
May 2006
        Bruce Kraemer, Marvell
Page 1

## Slide 2: Abstract
This contribution provides an overview of HEW functional requirements and identifies items requiring further discussions, for the development of the HEW Functional Requirements.
Notes: doc.: IEEE 802.11-06/0528r0
May 2006
        Bruce Kraemer, Marvell
Page 2

## Slide 3: Outline
Background
Examples of Functional Requirements (11ac and 11n)
HEW PAR Highlights
HEW Functional Requirement Discussions
References

## Slide 4: Background
HEW SG Status
  Has completed / submitted PAR and 5C;
  Expect approvals near the end of March-2014;
  Expect starting TG in May-2014 FtF meeting;
  Is the time to work on Technical Supporting Materials for developing the HEW amendment, e.g.,
    Functional Requirements
    Simulation Scenarios
    Evaluation Methodology
    HEW Functional Requirements
  Shall be derived from the HEW PAR
  must be addressed by the HEW amendment, i.e., mandatory requirements
  should be defined in an unambiguous and verifiable way

## Slide 5: Examples: 11ac Functional Requirements
System performance
  shall provide at least a mode of operation capable of achieving a maximum Multi-STA aggregate throughput measured at the MAC SAP to be at least 1 Gbps, utilizing no more than 80 MHz of channel bandwidth in 5 GHz band.
  shall provide at least a mode of operation capable of achieving a maximum Single-STA throughput measured at the MAC SAP to be at least 500 Mbps, utilizing no more than 80 MHz of channel bandwidth in 5GHz band
Backward compatibility with 802.11a/n devices operating in 5 GHz
  shall provide backward compatibility with IEEE802.11a /n devices operating in the 5 GHz frequency band
Coexistence with 802.11a/n devices operating in 5 GHz
  shall provide mechanisms that ensure coexistence between TGac and legacy IEEE802.11a/n devices
Compliance to PAR
  complies with the PAR and 5 Criteria

## Slide 6: Examples: 11n Functional Requirements
Number | Name | Requirement
1 | Single Link HT rate supported | Demonstrate at least one set of conditions under which 100 Mbps at the top of the MAC SAP can be achieved.
2 | HT rate supported in 20MHz channel | support at least one mode of operation that supports 100Mbps throughput at the top of the MAC SAP in a 20MHz channel.
3 | Supports 5GHz bands | support 5GHz bands (including those supported by .11a)
4 | .11a backwards compatibility | Some of the modes of operation shall be backwards compatible with 802.11a.
5 | .11g backwards compatibility | If it supports 2.4 GHz operation, some of the modes of operation shall be backwards compatible with 802.11g.
6 | Control of support for legacy STA from .11n AP | A .11n AP can be configured to reject or accept associations from legacy STA because they are legacy STA.
7 | .11e QoS support | Permit implementation of the 802.11e amendment within a .11n STA
8 | Spectral Efficiency | The highest throughput mode of the proposal shall achieve a spectral efficiency of at least 3 bps/Hz for the PSDU
9 | Compliance to PAR | Complies with all the mandatory requirements of the PAR [5] and 5 Criteria [6]
10 | Existence of single spatial stream transmission modes | Define single spatial stream transmission modes that provide at least one mode of operation that supports a maximum throughput of at least 50 Mbps in a 20MHz channel as measured at the MAC data SAP.
11 | Interoperability with single spatial stream non AP stations | A .11n AP or STA shall interoperate with a single spatial stream entity defined as a non-AP STA that complies with the .11n proposal with the exception of only supporting single spatial stream transmission modes as required by FR10.

## Slide 7: HEW PAR Highlights
Improve Average Throughput Per Station in dense deployment scenarios
  4 times improvements for at least one mode of operation (measured at the MAC data SAP)
  Target 5-10 times improvements
Focus on the relative improvements compared to previous IEEE 802.11 amendments
  IEEE 802.11n in 2.4 GHz
  IEEE 802.11ac in 5 GHz
Define operations in frequency bands between 1 GHz and 6 GHz
  Focus on the 2.4 GHz and the 5 GHz frequency bands.
  May add additional bands between 1 GHz and 6 GHz as they become available.
Enable backward compatibility and coexistence with legacy IEEE 802.11 devices operating in the same band.

## Slide 8: HEW PAR Highlights – con’t
Maintain or improve the power efficiency per station
  Power efficiency is intended to measure consumption of devices which can reasonably be assumed to be powered by batteries
  will take into account average power consumption for a given scenario
improve WLAN efficiency in three categories of objectives:
  Make more efficient use of spectrum resources in scenarios with a high density of STAs per BSS.
  Significantly increase spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in scenarios with a high density of both STAs and BSSs.
  Increase robustness in outdoor propagation environments and uplink transmissions.
Focus on improving metrics reflecting user experience
  average per station throughput, the 5th percentile of per station throughput, and area throughput.
  Packet delay
  Packet error ratio (PER)
  Note that: while specific throughput metrics are stated in the PAR, the primary objective of HEW is to deliver significant improvements in User Experience for all identified use cases

## Slide 9: HEW PAR Highlights – con’t
Support diverse deployment environments
  Dense deployments: the existence of many access points and non-AP stations in geographically limited areas.
  Deployment environments: wireless corporate office, indoor and outdoor hotspot, dense residential apartments, and stadiums.
  WLAN indoor and outdoor operations, where limit outdoor to stationary and pedestrian speeds.
Support a variety of applications:
  video, cloud access, and offloading.
  Expecting video traffic as the dominant type of traffic in many HEW deployments.
may include the capability to handle multiple simultaneous communications in both the spatial and frequency domains, in both the uplink (UL) and downlink (DL) direction.

## Slide 10: HEW Functional Requirement Discussions
Two Main Goals for HEW:
  Throughput improvements
  Efficiency improvements
Challenges for HEW Functional Requirements
  Relative throughput requirements
  Performance metrics reflecting efficiency improvement
  Performance Metrics focusing on user experience
  Diverse deployment environments
  A variety of applications
Two types of HEW Functional Requirements
  Straightforward, e.g.,
    compliance to the PAR, backward compatibility / coexistence to/with legacy devices, operation bands, etc.
  Challenging, e.g.,
    System performance requirements, efficiency improvements, etc.

## Slide 11: HEW Functional Requirements -- Straightforward
Operation band
  The TGax amendment shall define operations in frequency bands between 1 GHz and 6 GHz.
Backward compatibility with 802.11 Legacy Devices
  The TGax amendment shall enable backward compatibility with legacy IEEE 802.11 devices operating in the same band.
Coexistence with 802.11 Legacy Devices
  The TGax amendment shall enable coexistence with legacy IEEE 802.11 devices operating in the same band.
compliance to the PAR
  The TGax amendment shall comply with the PAR and the CSD.

## Slide 12: HEW Functional Requirements (FRs) – Need Discussions
Average throughput per station measured at MAC SAP
  The TGax amendment shall provide at least one mode of operation capable of achieving at least four times improvement in the average throughput per station (measured at the MAC data service access point), compared to the existing IEEE 802.11 standard and its amendments operating in the same band (IEEE 802.11n in 2.4 GHz and IEEE 802.11ac in 5 GHz) and in the same deployment scenario.
Discussions:
  Do we need any other performance measures in HEW FRs?
    the 5th percentile of per station throughput:
      Recommended, see next slide for details.
    area throughput:
      not recommended as a separate requirement, due to the average throughput per STA.
    packet delay:
      not recommended in HEW FRs, due to mainly belonging to application specific requirements.
    packet error ratio (PER):
      not recommended in HEW FRs, due to mainly belonging application specific requirements.

## Slide 13: HEW Functional Requirements (FRs) – Need Discussions -- con’t
the 5th percentile of per station throughput
  The TGax amendment shall provide a mechanism to improve the 5th percentile of per station throughput (measured at the MAC data service access point), compared to the existing IEEE 802.11 standard and its amendments operating in the same band (IEEE 802.11n in 2.4 GHz and IEEE 802.11ac in 5 GHz) and in the same deployment scenario.
Discussions:
  Should we quantify the improvement of the 5th percentile per station throughput?
  If so, the number, four times, also applies here?

## Slide 14: HEW Functional Requirements (FRs) – Need Discussions -- con’t
Improve WLAN efficiency
  The TGax amendment shall provide a mechanism to increase spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in scenarios with a high density of STAs per BSS or a high density of both STAs and BSSs.
  The TGax amendment shall provide a mechanism to increase robustness in outdoor propagation environments and uplink transmissions.
Discussions:
  Are these requirements clear and verifiable?
  Any overlapping with other requirements, e.g., dense deployment, outdoor deployment?

## Slide 15: HEW Functional Requirements (FRs) – Need Discussions -- con’t
Diverse Deployment Environment
  Dense Deployment
  The TGax amendment shall support at least one mode of operation that supports dense deployment environments characterized by the existence of a high density of STAs per BSS or a high density of both STAs and BSSs in geographically limited areas.
  Indoor / outdoor.
  The TGax amendment shall support at least one mode of operation that supports outdoor operations with stationary devices or devices at pedestrian speeds.
Discussions
  Do we need to quantify the definition of high density?
    Suggest to leave the details to the Simulation Scenario Descriptions.
  Do we need a specific requirement for indoor? Suggest not, as indoor is the default.
  Do we need a specific requirement for typical deployment environments, e.g., wireless corporate office, indoor and outdoor hotspot, dense residential apartments, and stadiums?
    Suggest not to include in the HEW FRs, leaving the details in Simulation Scenario Descriptions.

## Slide 16: HEW Functional Requirements (FRs) – Need Discussions -- con’t
Maintain or improve the power efficiency per station
  The TGax amendment shall maintain or improve the power efficiency per station as measured as average power consumption of device, compared to the existing IEEE 802.11 standard and its amendments operating in the same band (IEEE 802.11n in 2.4 GHz and IEEE 802.11ac in 5 GHz) and in the same deployment scenario.
Discussions:
  Do we need to mention battery-powered devices?
    Should focus on power efficiency improvements for the battery-powered devices.
  Do we need to further define the power consumption metrics?
    Keep the average power consumption per device as the main power consumption metric in the HEW FRs;
    Introduce additional metrics when needed, to the Simulation Scenario Descriptions.

## Slide 17: HEW Functional Requirements (FRs) – Need Discussions -- con’t
A variety of applications
  The TGax amendment shall provide a mechanism to improve the performance in delivering a variety of applications such as video, cloud access, broadcast/multicast, and offloading.
Discussions
  Is this requirement clear and verifiable?
    Focus on identifying the key applications for HEW based WLAN systems.
  Do we need to elaborate the specification of “performance”?
    Not needed in HEW FRs, and should we leave the details in the Simulation Scenario descriptions

## Slide 18: Discussions on HEW FR Documentation
Two options of HEW FR documentation
  As a separate document, i.e., HEW FRD (Functional Requirement Document)
  As a section in a combined doc for HEW FR and Simulation Scenario (SS) / Evaluation Methodology (EVM) document
Discussions
  HEW FRs are closely tied with deployment scenarios and applications whose details will be described in SS/EVM Doc;
  Leaving details in SS/EVM Doc could avoid duplication text;
  Option 2) above is recommended.

## Slide 19: References
11-14-0165-00-0hew-802-11-hew-sg-proposed-par
11-14-0169-00-0hew-ieee-802-11-hew-sg-proposed-csd
11-09-0451-16-00ac-tgac-functional-requirements-and-evaluation-methodology
11-03-0813-13-000n-functional-requirements