## Slide 1: Channel Models for different links in Simulations
Date: 2014-03-17
Authors:

## Slide 2: Abstract
System level Simulations require us to model channels for AP↔STA, STASTA, APAP links in both indoor and outdoor environments. While channel model for AP↔STA link are agreed, we do not have models specified for STASTA and APAP links. We propose path loss and shadowing models for outdoor STASTA links.

## Slide 3: Transmission Links in Simulations
Simulations, esp. System Level, require us to model different types of transmissions
Indoor: Scenarios 1, 2 & 3
Outdoor: Scenarios 4a & 4b
For each of these transmission links, we need to know models for path-loss, shadowing and short-term multi-path fading.
- AP↔STA, STA, AP links must be modeled.

## Slide 4: Current Status
 | Indoor |  |  | Outdoor |  | 
 | APSTA | STA | AP | APSTA | STA | AP
Path Loss |  | ? | ? |  | ? | ?
Shadowing |  | ? | ? |  | ? | ?
Multi-path fading |  | ? | ? |  | ? | ?
 | Indoor |  |  | Outdoor |  | 
Path Loss |  | ? | ? |  | ? | ?
Shadowing |  | ? | ? |  | ? | ?
Multi-path fading |  | ? | ? |  | ? | ?
Currently using TGn models in simulations
Currently using UMi models in simulations
Need clear assumptions for STASTA or AAP links in both indoor and outdoor environments
For STASTA or AAP links, path-loss and shadowing are definitely required to get accurate co-channel interference statistics while multi-path fading is necessary to model peer-to-peer transmissions.
This presentation focuses on outdoor STA STA links and provides alternatives models for path-loss and shadowing.

## Slide 5: Models for Outdoor
Outdoor: Scenarios 4a & 4b
APSTA
Path-loss, Shadow Fading and short-term multi-path fading well understood
  We agreed to use ITU Urban Micro(UMi) Model[6]
STASTA
UMi model has antenna height parameter in their equations that disallows usage for STA-STA links
Path-loss & Shadow Fading models are studied in literature[3]
Multi-path short-term fading not very well modeled
APAP
Models are not available for Path-loss, Shadow Fading and short-term fading
[3] provides models for path-loss and shadow fading for APs up to height 5m where as UMi assumes AP height of 10m
AP Height = 10m
STA Height = 1.5m

## Slide 6: Modeling outdoor STA-STA Path-Loss
For both 2GHz and 5GHz bands, path loss for outdoor STA-STA links can be modeled as [3]
Path-loss at reference distance of 1m
Attenuation Slope Exponent
Distance in meters
STA-STA | 2GHz |  | 5GHz | 
 | (dB) |  |  | 
NLOS | -62.01 | 5.86 | -51.22 | 5.82
LOS | -27.6 | 2 | -27.6 | 2
STA-STA | 2GHz |  | 5GHz | 
NLOS | -62.01 | 5.86 | -51.22 | 5.82
LOS | -27.6 | 2 | -27.6 | 2
Carrier Frequency (MHz)
Use free space path loss for LOS

## Slide 7: Outdoor STA-STA path loss comparison
The STA-STA path loss equation as defined in [3] is quite different from both UMi and IEEE Channel Model D.
[3] is backed by experimental evidence and a modification of the path loss equation is used in TG-ah[5]

## Slide 8: Outdoor STA-STA LOS probability
Links have an associated distance dependent LOS probability[3]
For
,

## Slide 9: Shadowing in outdoor STA-STA links
For both 2GHz and 5GHz bands, shadowing for outdoor STA-STA links can be modeled as log-normal distribution with standard deviation[3]
Tx- Rx distance
Max. Standard Deviation
Growth Distance Factor in meters
STA-STA | 2GHz |  | 5GHz | 
NLOS ( | 22.1 | 53 | 23.4 | 36
LOS ( | 2 | 53 | 2 | 36
STA-STA | 2GHz |  | 5GHz | 
 | 22.1 | 53 | 23.4 | 36
 | 2 | 53 | 2 | 36
[4] proposes a joint correlation model for shadowing between 2 STAs that can also be considered

## Slide 10: Multi-path Fading for Outdoor STA-STA links
Short term multi-path fading is not modeled in [3]
However, experiments in [3] have modeled Ricean K-factor for both LOS and N-LOS links
  For LOS links, the mean of the K-factor varies linearly with the distance
    For 2GHz – mean of K-factor = 15dB (with a distance related slope of 0.025)
    For 5GHz – mean of K-factor = 23dB (with a distance related slope of 0.035)
  For N-LOS, the K-factor is not 1, instead is log-normally distributed with mean and standard deviation as
    For 2GHz :
    For 5GHz :

## Slide 11: Recommended Parameters for outdoor STA-STA links
We propose that we use the following path loss and log normal shadowing parameters for outdoor STA-STA links
STA-STA | 2GHz |  | 5GHz | 
 | (dB) |  |  | 
NLOS | -62.01 | 5.86 | -51.22 | 5.82
LOS | -27.6 | 2 | -27.6 | 2
STA-STA | 2GHz |  | 5GHz | 
NLOS | -62.01 | 5.86 | -51.22 | 5.82
LOS | -27.6 | 2 | -27.6 | 2
STA-STA | 2GHz |  | 5GHz | 
NLOS ( | 22.1 | 53 | 23.4 | 36
LOS ( | 2 | 53 | 2 | 36
STA-STA | 2GHz |  | 5GHz | 
 | 22.1 | 53 | 23.4 | 36
 | 2 | 53 | 2 | 36
Path Loss
Shadowing

## Slide 12: Summary
 | Indoor |  |  | Outdoor |  | 
 | APSTA | STA | AP | APSTA | STA | AP
Path Loss |  | ? | ? |  |  | ?
Shadowing |  | ? | ? |  |  | ?
Multi-path fading |  | ? | ? |  | ? | ?
 | Indoor |  |  | Outdoor |  | 
Path Loss |  | ? | ? |  |  | ?
Shadowing |  | ? | ? |  |  | ?
Multi-path fading |  | ? | ? |  | ? | ?
This presentation presents Path loss and Shadow fading model with LOS Probability for outdoor STA-STA link.
Multipath fading for outdoor STA-STA link needs a reasonable model
Need models for AP-AP link in both indoor and outdoor environments or a common set of assumptions must be agreed
Continue using TGn models in simulations

## Slide 13: References
[1] 11-03-0940-04-000n-tgn-channel-models.doc
[2] Report ITU-R M.2135-1, Guidelines for evaluation of radio interface technologies for IMT-Advanced, Dec 2009
[3]Z. Wang, E. Tameh and A. Nix, Statistical Peer-to-Peer Models for outdoor urban environments at 2GHz and 5GHz, Proc. Of IEEE VTC, 2004
[4]Z. Wang, E. Tameh and A. Nix, “Joint Shadowing Process in Peer-to-Peer Radio Channels”, IEEE Transactions on Vehicular Technology, Vol. 57, No. 1, Jan 2008
[5] 11-11-0968-03-00ah-channel-model-text.docx
[6]11-13-1135-04-0hew-summary-on-hew-channel-models.pptx

## Slide 14: Appendix

## Slide 15: Outdoor AP-AP path loss model
Could use existing model with antenna height factor; also break point distance
According to the same reference, we’d like to propose for AP-AP path loss the following model (d: distance in meter, f: carrier frequency in MHz)
  PL_NLOS = -57.48 + 54.2 log10 (d) + 20 log10(f) (2GHz band)
  PL_NLOS = -48.71 + 54.4 log10 (d) + 20 log10(f) (5GHz band)
  PL_LOS = -27.6 + 20 log10(d) + 20 log10(f)
However, it is only validated for 5m antenna height; HEW simulation scenario assumes 10m antenna height

## Slide 16: AP-AP path loss model comparison