## Slide 1: Suggestion on PHY Abstraction for Evaluation Methodology
Date: 2014-03-16
Authors:

## Slide 2: Introduction
As stated in evaluation methodology document [1], PHY abstraction method is used to accurately predict packet error rate (PER) in a computationally efficient way to enable running system simulations in a timely manner
In [2], we presented an overview and performance of mean mutual information per bit (MMIB) PHY abstraction method for BPSK, QPSK, 16QAM and 64QAM modulation
In this contribution, we further provide MMIB method for 256QAM modulation
Moreover, we introduce SINR per tone calculation considering channel estimation error

## Slide 3: MMIB-based PHY abstraction method for 256 QAM

## Slide 4: Recap: PHY Abstraction Method
Effective SINR (SINReff ) can be calculated as follows
where SINRn is the post processing SINR at the n-th subcarrier, N is the number of symbols for a coded block or the number of data subcarriers used in an OFDM system, and Φ is Effective SINR Mapping (ESM) function
For the MMIB method, ESM function is derived for each modulation as follows (details in [3])
(Eq. 1)

## Slide 5: Proposed MMIB 256QAM Extension (1/2)
Need to find coefficients (ak and ck) to match Mutual Information of 256QAM modulation
  Approximation using sum of basis function J(∙) using curve fitting method considering all SNRs region
  Note that there exists a problem for large input x in function J(∙), and this is critical problem for higher order modulation due to high operating range
    Thus, we modify the valid range of input parameter x of J(∙) function
Chart: 256QAM
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30
Simulation | 0.0985 | 0.14326 | 0.1905 | 0.24243 | 0.29577 | 0.37104 | 0.44072 | 0.52561 | 0.60668 | 0.69312 | 0.77353 | 0.8475 | 0.92183 | 0.97674 | 0.99313 | 1
Approximation | 0.08796 | 0.12397 | 0.17057 | 0.22872 | 0.29815 | 0.37465 | 0.45066 | 0.52154 | 0.59252 | 0.67313 | 0.7654 | 0.85867 | 0.93497 | 0.9802 | 0.99678 | 0.9998

## Slide 6: Proposed MMIB 256QAM Extension (2/2)
Numerical approximation for MMIB mapping (Proposed change is noted as red color)
Modulation | Numerical Approximation
BPSK | K=1, a = [1], c = [2√2]
QPSK | K=1, a = [1], c = [2]
16-QAM | K=3, a = [0.5 0.25 0.25], c = [0.8 2.17 0.965]
64-QAM | K=3, a = [1/3 1/3 1/3], c = [1.47 0.529 0.366]
256-QAM | K=3, a = [0.6 0.36 0.04], c = [0.24 0.96 2.76]

## Slide 7: Performance of MMIB PHY Abstraction (20MHz, Convolutional Code)
TGac channel D-NLOS, 2 OFDM symbol
MCS8

## Slide 8: Performance of MMIB PHY Abstraction (20MHz, Convolutional Code)
TGac channel B-NLOS, 2 OFDM symbol
MCS8

## Slide 9: Performance of MMIB PHY Abstraction (40MHz, Convolutional Code)
TGac channel D-NLOS, 2 OFDM symbol
MCS8
MCS9

## Slide 10: Performance of MMIB PHY Abstraction (40MHz, Convolutional Code)
TGac channel B-NLOS, 2 OFDM symbol
MCS8
MCS9

## Slide 11: Channel estimation error compensation method for PHY abstraction

## Slide 12: Impact of Channel Estimation Error (1/3)
In order to calculate effective SINR (SINReff ), we need to calculate per tone SINR, i.e. SINRn in Eq. 1 of slide 4.
For example, in case of SISO, we can calculate SINRn as follows
  y= hx+n
    where y is a received signal
    h is channel response at each subcarrier
    x is a transmitted signal
    n is a noise
  Then, SINRn can be calculated as
    where ɛx is a signal strength
    σn2 is noise variance
However, if there exists channel estimation error, we need to modify per tone SINR calculation

## Slide 13: Impact of Channel Estimation Error (2/3)
20MHz, TGac channel D-NLOS, 2 OFDM symbol
Red solid line: AWGN Performance
Blue circle line: MMIB PHY abstraction method with perfect channel estimation
Green plus line: MMIB PHY abstraction method with LS channel estimator without channel estimation error compensation

## Slide 14: Impact of Channel Estimation Error (3/3)
20MHz, TGac channel B-NLOS, 2 OFDM symbol
Red solid line: AWGN Performance
Blue circle line: MMIB PHY abstraction method with perfect channel estimation
Green plus line: MMIB PHY abstraction method with LS channel estimator without channel estimation error compensation

## Slide 15: Proposed Channel Estimation Error Compensation Method (1/3)
In case of SISO, channel estimation error can be represented as an additional noise term
  The additional noise term is uncorrelated with the signal
Then, the per tone SINR for SISO is given by
    Where, ɛx is a signal strength
    is a noise variance of estimation without bias correlation
    is a additive noise variance
Signal loss term
Additional noise term

## Slide 16: Proposed Channel Estimation Error Compensation Method (2/3)
20MHz, TGac channel D-NLOS, 2 OFDM symbol
Red solid line: AWGN Performance
Blue circle line: MMIB PHY abstraction method with perfect channel estimation
Green plus line: MMIB PHY abstraction method with LS channel estimator with channel estimation error compensation
Cyan triangle line: MMIB PHY abstraction method with MMSE channel estimator with channel estimation error compensation

## Slide 17: Proposed Channel Estimation Error Compensation Method (3/3)
20MHz, TGac channel B-NLOS, 2 OFDM symbol
Red solid line: AWGN Performance
Blue circle line: MMIB PHY abstraction method with perfect channel estimation
Green plus line: MMIB PHY abstraction method with LS channel estimator with channel estimation error compensation
Cyan triangle line: MMIB PHY abstraction method with MMSE channel estimator with channel estimation error compensation

## Slide 18: Conclusion
We provided MMIB PHY abstraction method for 256QAM modulation
We introduced channel estimation error compensation method for PHY abstraction
  Note that the channel estimation error compensation method can be used for any PHY abstraction method

## Slide 19: Straw Poll
Do you support to include SINR calculation method considering channel estimation error in slide 15 as a part of PHY abstraction method in evaluation methodology document [1]?
In Favor:
Opposed:
Abstain:

## Slide 20: Reference
[1] IEEE 802. 11-13-1359, “HEW Evaluation Methodology ”
[2] IEEE 802.11-13/1059, “PHY Abstraction for HEW Evaluation Methodology ”
[3] IEEE 802.16m-08/004r5, “IEEE 802.16m Evaluation Methodology Document (EMD)”
[4] “Robust MMSE channel estimation in OFDM systems with practical timing synchronization” , WCNC IEEE, pp. 711 - 716 Vol.2 , 2004

## Slide 21: Appendix

## Slide 22: Simulation Parameters
Basic parameters
Frequency band | 2.4 GHz
Band Width | 20/40 MHz
FFT Size | 64/128
Channel Model | AWGN, TGac B/D
Channel condition | NLOS
Channel Estimation | Perfect, LS, MMSE
PHY Abstraction method | MMIB
Data size | 2 OFDM symbol

## Slide 23: Channel estimation [4]
LS estimation
MMSE estimation
Dongguk Lim, LG Electronics
P is N x N matrix with L nonzero elements which are along its principal diagonal
and are equal to the L elements of the channel Power delay Profile(PDP)
W is N x N DFT matrix defined as

## Slide 24: Mean Square Error
TGac Channel B

## Slide 25: Mean Square Error
TGac Channel D