## Slide 1: Calibration of System Level Simulators
Date: 2014-03-17
Authors:

## Slide 2: Outline
Abstract
Simulated Scenario
Results
  SINR
  Throughput
  Number of concurrent transmissions
Reference
Conclusions
Appendix

## Slide 3: Abstract
Simulation calibration verifies that simulators generate the same results on the same simulation scenario
  Calibration improves simulations reliability
The presentation introduces the most important calibration metrics [2]
  A new calibration metric is proposed
The presentation shows the calibration results for HEW scenario 1 [1]
  Scenario 1 is simplified to add understandability to the results

## Slide 4
Same parameters as in [1]
  5 floors building with 20 rooms (10x10x3) per each floor
  One AP per each room, x and y randomly chosen, z=1.5
  Wall loss: 12 dB
  Floor loss: 17dB + 4dB per floor
  TX Power: STA= 17dBm; AP= 23dBm;
Another parameters:
  TGn/TGac channel model C
  80 MHz bandwidth
  The same primary channel
  Full buffer traffic model
  Static MCS: 64QAM 5/6
Scenario and Parameters

## Slide 5
Number of STAs per scenario: 50, 100, 200, 400, 800
The STAs are randomly distributed over the building
STAs Drop Parameters
Figure A shows the average amount of STAs per one AP
Figure B shows the CDF of instantaneous number of STAs per one AP
A)
B)

## Slide 6
The presentation explains and shows results to following metrics:
  SINR
  Throughput
  Number of concurrent transmissions
The results are presented for the following parameters:
  FastFading: On/Off
  RtsCts: On/Off
  Traffic: DL/UL
  Number of concurrent STAs: 50, 100, 200, 400, 800
Simulation Results

## Slide 7
SINR metric is presented in Scalar and CDF form, where scalar figures show the average numbers over the whole simulation time
The SINR samples are collected from data PPDUs and one sample presents an average SINR over one MPDU
The SINR figures show the instantaneous SINR results for simulation with Fast Fading
In the simulations without Fast Fading the instantaneous SINR is equal to the long term SINR
SINR Statistics

## Slide 8
SINR
RTS CTS has big effect on SINR
The SINR in UL is probably lower due to the lower transmission power and more close-by interferers

## Slide 9
SINR
These figures show the CDF of SINR per MPDU containing user data
Left and right figures show SINR performance for 50 and 800 STAs respectively
It can be seen that the SINR difference between these figures is not big; thus SINR for other number of STAs is not showed

## Slide 10
Throughput metric is presented in scalar and CDF form, where scalar figures will show the average throughput over whole simulation time
In addition three throughput statistics are presented
  Throughput per call, which shows the average throughput over a call
  Total system/scenario throughput
  Throughput per AP
Throughput Statistics

## Slide 11
Throughput Statistics
Throughput statistics show the result of multiple features operation:
  Link adaptation and link performance
  Channel access and offered traffic load
Link adaptation is a key to good throuhgput
  Link adaptation mechanism should be discussed in IEEE
The results are created with constant MCS 64QAM 5/6
  Appendix1 describes a link adaptation principle and shows results with the link adaptation

## Slide 12
Total System/Scenario Throughput
  MCS 64QAM 5/6
The SINR and concurrent transmissions statistics are made for static MCS. Only throughput statistics with OLLA are provided
With OLLA
As explained in Appendix 1

## Slide 13: Throughput results
The fast fading has big impact on the throughput results
Link adaptation is required to adjust the transmissions to the interference level
  The constant MCS performs poorly especially when the number of concurrent transmissions gets high
Throughput with RTS CTS is similar with or without link adaptation performance
  RTS CTS reduces interference and limits the number of simultaneous transmissions in the BSS

## Slide 14
Average Throughput per Call
Figure in left shows DL throughput per call in Mbps
Figure in right shows UL throughput per call in Mbps
  Static MCS 64QAM 5/6 in use
A)
B)

## Slide 15
CDF of Throughput per Call
  MCS 64QAM 5/6

## Slide 16
CDF of Throughput per AP
  MCS 64QAM 5/6

## Slide 17
Number of Concurrent Transmissions Statistics
The number of concurrent transmissions statistics shows the number of transmitting devices at the same symbol
  This metric does not show the number of successful transmissions
The number of concurrent transmissions indicates the level of channel reuse
  The physical and virtual carrier sensing affect to the number of simultaneous transmissions
  EDCA parameters, number of competing STAs and traffic amount affect to the number of simultaneous transmissions
The number concurrent transmissions affects to the interference level

## Slide 18
Number of Concurrent Transmissions
When RTS CTS is not used, in UL the number of simultaneously transmitting STAs increases as a function of number of STAs
RTS CTS eliminates some simultaneous transmissions and makes the number of simultaneous transmissions constant

## Slide 19
Number of Concurrent Transmissions

## Slide 20
The presentation shows the calibration results for HEW scenario 1
Number of concurrent transmissions metric is proposed to calibration results
  The metric measures channel reuse
The calibration results verify the correct operation of the system level simulator
  The simulator implementation details may differ
Conclusions

## Slide 21: References
[1] 11-13-1051-01-0hew-evaluation-methodology
[2] 11-14-0053-00-0hew-further-consideration-on-calibration of system level simulation

## Slide 22: Appendix 1: Link Adaptation Algorithm
Link adaptation consists of inner-loop (ILLA) and outer-loop (OLLA) link adaptation functions
  ILLA assesses the RSSI of the link and selects the best MCS based on the RSSI thresholds
  OLLA counts the number of ACKs and NACKs and then tunes the MCS selected by the ILLA up or down
The target of OLLA is to select the MCS so that the MPDU failure rate is tuned to 5%
OLLA parameters were not optimized for the scenario and better performance could be gotten by doing that

## Slide 23
These figures shows the MPDU failure rate per user in %
Left figure shows results for simulation with static MCS (64QAM 5/6)
Right figure shows results with OLLA
  OLLA is used in all simulations presented in the next slides. In these simulations OLLA affects to the throughput results
Appendix 1: Link Adaptation versus static MCS

## Slide 24
Appendix 1: OLLA
Total System/Scenario Throughput

## Slide 25
Appendix 1: OLLA
Average Throughput per Call
Figure in left shows DL throughput per call in Mbps
Figure in right shows UL throughput per call in Mbps
A)
B)

## Slide 26
Appendix 1: OLLA
CDF of Throughput per Call

## Slide 27
Appendix 1: OLLA
CDF of Throughput per AP

## Slide 28
Full buffer traffic model is used in simulations
Each call creates traffic for 1 second
After 1 second the traffic generation is stopped. The STA empties its transmission buffer. When the buffer is empty the call is terminated
The figure in right hand side shows the mean STA lifetime in seconds [s]
When a STA finishes its call, another STA is created to a new random place
Separate simulations for DL and UL traffic
  Interpretation of the results is much more easier in this way
Appendix 2: Traffic Parameters

## Slide 29
Appendix 3: Numerical Results of One Parameter Set
 |  | SINR, dB |  |  | Throughput per Call, Mbps |  |  | Throughput per AP, Mbps |  |  | Transmissions |  | System throughput, Mbps
Simulation case | 5% | 50% | 95% | 5% | 50% | 95% | 5% | 50% | 95% | 5% | 50% | 95% | 
DL, FF, RtsCts, 50 | 16.7 | 30.84 | 46.15 | 3.36 | 31.86 | 98.02 | 5.85 | 18.2 | 32 | 10 | 14 | 18 | 1880.74
DL, FF, RtsCts, 100 | 15.53 | 29.1 | 43.95 | 1.34 | 14.87 | 56.38 | 6 | 17.2 | 34.8 | 13 | 17 | 21 | 1880.27
DL, FF, RtsCts, 200 | 14.74 | 28.21 | 42.78 | 0.44 | 7.06 | 33.26 | 6.4 | 17.1 | 34.95 | 14 | 18 | 23 | 1870.33
DL, FF, RtsCts, 400 | 14.06 | 27.48 | 41.79 | 0.14 | 3.5 | 19.34 | 6.45 | 16.85 | 34.8 | 15 | 20 | 24 | 1845.77
DL, FF, RtsCts, 800 | 14.09 | 27.14 | 41.34 | 0.02 | 1.74 | 10.03 | 6.5 | 16.95 | 36.1 | 16 | 21 | 25 | 1889.79
UL, FF, RtsCts, 50 | 14.45 | 28.98 | 43.46 | 1.87 | 30.75 | 102.52 | 6.65 | 17.25 | 33.3 | 11 | 15 | 19 | 1841.97
UL, FF, RtsCts, 100 | 13.21 | 27.31 | 41.83 | 0.63 | 13.5 | 55.96 | 6.65 | 16.7 | 35.25 | 14 | 18 | 22 | 1804.8
UL, FF, RtsCts, 200 | 12.39 | 26.36 | 41.21 | 0.18 | 6.26 | 30.88 | 4.8 | 15.6 | 31.7 | 15 | 19 | 24 | 1720.46
UL, FF, RtsCts, 400 | 11.76 | 25.71 | 40.69 | 0.06 | 2.9 | 17.02 | 5.05 | 14.65 | 34.4 | 15 | 20 | 25 | 1600.77
UL, FF, RtsCts, 800 | 11.8 | 25.54 | 40.57 | 0 | 1.3 | 8.76 | 4.25 | 14.2 | 32.1 | 15 | 21 | 26 | 1541.72
DL, UL – Downlink, Uplink, FF – Fading ON, RtsCts – RTS CTS applied, Fixed MCS – 64QAM 5/6
50, 100, 200, 400, 800 – number of STAs in simulation