## Slide 1: Considerations on evaluation methodology for candidate HEW PHY&MAC techniques
Date: 2014-03
Authors:
Name | Affiliations | Address | Phone | Email
Le Liu | Huawei Technologies Co., Ltd. | F1-17, Bantian Huawei, Shenzhen, China |  | liule@huawei.com
 |  |  |  | roy.luoyi@huawei.com
Roy Luo |  |  |  | 
David Xun Yang |  |  |  | david.yangxun@huawei.com
Chixiang Ma |  | No. 2222, Xin Jinqiao Rd. Pudong, Shanghai, China |  | machixiang@huawei.com
Rossi Jun Luo |  |  |  | jun.l@huawei.com
Zhang Jiayin |  |  |  | zhangjiayin@huawei.com
Phillip Barber |  |  |  | 
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa clara, CA 95054 |  | 
Yan Zhang |  |  |  | 

## Slide 2: Abstract
Comparison between standalone and integrated system level simulation (SLS) shows that integrated SLS is more comprehensive and provides stronger insights to investigate and evaluate candidate PHY&MAC techniques for HEW system and HEW scenarios.

## Slide 3: Background
Following SLS evaluation methodologies are proposed to evaluate multi-BSS performance:
  PHY SLS [1]
    Accurate modeling of PHY
      e.g., channel model, MIMO configuration, SU OL/BF, MU.
    Simplified MAC
      e.g., random AP/STA transmission, CCA
  MAC SLS [1]
    Simplified PHY
      e.g., SISO over AWGN
    Accurate modeling of MAC
      e.g., CSMA/CA, aggregation policy, usage of RTS/CTS/CTS-to-self, configuration of EDCA parameters, use of beacon and management frames.
  Integrated SLS [2]
    Accurate modeling of PHY
    Accurate modeling of MAC
    Accurate traffic modeling, e.g. FTP, HTTP, video, gaming, VDI …

## Slide 4: Candidate PHY&MAC Techniques for HEW
As pointed out in PAR discussion [3], this project may include the capability to handle multiple simultaneous communications in both the spatial and frequency domains, in both UL and DL direction.
Candidate PHY&MAC techniques
  OFDMA
  UL MU-MIMO
  Interference management
  Channel bonding
  …
 In the following, we take some candidate PHY&MAC techniques as examples to compare EM.

## Slide 5: SLS for OFDMA
For UL/DL OFDMA, to efficiently allocate limited number of subbands to a large quantity of STAs/APs may need to consider
  Scheduling granularity
  Frequency selective channel
  User fairness
  Traffic load
  Device type: legacy or not
  Impact of Transmission opportunity
However,
  Based on PHY SLS, simple MAC only supports resource allocation for random selected STAs/APs  not realistic inter-cell interference with OFDMA scheduling for variable traffic load
  Based on MAC SLS, simple PHY cannot take into account the time/freq. fading channel  not realistic instantaneous signal/interference.
 Integrated SLS is necessary to investigate the achievable performance gain of OFDMA.

## Slide 6: SLS for UL MU-MIMO
For UL MU-MIMO, similar with DL MU-MIMO, scheduling for user grouping should consider
  Precoding vector selection for user grouping to maximize throughput
  Traffic load and packet size for non-full buffer traffic
  Signaling overhead for grouped users
  Impact of Transmission opportunity
However,
  Based on PHY SLS, simple MAC only supports user grouping from random selected STAs/APs  not realistic interference for user grouping with variable traffic.
  Based on MAC SLS, simple PHY cannot take into account the MIMO fading channel  not realistic instantaneous signal/interference for user grouping.
 Integrated SLS is necessary to investigate the achievable performance gain of UL MU-MIMO.

## Slide 7: SLS for Interference management
Interference management is applied to avoid significant inter-cell interference among dense APs/STAs in OBSS.
  Frequency reuse management
  Load/traffic balancing
  Coordinated transmission
However,
  Based on PHY SLS, simple MAC only supports inter-cell interference with simple interference coordination (e.g., CCA) not realistic inter-cell interference after complicated coordination.
  Based on MAC SLS, simple PHY cannot take into account the time/freq. fading channel and MIMO channel  not realistic instantaneous signal/interference.
 Integrated SLS is necessary to investigate the achievable performance gain of Interference management.

## Slide 8: SLS for Channel Bonding
Channel bonding is supported in 802.11ac to efficiently extend the frequency spectrum.
  Load/traffic adaptation
  MAC layer mechanism for channel selection
  Control signaling overhead
However,
  Based on PHY SLS, simple MAC only supports bandwidth extension without considering realistic MAC layer control  not realistic MAC layer mechanism for channel selection.
  Based on MAC SLS, simple PHY cannot take into account the time/freq. fading channel and adjacent channel interference  not realistic multi-channel instantaneous signal/interference.
 Integrated SLS is necessary to investigate the achievable performance of Channel bonding.

## Slide 9: Integrated vs. Standalone SLS
Candidate techniques | Standalone SLS |  | Integrated SLS
 | PHY SLS | MAC SLS | 
OFDMA | resource allocation for random selected STAs/APs | not realistic instantaneous signal/interference | realistic inter-cell interference with OFDMA scheduling for variable traffic load; realistic instantaneous signal/interference
UL MU-MIMO | user grouping from random selected STAs/APs | not realistic instantaneous signal/interference for user grouping | Realistic interference with user grouping; realistic instantaneous signal/interference for user grouping
Interference management | inter-cell interference with simple coordination | not realistic instantaneous signal/interference | realistic inter-cell interference after coordination; realistic instantaneous signal/interference
Channel bonding | simple band extension without complicated MAC layer control | no modeling of multi-channel instantaneous signal/interference | realistic MAC layer mechanism; realistic multi-channel instantaneous signal/interference

## Slide 10: Example of 802.11n Evaluation
In [5], user throughput considering MAC overhead is given as a non-linear function of PHY rate.
  PHY SLS is difficult to consider MAC overhead and impact of MAC scheme.
  MAC SLS is difficult to provide achievable rate for different MIMO channel.
   System-wise throughput should be evaluated by using integrated SLS.
TXOP
BW
MIMO

## Slide 11: Our Recommendation
Integrated SLS is recommended to evaluate to achievable system-wise performance gain of candidate PHY&MAC techniques for HEW.

## Slide 12: Summary
Compared with standalone SLS, integrated SLS is more comprehensive and provides stronger insights to investigate and evaluate candidate PHY&MAC techniques for HEW system and HEW scenarios.

## Slide 13: Reference
[1] 11-13-1051-01-0hew-evaluation-methodology
[2] 11-14-0059-01-0hew-integrated-system-level-simulation
[3] 11-14-0165-01-0hew-802-11-hew-draft-par-and-5c
[4] 11-13-1421-01-0hew-str-radios-and-str-media-access
[5] 11-07-2431-00-0vht-analysis-on-ieee-802-11n-mac-efficiency