## Slide 1: Simulation Methodolgy and Calibration
Date: 2014-03-14
Authors:

## Slide 2: Introduction
Evaluation Methodology document defines multiple simulators
  MAC systems: With a simplified PHY and detailed MAC
  PHY system: With a simplified MAC and detailed PHY
  Integrated [in 1359r1]: With detailed MAC and PHY
  PER simulator
The definition of integrated simulator [1359r1] includes
  MAC simulation accuracy based on event driven approach, and initial features
  PHY abstraction which includes advanced PHY features (MIMO, BF etc…)
The definition of MAC simulator is unclear/TBD
  PHY abstraction not well defined and may be too simplistic
    “The PHY parameters can be simplified to a SISO configuration running over AWGN - path and penetration loss should be modeled according to the scenario-specific definition.” [1359r0]
    “MAC system simulation is an integrated system simulation stripped out of the details of PHY modelling, e.g. a SISO configuration with AWGN - path loss and penetration loss should be modeled according to the scenario-specific definition.” [1359r1]
  MAC simulation accuracy same as the integrated simulator [1359r1]
In order to proceed with the calibration, we suggest some clarifications on the MAC/Integrated simulators definitions

## Slide 3: Proposals in this presentation
We suggest to merge the definition of MAC and Integrated simulators and e.g. keep the name ‘Integrated’
Within the Integrated sim, define multiple levels of PHY and MAC features to be the target for development and calibration steps
  “Phase I” PHY (SISO, flat channel)
  “Phase II” PHY (SISO, multipath channel)
  “Phase I” MAC (minimal essential MAC features)
  “Phase II” MAC (more advanced MAC features)
  The definition of Phases is helpful in identifying common milestones in the development process across companies and facilitates the comparison and calibration across simulators
Define calibration steps according to the defined phases
  Define a sequence of tests per each PHY and MAC phase

## Slide 4: PHY Abstractions for Integrated Simulator
Phase I: (minimum requirement for Integrated simulator)
  SISO channel with propagation modeled by path loss, wall loss and shadowing only (‘narrowband model’)
  SINR computed with interference from all the sources
    Interference recalculated at each “interference event” (e.g. may be multiple in a MPDU)
  SINR to PER Mapping
    Map SINR on PER curve for the selected MCS and determine loss probability of each MPDU
    PER abstraction: use long term SINR-> PER curves mapping (1x1)
    PER curves to be used: according to the channel model indicated by the test scenario (e.g. Channel D)
Phase II:
  Phase 1 features, with the following differences:
  Fading channel model (w/o doppler)
  PER abstraction: Effective SINR vs PER mapping curves (1x1)
    See separate presentation [2]
Additional phases TBD
  MIMO
  BF, …

## Slide 5: MAC Features for Integrated Simulator
Phase I: (minimum requirement - to be modeled as per IEEE specs)
  Backoff procedure with EDCA
  Deferral according to Packet Detection and Energy Detection
  All overheads
    MAC header, FCS, LLC/SNAP, TCP/IP
  A-MPDU aggregation
  RTS/CTS
  BA
  Rate selection TBD
Phase II: Additional features
  A-MSDU aggregation, BAR
  BF, MU-MIMO
Note: EM document should define the required features and the accuracy of modeling, not the way features are to be coded in the simulator

## Slide 6: Initial Calibration Plan
Test for Phase I MAC features : Start with simple MAC calibration tests where PHY abstraction is largely irrelevant
  E.g. two nodes at short distance such that PER is negligible.
  E.g. Multiple nodes at distances such that collisions will cause packet failure with very high probability
Test for Phase I PHY features
  Calibration tests with MAC “disabled”: calibrate the PHY abstraction
    MAC “disabled” assumes no deferral and no backoff (reuse-one);
    The goal is to calibrate the SINRs. MAC overheads need not be modeled
Test for Phase I PHY and Phase I MAC features combined
  Simple Calibration tests with MAC functionalities
  Calibration of Simulation Scenarios with Phase I PHY
    E.g. run the Residential scenario with default parameters (TBD)
Tests for Phase II MAC features … Tests for Phase II PHY ….

## Slide 7: Initial Calibration Plan
Calibration tests scenarios
  Define, in SS / EM docs, new simple scenarios to be used per each phase
  Define default parameters in each Simulation Scenarios (1-4), to be used for more comprehensive calibration
    E.g. see doc XXXX
Metrics for the calibration
  PHY: CDF of SINR
  MAC: TPUT
    Use application layer Tput
  Other metrics for debugging
    Ex: PER log, event traces, etc.

## Slide 8: Conclusions
MAC system simulator is vaguely described in EM
The calibration procedure is undefined
We propose to unify the description of MAC and Integrated simulator and define a phased approach for the development and calibration
  See doc 14/387 for related proposed changes in the EM document
  See doc 14/355 for related proposed changes in the SS document
We propose a plan for the calibration tests