## Slide 1: Traffic Separation Scheme for Optimizing WLANs using PHY and MAC options
Date: 2014-03-20
Authors:

## Slide 2: Problem statement
Lots of PHY and MAC techniques enhancing WLAN performance are available.
It is up to traffic condition in a channel whether the techniques increase or decrease the WLAN performance.
RTS/CTS
Channel Bonding
It is difficult for WLAN operator to select optimal WLAN options such as RTS/CTS, Channel aggregation etc..

## Slide 3: WLAN traffics
High contention
Large number of WLANs including smartphone tethering and Lots of WLAN devices including sensors
Busty traffic of short frames Smartphone applications and sensing devices generate huge number of very short data frames.
Large Volume Multimedia Traffic
Such as photos and video streaming, which are transmitted via TCP flow

## Slide 4: Objective
Leveraging dual WLAN interfaces enables nodes to separate their traffic in order to make traffic conditions where WLAN options always work well.
Mixed traffic
It dynamically changes
Conventional
Proposed
Uniform and stable traffic
Mixed and dynamic traffic
The channel is easy to optimize with the WLAN options

## Slide 5: Traffic Separation Policy
Channel 1: Contention Less
Channel 2: Other
Traffic
TCP traffic
Downlink UDP traffic
Traffic
Uplink UDP traffic
Other Uplink traffics
Options
Effective options for uncongested WLAN
Frame aggregation
Channel bonding
Short GI
Options
Other effective options for congested WLAN
RTS/CTS
RandomAIFSN [1]
[1] OGAWA, K., et.al. (2013). IEEE 802.11ah Based M2M Networks Employing Virtual Grouping and Power Saving Methods. IEICE Trans. on Comm., E96.B(12), 2976–2985.

## Slide 6: Performance evaluation (1/2)
Conventional
Proposed scheme
40MHz channel
20MHz channel x 2
IEEE 802.11n WLAN
Auto Rate Fallback: Enable
All the STAs use TCP downlink flow
Some of the STAs use UDP flow
Num. of STAs: 15

## Slide 7: Performance evaluation (2/2)
Chart: 
| 15 | 12 | 10 | 7 | 5 | 3
Conventional (RTS/CTS enable) | 189512.746 | 219312.7166 | 241088.4972 | 289809.9829 | 337613.4663 | 429489.7073
Conventional (RTS/CTS disable) | 218359.3514 | 252264.8086 | 279282.2637 | 311712.8212 | 358361.89 | 430218.3338
 | 518508.974 | 589428.4041 | 648738.3685 | 766123.7621 | 870236.3123 | 1013047.0196
 | 466756.4352 | 528139.4295 | 579223.2225 | 679742.0044 | 769081.7067 | 887235.9419
Number of STAs using UDP uplink flow in each channel
Average throughput of STAs
Proposed scheme
Conventional
RTS/CTS enable
RTS/CTS disable

## Slide 8: Conclusion
We proposed the traffic separation scheme which enables WLANs to coordinate traffic so that WLAN options increase the system throughput efficiently.
The advantages of the scheme
It is applicable for lots of WLAN options.
Easy implementation
It can be used for several usage scenario such as minimizing delay, prioritizing real time application etc..
The present study was supported by the Strategic Information and Communications R&D Promotion Programme (SCOPE) of the Ministry of Internal Affairs and Communications, Japan.

## Slide 9: WLAN traffics
High contention
Large number of WLANs including smartphone tethering and Lots of WLAN devices including sensors compete
Busty traffic of short frames Smartphone applications and sensing devices generate huge number of very short data frames.

## Slide 10: WLAN traffics
High contention
Large number of WLANs including smartphone tethering and Lots of WLAN devices including sensors compete
Busty traffic of short frames Smartphone applications and sensing devices generate huge number of very short data frames.

## Slide 11: Traffic Separation