## Slide 1: Small-Scale Characteristics of 45 GHz Based on Channel Measurement
Authors/contributors:
Date: March 19, 2014
Presenter: Haiming WANG
Name | Company | Address | Phone | Email
Haiming WANG | SEU/CWPAN | 2 Sipailou, Nanjing 210096, China | +86-25-5209 1653-301(ext.) | hmwang@seu.edu.cn
Jin ZHU |  |  |  | jinzhu@emfield.org
Wei HONG |  |  | +86-25-5209 1650 | weihong@seu.edu.cn
Nianzu ZHANG |  |  | +86-25-5209 1653-320(ext.) | nzzhang@seu.edu.cn
Shiwen HE |  |  | +86-25-5209 1653-3121(ext.) | hesw01@seu.edu.cn

## Slide 2: Abstract
This presentation gives small-scale characteristics of 45 GHz band based on channel measurement.

## Slide 3: Outline
Channel Measurement Scheme
  Transmission Scenarios
  Channel measurement setup
Small-Scale Characteristics at 45 GHz band
  Number of clusters and rays
  Power delay profile
  Angle of arrival and departure
  Time of arrival

## Slide 4: Transmission Scenarios
Conference room
Cubicle room
Living room

## Slide 5: Conference Room Scenario Setup
Tx height: 1.95m
Rx height: 1.00m
Fixed Tx position and 4 Rx positions
Tx height: 10 dBm
Freq center: 44.955GHz
Sampling frequency: 660 MHz
Number of Subcarriers: 256

## Slide 6: Channel Measurement Setup
A PC is used to not only control the rotary table with an RS-232 port but also control the signal generator and vector network analyzer (VNA) with LAN ports.
The signal generator transmits CW signal at each frequency, then Rx power and channel frequency response are obtained by the VNA. The positions of Tx and Rx antennas and measured data are simultaneously recorded.

## Slide 7: Antennas for Channel Measurement
Type II: Open-ended waveguide (OEW) antenna with 6-dBi gain
Type I: Horn antenna with 23.7-dBi gain
Angle (degree)
Pattern (dB)
H-Plane
E-Plane

## Slide 8: Antennas for Channel Measurement
Gain
Angle (deg)
Angle (deg)
Gain
Maximum Gain
Maximum Gain
Gain
Type Ⅲ: SIW antenna with 3-dBi gain
Three antennas are linear polarized

## Slide 9: Channel Measurement Technique
Frequency domain measurement
Complex response is recorded in the frequency domain
Channel impulse response is obtained from channel frequency response using IFFT

## Slide 10: Double-directional Scanning
Horn-Horn:
Tx antenna rotates at each 10 degrees, Rx antenna rotates at each 10 degrees
OEW-OEW:
Tx antenna rotates at each 60 degrees, Rx antenna rotates at each 60 degrees

## Slide 11: The Channel Impulse Response Function
and are the gain and channel impulse response of the ith cluster respectively;
Amplitude, delay and angle characteristics of clusters as well as rays can be derived from massive channel measurements.

## Slide 12: Power Angle Profile (PAP)

## Slide 13: PAP at Rx 1 Position
(a) Average power of each angle
(b) Delay of each angle
Sub-paths whose average power 20dB less than the max path power are ignored
Power of each sub-path is the expectation of powers of 256 sub-carriers

## Slide 14: PAP at Rx2 Position
(c) Average power of each angle
(d) Delay of each angle
Sub-paths whose average power 20dB less than the max path power are ignored
Power of each sub-path is the expectation of powers of 256 sub-carriers

## Slide 15: PAP at Rx 3 Position
(e) Average power of each angle
(f) Delay of each angle

## Slide 16: PAP at Rx 4 Position
(g) Average power of each angle
(h) Delay of each angle
Rx2

## Slide 17: Discussion
Amount to 36×36 (1296) sub-channels are measured to analyze the spatial characteristics of clusters.
The left illustration shows the average power of each path, the right illustration shows the corresponding delays of all paths.
Clustering is obvious and there are about 6 or more clusters .
Cluster with larger power usually has smaller time delay.

## Slide 18: Power Delay Profile (PDP)

## Slide 19: PDP of Horn-Horn
Rx1
Rx2
Rx3
Rx4

## Slide 20: PDP of OEW-OEW
Rx1
Rx2
Rx3
Rx4

## Slide 21: Discussion
There is no LoS path component in the horn scanning setup for a misalignment of TR antennas while in OEW scanning setup there is no such effect.
The first ray arrives at about 10ns as radio propagation when there is LoS component.
The LoS component is of much significant comparing the reflection and scattering components.

## Slide 22: Future Work
Continue the small-scale channel measurement in other two transmission scenarios.
Extract the distribution of parameters and finish the channel models based on channel measurement.
Set up MIMO channel measurement and derive the relative correlation matrix.
Give the Matlab code of channel generation at 45 GHz band.