## Slide 1: Reuse Subelement
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Date: 2014-03-18
Authors:

## Slide 2: Abstract
This document explains TLV renaming.

## Slide 3: Issue
Why do we need to change the name of “TLV”?
  .11af already defined the term “TLV” as following.
    type/length/value (TLV): A formatting scheme that adds a tag to each transmitted parameter containing the parameter type (and implicitly its encoding rules) and the length of the encoded parameter.
  Our D1.3 has another definition.
    type length value (TLV): The TLV identity is used to encode optional information of fixed and variable length. The first field is the assigned identifier of data being processed, the second field specifies the number of octets of the value, and the third field contains that number of octets of data representing the value for the “type”.
  But TLV of af and ai have different formats.
    This will cause confusion.

## Slide 4: Format
 | Type / ID | Length | Usage
Element | 1 | 1 | Used in Management/Action frames Defined for any frames
TLV (af) | 1 | 1 | Used in Management/Action frames Defined for any frames
Subelement | 1 | 1 | Used in specific elements Defined for specific elements
ANQP element | 2 | 2 | Used in GAS frames Defined for GAS frames
TLV (ai) | 1 | 2 | Used in specific elements
What we need | * | 2 | Used in specific elements
We need 2-octet length field for accomodating data larger than 255 octets.

## Slide 5: Reuse of ANQP element
ANQP element has 2-octet length field.
So we can reuse ANQP element for our TLV.
My personal opinion:
  But the name “ANQP” will cause confusion.
  The “ANQP element” is considered to use just for GAS frames. If we reuse this name, large modifications are required.

## Slide 6: Reuse of Subelement
I propose to reuse “Subelement”.
The usage of the “Subelement” is very similar to our TLV.
Subelements are defined in each parent element.
  Subelement definitions are closed in a specific element.
  New subelement format in new elements does not cause backward compatibility issues.
We can reuse it by small modification of the definition of the “Subelement” in clause 8.4.3.

## Slide 7: Clause 8.4.3
8.4.3 Information Subelements
Subelements are defined to have a common general format consisting of a 1-octet element-specific Subelement ID field, a 1-octet or a 2-octet Length field, and a variable-length subelement-specific Data field. Each subelement is assigned a subelement ID that is unique within the containing element or subelement. The Length field specifies the number of octets in the Data field. The size of the Length field is defined by each containing element or subelement. See Figure 8-516 (Subelement format). Subelements are ordered by nondecreasing Subelement ID. See 9.25.9 (Extensible subelement parsing).
Subelement ID
Length
Data
Octets:
1
1 or 2
variable
Figure 8-516 – Subelement format

## Slide 8: Existing Subelement Definitions 1
Subelements are defined at 50 locations in mc D2.0.
40 definitions have the following description.
  The Optional Subelements field format contains zero or more subelements, each consisting of a 1-octet Subelement ID field, a 1-octet Length field, and a variable-length Data field, as shown in Figure 8-516 (Subelement format).
No need to change.

## Slide 9: Existing Subelement Definitions 2
8 definitions have the following description.
  The Length field is defined in 8.4.3 (Information Subelements).
  with the following figure.
No need to change? Or modify description?
Subelement ID
Length
Octets:
1
1

## Slide 10: Existing Subelement Definitions 3
1 definition has the following description.
  Just a figure.
No need to change? Or add description?
1 definition just refers other element (not subelement).
No need to change.
  Because the refered element has the definition.
Subelement ID
Length
Octets:
1
1

## Slide 11: Strawpoll
Do you support to reuse “Subelement” for our TLV?
Result
  Yes:
  No:
  Need more discussion:
  Don’t care: