## Slide 1: PHY recommended practice
Date: 2014-03-17
Authors:

## Slide 2: Abstract
This presentation contains recommended practice statements on PHY mode use in the 2.4GHz band, in partial resolution of LB199 CID 2423.

## Slide 3: Background
Slide 3
The role of 11b traffic has been the subject of intense discussion in TGmc and elsewhere
  See (among others) doc. IEEE 802-11-13-1533-1-00-mc, “Clause 16 and 17 deprecation”, Graham Smith, Mark Hamilton, Mark Rison
Multiple views exist on how to proceed, some diametrically opposed
This presentation deals exclusively with “should” statements on the topic
  In accordance with action item from January meeting
Premises:
  1 Mbps and 2 Mbps rates have longer range than 6 Mbps
  There are (potential) applications where this longer range may be important
    E.g., IoT applications with very low traffic
    Existence of 1 Mbps and 2 Mbps rates may be important even if rarely used
  We should therefore not deprecate 11b data rates in their entirety
  “Should” statements address the properties of newly deployed such devices
    If there are millions or billions of such new devices, how should they behave?
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 3

## Slide 4: Justification for proposed changes
Slide 4
“Backward compatibility” is a key criterion
  But what exactly does it mean?
  In one sense it means that new specifications /amendments must be backward compatible with older specifications /amendments
    So g, n, ac, and ax must be backward compatible with b, but b does not have to be backward compatible with g, n, ac, and ax
  But in another sense it means that new devices must be backward compatible with existing deployed devices
    So newly deployed b devices must be backward compatible with g, n, and n+ac devices
    New b devices must support the 6 Mbps g mode in particular, to enable decoding of g and n preambles
The proposed changes have two aims:
  Ensure that new b-capable devices implement the essential modes from g
  Encourage the use of the g modes when they work
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 4

## Slide 5: Proposed changes
Slide 5
In Clause 16.1 (DSSS PHY specification for the 2.4GHz band designated for ISM applications—General), add
  “A DSSS (Clause 16) STA should support the mandatory features of Clause 19 (ERP).”
In Clause 17.1 (HR/DSSS PHY Specification—General), add
  “An HR/DSSS (Clause 17) STA should support the mandatory features of Clause 19 (ERP).”
In Clause 9.7.5.7 (Rate selection for other individually addressed Data and Management frames), add
  “An ERP STA should not transmit other individually addressed Data and Management frames to ERP STAs using the 5.5Mbps or 11Mbps rates.”
  “An ERP STA that transmits a frame to an ERP STA using the 1Mbps or 2Mbps rate and that receives an acknowledgment or block acknowledgment with a received energy that is equal to or greater than –62 dBm should use an ERP-OFDM rate or HT or VHT rate for the next frame transmitted to that STA.”
  “An ERP STA should not transmit a Probe Request using the 1Mbps or 2Mbps rate in any channel unless it has received no response to a Probe Request transmitted a Probe Request using the 6Mbps rate in that channel within the previous 65535 TUs.”
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 5

## Slide 6: Motions
Slide 6
Motion 1:
  In Clause 16.1 (DSSS PHY specification for the 2.4GHz band designated for ISM applications—General), add
    “A DSSS (Clause 16) STA should support the mandatory features of Clause 19 (ERP).” and
  In Clause 17.1 (HR/DSSS PHY Specification—General), add
    “An HR/DSSS (Clause 17) STA should support the mandatory features of Clause 19 (ERP).”
Motion 2:
  In Clause 9.7.5.7 (Rate selection for other individually addressed Data and Management frames), add
    “An ERP STA should not transmit frames to ERP STAs using the 5.5Mbps or 11Mbps rates.” and
    “An ERP STA that transmits a frame to an ERP STA using the 1Mbps or 2Mbps rate and that receives an acknowledgment or block acknowledgment with a received energy that is equal to or greater than –62 dBm should use an ERP-OFDM rate or HT rate for the next frame transmitted to that STA.” and
    “An ERP STA should not transmit a Probe Request using the 1Mbps or 2Mbps rate in any channel unless it has received no response to a Probe Request transmitted using the 6Mbps rate in that channel within the previous 65535 TUs.”
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 6